## Slide 1: WF on CRS muting for eFeMTC RRM
Huawei, HiSilicon, Ericsson
3GPP TSG-RAN WG4 Meeting #84 R4-1709085
Berlin, Germany, 21th – 25th August, 2017
Agenda Item: 8.25.3.1

## Slide 2: Agreements for Cat-M1
CRS is always transmitted over the center 6 PRBs
For cat-M1 UEs, CRS is also transmitted over the part of the cell bandwidth (1.4 MHz)where the UE reception is configured during following occasions:
  Subframe containing SIBs
  Paging occasions
  Scheduled subframes
  DRX ON durations
  Configured MPDDCH monitoring
  RACH occasions (e.g. during Msg 2/4 reception)
  FFS if additional CRS for CSI measurement in subframes outside the MPDCCH search space
CRS is transmitted over the UR RF bandwidth Y1 subframes before and Y2 subframes after the abovementioned UE RF transmission and reception occasions to “warm up” and “cool down”:
  Y1 is warm up time: Y1 is FFS
  Y2 is the cool down time: Y2 is FFS

## Slide 3: Agreements for Cat-M2
CRS is always transmitted over the center 6 PRBs
For cat-M2 UEs, CRS is also transmitted over the part of the cell bandwidth (5 MHz)where the UE reception is configured during following UE reception occasions:
  Subframe containing SIBs
  Paging occasions
  Scheduled subframes
  DRX ON durations
  Configured MPDDCH monitoring
  RACH occasions (e.g. during Msg 2/4 reception)
  FFS if additional CRS for CSI measurement in subframes outside the MPDCCH search space
In addition, CRS is also transmitted over central 24 RBs within the cell bandwidth prior to following UE transmission occasions:
  Random Access
  SRS
  PUCCH/PUSCH
CRS is transmitted over the UR RF bandwidth Y1 subframes before and Y2 subframes after the abovementioned UE RF transmission and reception occasions to “warm up” and “cool down”:
  Y1 is warm up time: Y1 is FFS
  Y2 is the cool down time: Y2 is FFS

## Slide 4: Agreements for Cat-M1/M2
Whether CRS over full cell bandwidth is needed for frequency scanning is FFS.
  Interested UE companies are encouraged to provide more information on the impact for frequency scanning due to CRS muting.