## Slide 1: Optimization of capability signalling
Qualcomm
3GPP TSG-RAN WG4 Meeting #84 Berlin, Germany., 21 - 25 August 2017
R4-1707725

## Slide 2: Separation of MIMO layer
It was proposed to indicate MIMO layer capability per-band instead of per-BoBC (band of band combination)
Since MIMO layer support is still dependent on CA RF architecture, it is not possible to separate MIMO layer capability from CA capability
Counterexample
  UE supports CA_3A_41C
  UE has 6 Rx chain
  UE can support 4 layer MIMO on 2 CC when 2 CC CA is configured
# of CCs | Band | # Rx on band 3 | # Rx on band 41 | # 4 layer CC
1 | 3A | 4 | N/A | 1
1 | 41A | N/A | 4 | 1
2 | 3A+41A | 2 | 4 | 1
2 | 3A+41A | 4 | 2 | 1
2 | 41C | N/A | 4 | 2
3 | 3A+41C | 4 | 2 | 0
3 | 3A+41C | 2 | 4 | 0

## Slide 3: Capability signaling structure
Split capability signaling for baseband features into RF-dependent CA configuration signaling and baseband feature capability signaling
eNB determine UE’s baseband feature capability for specific CA configuration by combining CA capability and baseband feature capability
RF-dependent CA configuration
  In CA configuration capability signaling, remove all baseband capability
  MIMO layer is still indicated per-CC in CA capability signaling
Baseband feature capability IE
  Number of CCs in CA configuration
  Number of 4 layer CC
  List of baseband feature capability
eNB provides list of baseband features that are supported in the network to reduce UE’s baseband feature capability signaling
UE can declare multiple baseband feature capability for given {number of CCs in CA configuration, number of 4 layer CC} combination

## Slide 4: Capability signaling structure
Baseband feature capability
  TM10 CSI process capability
  NAICS capability
  FD-MIMO capability
  eFD-MIMO capability
  MUST capability
Need to determine a rule to index CCs
  2 layer CCs are indexed first
  4 layer CCs are indexed next
It would be desirable to make the signaling flexible so that it can be extended to 8 Rx or 8 layer in the future

## Slide 5: Example UE
UE supports CA up to 3 CC
UE supports FD-MIMO, NAICS and TM10
For single CC
Case | # 4 layer CC | CC 1
1 | 0 | NAICS up to (1 CC, 20MHz)
2 | 0 | FD-MIMO class B TM10 with 4 CSI processes
3 | 1 | TM10 4 CSI processes
4 | 1 | FD-MIMO class B

## Slide 6: Example UE
For 2 CC
  When number of 4 layer CC is 1, CC1 is 2 layer CC and CC2 is 4 layer CC
Case | # 4 layer CC | CC 1 | CC2
1 | 0 | NAICS up to (1 CC, 20MHz) or up to (2 CC, 20MHz) | 
2 | 0 | FD-MIMO class B | FD-MIMO class B
3 | 0 | TM10 with 3 CSI processes | TM10 with 3 CSI process
4 | 1 | NAICS | N/A
5 | 1 | FD-MIMO class B | N/A
6 | 1 | TM10 with 3 CSI processes | N/A
7 | 1 | TM10 with 1 CSI processes | TM10 with 1 CSI processes

## Slide 7: Example UE
For 3 CC
Case | # 4 layer CC | CC 1 | CC2 | CC3
1 | 0 | FD-MIMO class B | N/A | N/A
2 | 0 | TM10 with 1 CSI process | TM10 with 1 CSI process | TM10 with 1 CSI process