## Slide 1: Way forward on eFD-MIMO performance requirements
Samsung, CATT, Qualcomm, Intel, Ericsson
3GPP TSG-RAN WG4 Meeting #84
Berlin, Germany, 21st – 25th August, 2017
R4-1708725

## Slide 2
MCS and Rank
  Single PMI test case: 16QAM ½ Rank2
  Multiple PMI test case: 64QAM ½ Rank2
Reference Test point
  90% of the maximum throughput with following PMI
Class A PMI test cases

## Slide 3: PDSCH demodulation test cases for semi-open MIMO transmission
Test parameters for Rank1 test case
  2*2 EVA70Hz with Medium correlation, QPSK 1/3
Test parameters for Rank2 test case
  16QAM , EVA 70Hz , ULA low correlation
  4*2 MIMO
Precoding matrix
  2Tx: 1/sqrt(2) [1 0;0 1];
  4Tx: The precoding matrix random selected from Table 6.3.4.2.3-2 in TS 36.101 with layer =2, updated granularity as per PRG per TTI basis

## Slide 4
Introduce advanced Codebook PMI test case with below configuration:
    PUSCH 1-2 feedback mode, 16 CSI-RS ports with (N1,N2) = (2,4), (O1, O2) = (8, 4), CDM4, CSS configuration = 1,2, 3, 4 , EVA5Hz
  Test metric:
    Option 1: Throughput ratio between the followed Advanced PMI/RPI and followed Advanced PMI with fixed RPI=0.
    Option 2: Throughput ratio between the followed Advanced PMI/RPI and randomized {i1,3, i2, RPI} with the Advanced CSI. (Baseline)
  MIMO correlation matrix:
    Option 1: High correlation as existing in specs
    Option 2: Medium spatial correlation
  MCS and Rank:
    Option 1: 16QAM 1/2 Rank2 (Baseline)
    Option 2: 64QAM 1/2 Rank1
  Beam steering model: Dual cluster beam with independent MIMO channels
    Relative power ratio : 1 (p=1)
PMI/RPI reporting test for the advanced CSI codebook
 | α1 | α2 | β | γ
High spatial correlation | 0.9 | 0.9 | 0.9 | 0.3
Medium spatial correlation | 0.3 | 0.3 | 0.6 | 0.2

## Slide 5: CSI test case for Hybrid CSI mechanism 1
FFS for the necessity of introducing test cases for mechanism 1

## Slide 6: CSI test cases for Hybrid CSI mechanism 2
Test metric : Introducing test metric as relative throughput ratio under FRC between following CRI (1st CSI reporting), PMI reporting (2nd CSI reporting) and fixed CRI, random PMI
Test parameter (baseline):
  MIMO correlation in test: 4*2 EPA5Hz ULA Low Correlation
  BF CSI resources configurations: Two CSI-RS resources {0,1} with Nk =4
    Power scaling for CSI-RS resources as specified in B.4.6 of TS 36.101
k = 0,1
  CSI configuration:
    For 1st eMIMO-Type , 2 (K=2) BF CSI-RS resources configured as Nk =4 ports; CSI reporting periodicity is multiple times of 2nd eMIMO-Type with additional offset
    For 2nd eMIMO-Type, one BF CSI-RS resources configured as Nk =4 ports
  CSI feedback mode configuration
    PUSCH 3-1 mode
    eMIMO-Type: Reporting interval fixed as 40ms, with aperiodic CSI request in SF#1
    eMIMO-Type2: Reporting interval fixed as 5ms, with aperiodic CSI request in SF#1,SF#6

## Slide 7: CSI Test cases for Multi-Shot and Aperiodic CSI-RS
BF CSI-RS resources configuration for aperiodic CSI-RS test case
  For aperiodic CSI-RS test case, through RRC configured 2 CSI-RS resources, and during test through MAC CE, random selected one of CSI-RS resources activated (fixed during test)
  The corresponding [25] SFs after activation command will be skipped for PDSCH transmission
BF CSI-RS resources configuration for “must-shot” CSI-RS test case
  For multi shot test case, through RRC configured 2 CSI-RS resources, and during test through MAC CE, random selected one of CSI-RS resources activated/released in an alternative way
    The activation and deactivation command will be transmitted in sub-frame #0 with fixed periodicity [X] ms
      Note: X FFS
    The corresponding [25] SFs after deactivation/activation commands will be skipped for PDSCH transmission
Codebook configuration for aperiodic CSI-RS test case and multi-shot CSI-RS test cases
  Rel-10 codebook based on existing Rel-10 CSI-RS single PMI test cases in 36.101 9.1.4.3
  4*2 ULA Low for both TDD and FDD
  Companies are encourage to bring simulation results at least for TDD case in future meetings

## Slide 8: Simulation assumption for advanced CSI (Information)
Parameter | Unit | Test 1 (Multiple PMI test) -16ports
Bandwidth | MHz | 10
Transmission mode |  | 9
Propagation channel |  | EVA5
Precoding granularity (only for reporting and following PMI) |  | 6
Correlation and antenna configuration |  | 2D XP 16 x 2 (N1,N2,P) =(2,4,2) High or Medium
Beamforming model |  | [Annex B.4.3]
Cell-specific reference signals |  | Antenna ports 0,1
CSI reference signals |  | Antenna ports
 |  | 15,…,30
Number of CSI-RS ports |  | 16
CDM Type |  | CDM4
CSI-RS periodicity and subframe offset TCSI-RS / ICSI-RS |  | 5/1
NZP-CSI-RS-Configuration-List |  | {0,1,2,3}
FrequencyDensityNonPrecoded |  | 1
NZP-TransmissionCombNonprecoded |  | 1
eMIMO-Type |  | Class A
advancedCodebookEnabled |  | True
codebookConfig-N1 |  | 2
codebookConfig-N2 |  | 4
codebook-Over-Sampling-RateConfig-O1 |  | 8
codebook-Over-Sampling-RateConfig-O2 |  | 4
codebookSubsetRestriction-1 |  | 0x02/01 FFFF FFFF FFFF FFFF FFFF FFFF FFFF FFFF FFFF FFFF FFFF FFFF FFFF FFFF FFFF FFFF
codebookSubsetRestriction-2 |  | Codebook-Config 1: 0000 1111 0000 Codebook-Config 2,3,4: 0x 00 000000 FFFF 0000
Reporting mode |  | PUSCH 1-2
Reporting interval | ms | 5
PMI delay | ms | 8
MCS &Rank |  | 16QAM 1/2, Rank2 or 64QAM 1/2, Rank1
Max number of HARQ transmissions |  | 4
Redundancy version coding sequence |  | {0,1,2,3}

## Slide 9: Simulation assumption for Hybrid CSI mechanism 2 (Information)
Parameter |  | Unit | Test 1
Bandwidth |  | MHz | 10
Transmission mode |  |  | 9
Propagation channel |  |  | EPA5
Precoding granularity (only for reporting and following PMI) |  | PRB | 50
Correlation and antenna configuration |  |  | 4*2 ULA Low
Cell-specific reference signals |  |  | Antenna ports 0,1
Beamforming model |  |  | B.4.6 (Note 4)
CSI reference signal configuration List |  |  | {0,1}
Number of CSI-RS ports (Nk) |  |  | {4,4}
CSI-RS-SubframeConfig List |  |  | {1,1}
eMIMO-Type |  |  | Class B
Number of NZP-CSI resources (K) |  |  | 2 for following CRI
NZP-CSI-RS-ID-List |  |  | {0,1}
eMIMO-Type2 |  |  | Class B
NZP-CSI-RS-ID |  |  | {0}
codebookSubsetRestriction |  |  | 001111
Reporting mode |  |  | PUSCH 3-1
Physical channel for PMI(1) reporting |  |  | PUSCH
Reporting interval for PMI(1) reporting |  | ms | 40 (Note 5)
Physical channel for RI(2)/CQI(2)/PMI(2) reporting |  |  | PUSCH
Reporting Interval for RI(2)/CQI(2)/PMI(2) reporting |  | ms | 10
Downlink power allocation |  | dB | 0
 |  | dB | 0
 | Pc | dB | -3
 |  | dB | -3
Rank Number of PDSCH |  |  | 1
Measurement channel |  |  | R.50A-1 FDD
OCNG Pattern |  |  | OP.1 FDD
Max number of HARQ transmissions |  |  | 4
Redundancy version coding sequence |  |  | {0,1,2,3}
Scheduled PDSCH SFs |  |  | SF 0,2,3,4,7,8,9
Note 1: For random precoder selection, the precoder shall be updated in each TTI (1 ms granularity). Note 2: If the UE reports in an available uplink reporting instance at subrame SF#n based on CRI,PMI estimation at a downlink SF not later than SF#(n-4), this reported CRI, PMI cannot be applied at the eNB downlink before SF#(n+4). Note 3: To avoid collisions between CQI/PMI reports and HARQ-ACK it is necessary to report both on PUSCH instead of PUCCH. Note 4: The precoder matrix as specified in Table 6.3.4.2.3-1of [4].For following PMI, PMI equals to UE reported PMI(2) for eMIMO-Type2 “Class B”. Note 5: PDCCH DCI format 0 with a trigger for aperiodic CSI of eMIMIO-Type shall be transmitted in downlink SF#6 to allow aperiodic PMI(1) to be transmitted on uplink SF#0. PDCCH DCI format 0 with a trigger for aperiodic CSI of eMIMIO-Type2 shall be transmitted in downlink SF#1 to allow aperiodic RI(2)/CQI(2)/PMI(2) to be transmitted on uplink SF#5. |  |  | 

## Slide 10: Simulation assumption for multi-shot and aperiodic CSI-RS (TDD) - Information
Parameter |  | Unit | Aperiodic | Multi shot | 
Bandwidth |  | MHz | 10 | 10 | 
Transmission mode |  |  | 9 | 9 | 
Uplink downlink configuration |  |  | 1 | 1 | 
Special subframe configuration |  |  | 4 | 4 | 
Propagation channel |  |  | EPA5 | EPA5 | 
Precoding granularity |  | PRB | 50 | 50 | 
Correlation and antenna configuration |  |  | ULA Low 4 x 2 | ULA Low 4 x 2 | 
Beamforming model |  |  | Annex B.4.3 | Annex B.4.3 | 
Cell-specific reference signals |  |  | Antenna ports 0,1 | Antenna ports 0,1 | 
CSI reference signals |  |  | Antenna ports 15,…,18 | Antenna ports 15,…,18 | 
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  |  | 5/ 4 | 5/ 4 | 
FrequencyDensityBeamformed |  |  | 1 | 1 | 
NZP-TransmissionCombBeamformed |  |  | NA | NA | 
csi-RS-NZP-mode |  |  | Aperiodic | Multishot | 
NumberActivatedAperiodicCSI-RS-Resources |  |  | 1 | NA | 
CSI-RS-ConfigNZPAperiodic |  |  | 6 ,7 (Note 5) | NA | 
NumberActivatedCSI-RS-Resources |  |  | NA | 1 | 
CSI-RS reference signal configuration(s) |  |  | 6 | 6,7 (Note 6,7) | 
eMIMO-Type |  |  | Class B | Class B | 
alternativeCodebookEnabledCLASSB_K1 |  |  | FALSE | FALSE | 
codebookSubsetRestriction |  |  | 0x0000 0000 0000 FFFF | 0x0000 0000 0000 FFFF | 
Downlink power allocation |  | dB | 0 | 0 | 
 |  | dB | 0 | 0 | 
 | Pc | dB | -3 | -3 | 
 |  | dB | -3 | -3 | 
 |  | dB[mW/15kHz] | -98 | -98 | 
Reporting mode |  |  | PUCCH 1-1 | PUCCH 1-1 | 
Reporting interval |  | ms | 5 | 5 | 
PMI delay (Note 2) |  | ms | 10 | 10 | 
Physical channel for CQI/PMI reporting |  |  | PUSCH (Note 3) | PUSCH (Note 3) | 
PUCCH Report Type for CQI/ PMI |  |  | 2 | 2 | 
Physical channel for RI reporting |  |  | PUSCH | PUSCH | 
PUCCH Report Type for RI |  |  | 3 | 3 | 
cqi-pmi-ConfigurationIndex |  |  | 4 | 4 | 
ri-ConfigIndex |  |  | 805 | 805 | 
Measurement channel |  |  | QPSK 1/3 | QPSK 1/3 | 
Rank number of PDSCH |  |  | 1 | 1 | 
OCNG Pattern |  |  | OP.1 TDD | OP.1 TDD | 
Max number of HARQ transmissions |  |  | 4 | 4 | 
Redundancy version coding sequence |  |  | {0,1,2,3} | {0,1,2,3} | 
ACK/NACK feedback mode |  |  | Multiplexing | Multiplexing |