## Slide 1: WF on referense sensitivity for mmWave
LG Electronics, Huawei, Sumitomo, Sony, Ericsson, Skyworks, Intel Corporation, KT, Media Tek
R4-17091408905
3GPP TSG-RAN WG4 #84 Meeting
Berlin, Germany, August 21st -25th, 2017
Agenda: 9.4.4.1

## Slide 2: Background (1)
WF in RAN4 #83 meeting
  R4-1706067 WF on UE reference architecture, Sony, Skyworks, LGE
Contributions in RAN4 #84
  R4-1708175 NR UE REFSENS requirments LGE
  R4-1707332 UE reference sensitivity for mmWave 28GHz Sony
  R4-1707828 Preliminary smartphone EIS performance evaluation Huawei
  R4-1708542 Reference sensitivity for mmW UE Qualcomm
  R4-1707511 MSD for combinations including 3.5GHz, 4.5GHz, 28GHz NTT DoCoMo
  R4-1706506 mmWave UE REFSENS considerations & proposals Intel
In RAN4 #84 meeting, RAN4 has been discussed in terms of the REFSENS equations and test parameters to derive REFSENS RF requirements in mmWave.
Based on online discussion, RAN4 need to aligned REFSENS equation and test parameters to encourage REFSENS test campaign.

## Slide 3
Agreements in WF (R4-1706067)
  In Rel-15 UE in the 28GHz mmWave range NR
    REFSENS requirement shall be based on DL MRC diversity (rank 1 with two receivers).
      FFS whether this apply to all directions.
    UE architecture shall support minimum dual layer (same as LTE rank 2) for demodulation performance requirement.
      FFS whether this apply to all directions.
    RF architecture support for higher order DL layers is optional.
Background (2)

## Slide 4
Definition of Sensitivity equation in mmWave
  RAN4 can derive the REFSENS requirement based on alignment on the peak EIS level equation and the options listed in slide #6
    Sensitivity = -174dBm(kT) + 10*log(Max. RX BW) + NF – Total Ant. gain - diversity/polarization gain + SNR + ILs
      In here, Total ant. gain = element gain + beamforming gain
      ILs: Implementation Losses
      Max. RX BW: Max. Received Bandwidth
Way Forward (1)

## Slide 5
Expected Schedule for REFSENS requirements in mmWave
  In RAN4 RF session, detail REFSENS requirement will be discussed and decided
    Option1: Defined as Beam Peak EIS or
    Option2: Defined as a CDF EIS
      [A %] EIS CDF : The percentile and # of points of CDF curve will be FFS.
    Option3 : Defined as Beam Peak and CDF EIS combinations
  In RAN4 demodulation session, should be decided target SNR level.
    Refer the agreed WF (R4-1708904).
  RAN4 should complete REFSENS requirements in RAN4 #85 meeting.
Way Forward (2)