## Slide 1: WF on 1 RX CRS-IM performance
Intel Corporation
3GPP TSG-RAN WG4 Meeting #84bis Dubrovnik, Croatia, 9 - 13 October 2017
Agenda Item: 8.29
R4-1711672

## Slide 2: General impact of CRS-IM
Performance
  1RX CRS-IM provide performance improvement for Cat1bis and CatM2 device categories for both data and control channels in some scenarios.
UE complexity
  The complexity for 1Rx CRS-IM receiver is different for different implementation of different companies.
  1RX CRS-IM impact on UE complexity is acceptable at least for some UEs
UE power consumption
  1RX CRS-IM impact on UE power consumption is acceptable at least for some UEs

## Slide 3: Target device types / UE categories
Specify 1RX CRS-IM requirements for the following UE types:
  Cat1bis (UE Cat 1 with 1 RX)
  CatM2
Additionally investigate 1RX CRS-IM feasibility for CatM1 UEs

## Slide 4: Cat1bis Performance Requirements
Test cases for 1RX CRS-IM Cat1bis performance requirements
  PDSCH
    Test #1:
      TM4, 4 CRS APs, 24 PRBs, MIMO Rank 1
      MCS:
        Option 1: 64QAM (MCS20)
        Option 2: 16QAM (MCS12)
      Interference loading: FFS between [10, 20, 30]%
    Test #2:
      TM9, 2 CRS APs, 24 PRBs, MIMO Rank 1
      MCS:
        Option 1: 64QAM (MCS20)
        Option 2: QPSK (MCS9)
      Interference loading: FFS between [10, 20, 30]%
  PDCCH
    Test #1: PDCCH AL2, 2 CRS APs, CFI = 1
    Test #2: PDCCH AL4, 4 CRS APs, CFI = 2

## Slide 5: CatM2 Performance Requirements
Test cases for 1RX CRS-IM CatM2 performance requirements
  PDSCH test cases
    Test #1: TM6 with 4 CRS APs
      CE mode A, FFS for repetitions and frequency hopping
      Option 1: 16QAM + Rank 1, 20% interference loading
      Option 2: QPSK + Rank 1, 30% interference loading
    Test #2: TM6 with 2 CRS APs
      CE mode A, FFS for repetitions and frequency hopping
      Option 1: 16QAM + Rank 1, 20% interference loading
      Option 2: QPSK + Rank 1, 30% interference loading
  MPDCCH test cases
    Test #1: MPDCCH AL4, [0, 20%] interference loading, CE mode A, No repetitions and no frequency hopping
    Test #2: MPDCCH AL16, 10% interference loading, CE mode A, No repetitions and no frequency hopping
  FFS if additional tests PDSCH and/ore MPDCCH test for CE Mode B, multiple repetitions or frequency hopping

## Slide 6: UE Features/Capabilities
FFS whether to define different UE features for 1RX CRS-IM for 2/4 CRS APs scenarios and for Data/Control channels
Further discuss the detailed UE features set and associated capabilities signalling.