## Slide 1: WF on wideband operation
Intel Corporation, LGE
R4-1711819
3GPP TSG-RAN WG4 Meeting #84bis
Dubrovnik, Croatia, October 9-13, 2017
Agenda: 9.3.1.2

## Slide 2: Overview
Wide bandwidth operation in LTE is enabled by CA (inter-band or intra-band)
For LTE the system bandwidth does not differentiate BS BW and UE BW; NR has introduced separate BW definitions for BS and UE
For LTE CA the BS CC and UE CC are the same BW and same carrier
For NR wideband operation, it is understood that CA operations are fully supported
Additional functionality and, potentially, RF requirements for NR wideband operation are presented on a case-by-case basis
Relevant RAN1 agreements are provided in the next two slides
Three wideband operation scenarios and the applicable RF requirements are described in the following slides

## Slide 3: Relevant RAN1 agreements (1)
Meeting | Agreements
RAN1 #88bis | A gNB can operate simultaneously as wideband CC for some UEs and as a set of intra-band contiguous CCs with CA for other UEs RAN1 believes that it is beneficial to allow zero guardband between CCs within wideband CC and asks RAN4 to take it into account when discussing channel raster
RAN1 #89 | One or multiple bandwidth part configurations for each component carrier can be semi-statically signalled to a UE A bandwidth part consists of a group of contiguous PRBs The bandwidth of a bandwidth part equals to or is smaller than the maximal bandwidth capability supported by a UE Configuration of a bandwidth part may include the following properties: Numerology, Frequency location (e.g. center frequency), Bandwidth (e.g. number of PRBs) FFS how to indicate to the UE which bandwidth part configuration (if multiple) should be assumed for resource allocation at a given time A UE can assume that PDSCH and corresponding PDCCH (PDCCH carrying scheduling assignment for the PDSCH) are transmitted within the same BWP if PDSCH transmission starts no later than K symbols after the end of the PDCCH transmission. In case of PDSCH transmission starting more than K symbols after the end of the corresponding PDCCH, PDCCH and PDSCH may be transmitted in different BWPs

## Slide 4: Relevant RAN1 agreements (2)
Meeting | Agreements
RAN1 NR AH#2 | Primary focus is to complete the single active bandwidth part case For FDD, separate sets of bandwidth part (BWP) configurations for DL & UL per component carrier For TDD, separate sets of BWP configurations for DL & UL per component carrier For UE, if different active DL and UL BWPs are configured, UE is not expected to retune the center frequency of channel BW between DL and UL
RAN1 #90 | Common PRB indexing is used at least for DL BWP configuration in RRC connected state
RAN1 NR AH #3 | In Rel-15, for a UE, there is at most one active DL BWP and at most one active UL BWP at a given time for a serving cell NR supports the case that a single scheduling DCI can switch the UE’s active BWP from one to another (of the same link direction) within a given serving cell

## Slide 5: Wideband operation case 1 with BWP
Rel-15 gNB
BS CC1
(400MHz)
BWP(1,1)
(400MHz)
time
BWP(1,1)
(200MHz)
BWP(1,1)
(200MHz)
BS CC1
(800MHz)
Rel-x gNB
BS CC2
(400MHz)
UE1 CC
(400MHz)
BWP(1,2)
(200MHz)
Multiple active BWP per serving cell
not supported in Rel-15
BS CCs are contiguous and may have GB depending on raster
  Note 1: the BWP # is just shown as example.
  Note 2: single-carrier requirements apply
BWP(1,2)
(200MHz)
BWP(1,3)
(200MHz)
BWP(1,3)
(200MHz)
BWP(1,2)
(200MHz)
Active BWP
Configured BWP but not active one
UE1

## Slide 6: Wideband operation case 2
Rel-15 gNB
BS CC1
(400MHz)
BS CC1
(800MHz)
Rel-x gNB
BS CC2
(400MHz)
UE2 CC1
(200MHz)
RAN4 agreement
RAN4 agreement in R4-1706321:
UE is allowed to aggregate channel bandwidths to operate within a gNB configurable CHBW that is higher than the maximum bandwidth supported by the UE
  For example, a 400MHz UE that does not support 400MHz channel bandwidth can support 2x200MHz or 4x100MHz even if the gNB could configure 400MHz channel bandwidth
    Each CC bandwidth is from the set of channel bandwidths defined for that band
  UE should indicate to gNB its bandwidth capability and how it supports this bandwidth (e.g. what CA combination)
    Signaling details are FFS
  Which aggregated channel bandwidth combinations are allowed is FFS, BS complexity should be considered
BS CCs are contiguous and may have GB depending on raster
BWP(1,1)
(200MHz)
BWP(2,1)
(200MHz)
UE2 CC2
(200MHz)
BWP(1,1)?
(200MHz)
BWP(2,1)?
(200MHz)
RAN1 clarification is needed
  Note: the BWP # is just shown as example.
UE2

## Slide 7: Wideband operation case 3
Rel-15 gNB
BS CC1
(400MHz)
BWP(1,1)
(400MHz)
time
BWP(1,1)
(200MHz)
BWP(1,1)
(200MHz)
BS CC1
(800MHz)
Rel-x gNB
BS CC2
(400MHz)
UE3 CC1
(400MHz)
BS CCs are contiguous and may have GB depending on raster
UE3 CC2
(400MHz)
BWP(2,1)
(400MHz)
BWP(2,1)
(200MHz)
BWP (2,1)
(400MHz)
Not supported in rel-15
Supported in rel-15
Supported in rel-15
BWP(1,1)
(200MHz)
BWP(2,1)
(200MHz)
UE3

## Slide 8: Spectral Utilization for intra-band contiguous CA
Rel-15 gNB
BS CC1
(100MHz)
UE CC1
(50MHz)
Spectral utilization
  Option1: Spectral utilization based on individual CCs (UE CC1 and UE CC2)
    E.g. for 50MHz sub6, SU is 65RBs, for 100MHz SU is 135, UE configured with 2x50MHz in 100MHz channel is using 130RBs
  Option2: Spectral utilization based on the wider channel bandwidth
    E.g. for 50MHz sub6, SU is 65RBs, for 100MHz SU is 135, UE configured with 2x50MHz in 100MHz channel is using all 135RBs
UE CC2
(50MHz)
UE CC1
(50MHz)
UE CC2
(50MHz)
Option 1
Option 2

## Slide 9: Agreements
An LS to RAN1 is needed to and clarify the potential conflict between RAN1 and RAN4 agreement
  the applicability of RAN1 agreement on BWP to case2
    i.e. the feasibility to activate both BWP(1,1) and BWP(2,1) simultaneously for UE2 in Case 2
  Question for RAN1:
    RAN4 respectfully requests RAN1 to clarify the mechanism by which the scenario described in case 2 is supported; i.e. the case of multiple BWPs operating simultaneously across a contiguous bandwidth spanned by multiple CCs per UE
The SU for wideband operation and associated impact on UE RF requirement should be decided based on two options in slide 8 at next RAN4 meeting.
The scenarios associated with BWP retuning or reconfiguration should be discussed during the next RAN4 meeting

## Slide 10: References
TDoc | Title | Source
R4-1710106 | LS on Further agreements for Bandwidth part operation | RAN1, LGE
R4-1710126 | Reply LS on multiple SSBs within a wideband carrier | RAN1, Ericsson
R4-1710173 | Wideband and CA Operation for NR | Qualcomm Incorporated
R4-1710380 | On UE wide bandwidth support | Intel Corporation
R4-1710632 | RF requirements for BS and UE in wideband operation | ZTE Corporation
R4-1710912 | Further clarification for wideband operation of NR UE | LG Electronics France
R4-1711040 | Understanding on BWP agreement | Samsung
R4-1711378 | Intra-band CA and wideband operation RF requirement | Nokia, Nokia Shanghai Belll