## Slide 1: Way Forward on additional UE spurious emission requirements to protect passive bands
Qualcomm Incorporated, Intel, Skyworks Solutions
3GPP TSG-RAN WG4 RAN#84 Bis
Dubrovnik, Croatia, October 9th-13th, 2017
R4-1711403
Agenda Item: 9.4.3.9.2

## Slide 2: Background information (1)
ITU-R asks the feasibility of more string limit compared to the categories defined in recommendation ITU-R SM.329. In particular:
  Feasibility of -30 dBm/MHz for both UE and BS, and if not feasible, achievable value is requested.
  Additional spurious emission requirements: ITU-R requests information regarding feasibility of more stringent limits to protect specific sensitive services.
Regarding the protection of passive services (e.g. EESS passive), one of ITU-R proposals is to increase reference bandwidth. An example is given by the following list which shows band of operation of passive services and corresponding reference bandwidth to be studies:
23.6-24 GHz -> 200MHz
31.3-31.8 GHz -> 200MHz
50.2-50.4 GHz -> 200MHz
52.6-54.25 GHz -> 100MHz
86-92 GHz -> 100MHz

## Slide 3: Background information (2)
For UE the following observations were agreed [2]:
  … the emissions are possibly not flat within 200 MHz measurement bandwidth and thus a more stringent emission level in the protected band with larger measurement BW (e.g. 200MHz) might be feasible

## Slide 4: Way Forward
To define an additional requirements to protect the passive bands with measurement BW of 200MHz
The value of the additional requirement is TBD dBm/200MHz
RAN4 does not need to specify any image rejection requirement
RAN4 will study required power back off and/or RB restriction needed to meet the target of -7 dBm/200MHz in the 23.8-24 GHz frequency range.
The following NR transmission configuration should be studied:
  Band: n257 and 258.
  Channel BW: 400 MHz and 800MHz.
  Channel location: lowest channel in the band (i.e. starting from 26.5GHz for n257 and from 24.25GHz for n258)
    If the cases above need no restriction, evaluation for different channel location is not needed .
    Otherwise, upper frequency channel allocation needs to be studied with steps of 200 MHz granularity.
In RAN4 #85, we will inform ITU-R WP5D and CEPT PT1 about the outcome of the study in terms of power reduction, resource allocation restriction needed to meet the additional requirement

## Slide 5: References
[1] R4-1707004, "LIAISON STATEMENT TO 3GPP ON UNWANTED EMISSIONS OF IMT-2020" (ITU-R WP5D).
[2] R4-1710084, "LS on Unwanted emissions of IMT-2020" to ITU-R WP5D, (RAN4)..
[3] R4-1709363, LS response to WP5D on Unwanted emissions of IMT-2020
[4] R4-1707701, “Feasibility of improved spurious emissions in NR mmWave UE”, Skyworks Solutions Inc.
[5] R4-1708125, “On spurious emission limits for mm-wave bands”, Ericsson.
[6] R4-1708450, “General observations on UE emissions in mmW”, Qualcomm Incorporated.
[7] R4-1709330, “NR UE above 24GHz Spurious Emissions and Protected Bands”, Skyworks Solutions Inc.
[8] R4-1709408, “On spurious emissions requirement for mmWave NR”, Intel Corporation.
….