## Slide 1: WF on UE IBE for mmWave for MPR evaluation for NR
Qualcomm
3GPP TSG-RAN WG4 #84BIS Meeting
Dubrovnik, Croatia, October 09 -13, 2017
Agenda: 9.4.3.7.2
R4-1711570

## Slide 2: Background
IBE Specification definition is required for NR, FR2
R4-1711396 had a proposal for IBE covering FR1 and FR2.
  Chairman recommended creation of this WF addressing just FR2, for the purpose of enabling MPR studies.
  FR1 spec addressed in separate document R4-1710959
  some parameter values may be adjusted later before entry as final specification for FR2

## Slide 3: WF Proposal
Parameter description | Unit | Limit (NOTE 1) |  | Applicable Frequencies
General | dB |  |  | Any non-allocated (NOTE 2)
IQ Image | dB | -25 | Output power > 10 dBm | Image frequencies (NOTES 2, 3)
 |  | -20 | Output power ≤ 10 dBm | 
Carrier leakage | dBc | -25 | Output power > 0 dBm | Carrier frequency (NOTES 4, 5)
 |  | -20 | -13 dBm ≤ Output power ≤ 0 dBm | 
NOTE 1: An in-band emissions combined limit is evaluated in each non-allocated RB. For each such RB, the minimum requirement is calculated as the higher of (PRB - 17 dB) and the power sum of all limit values (General, IQ Image or Carrier leakage) that apply. PRB is defined in NOTE 10. NOTE 2: The measurement bandwidth is 1 RB and the limit is expressed as a ratio of measured power in one non-allocated RB to the measured average power per allocated RB, where the averaging is done across all allocated RBs. For pulse-shaped pi/2 BPSK, the limit is expressed as a ratio of measured power in one non-allocated RB to the measured power in the allocated RB with highest PSD NOTE 3: The applicable frequencies for this limit are those that are enclosed in the reflection of the allocated bandwidth, based on symmetry with respect to the carrier frequency, but excluding any allocated RBs. NOTE 4: The measurement bandwidth is 1 RB and the limit is expressed as a ratio of measured power in one non-allocated RB to the measured total power in all allocated RBs. NOTE 5: The applicable frequencies for this limit are those that are enclosed in the RBs containing the DC frequency if NRB is odd, or in the two RBs immediately adjacent to the DC frequency if NRB is even, but excluding any allocated RB. NOTE 6: LCRB is the Transmission Bandwidth (see Figure 5.6-1). NOTE 7: NRB is the Transmission Bandwidth Configuration (see Figure 5.6-1). NOTE 8: EVM s the limit for the modulation format used in the allocated RBs. NOTE 9: DRB is the starting frequency offset between the allocated RB and the measured non-allocated RB (e.g. DRB=1 or DRB= -1 for the first adjacent RB outside of the allocated bandwidth). NOTE 10. PRB is the transmitted power per allocated RBs, measured in dBm. NOTE 11. All powers are peak EIRP. |  |  |  | 
IBE target values for NR, FR2, limited to MPR simulation only