## Slide 1: WF on power class in FR2
Intel Corporation, Apple, Samsung, LGE, Huawei, MediaTek, Xiaomi, vivo, OPPO, Motorola
R4-1711609
3GPP TSG-RAN WG4 Meeting #84bis
Dubrovnik, Croatia, October 9-13, 2017
Agenda: 9.4.3.2

## Slide 2: Agreements (1)
A single power class is defined for handheld UEs operating in FR2 in Rel-15
  FFS for other UE types, such as fixed wireless access (WFA) devices, etc.
The power class value is defined as the peak EIRP and is band dependent
  Baseline definition: the peak EIRP requirement is defined as the minimum value with no tolerance; it is bounded by the range of values between 22 dBm and 2930.2 dBm
    Option to study: the peak EIRP requirement is defined as the nominal value with tolerance; companies are encouraged to provide the relevant analysis for the next meeting in case this option is preferred
    For both Baseline and Option to Study, the derivation of peak EIRP value is itemized as shown in R4-1711406 as a baseline; additional terms are not precluded
The requirements on max allowed EIRP and upper limit TRP for handheld UEs are defined as captured in R4-1710081
Agreement on the peak EIRP for handheld UEs is sufficient to complete the power class requirement in Rel-15by Dec 2017

## Slide 3: Agreements (2)
The spherical coverage requirement targeted for definition in Rel-15 according to the following steps:
  Step 1: simulated CDFs which model aspects captured above are used to derive the percentile and value; R4-1710708 and R4-1711036 have provided analysis targeting these criteria; the spherical coverage value feasibility can be identified. Contributions from UE vendors are encouraged to include above criteria, additional items not precluded.
  Step 2: measured CDFs from prototype devices satisfying the above criteria are used to derive the percentile and value; the spherical coverage requirement can be defined as a minimum requirement in Rel-15
Parameter | Priority | Value
EIRP radiation pattern coordinate system | 1 | Spherical
EIRP radiation pattern elevation & azimuth angle step size | 1 | 1 deg
Simulated pattern considers the presence of a full screen display panel (with LCD or OLED) | 1 | Yes
Method of CDF generation from EIRP radiation pattern | 1 | Test points with equal area on the spherical surface [1]
Simulated pattern considers the device case material | 2 | Optional
Simulated pattern considers the gap between antenna & housing | 2 | Optional
http://corysimon.github.io/articles/uniformdistn-on-sphere/
https://www.mathworks.com/matlabcentral/fileexchange/16920-returns-weighted-percentiles-of-a-sample
[1]
The following aspects shall be included in the analysis of the spherical coverage:

## Slide 4: Work Plan
RAN4 #85 (November ’17)
  Finalize the peak EIRP requirement for handheld UEs
  Initial discussion of simulation results for spherical coverage based on agreements in slide #3
  Based on the simulation outcome, take a working assumption on the CDF percentile
RAN4 NR AH #4 (January ’18)
  Continue to improve the simulation effort
RAN4 #86 (February ’18)
  Initial discussion of measurement results for prototype devices based on agreements in slide #3
  Reach agreements related to Step #1 in slide #3
RAN4 #86bis (April ’18)
  Continue to improve the measurement effort
RAN4 #87 (May ’18)
  The spherical coverage requirement (percentile and limit value) shall be based on measured data
  Finalize the spherical coverage requirement for handheld UEs

## Slide 5: References
TDoc | Title | Source
R4-1710122 | LS reply to RAN4 on UE Power Class and Power Control | RAN1, Interdigital
R4-1710958 | TP to TS 38.101: Draft CR to Transmitter power clause | Nokia, Nokia Shanghai Bell
R4-1711000 | TP for UE RF TR 38.817-01: mmWave power class | Sumitomo Elec. Industries, Ltd
R4-1710381 | On power control for FR2 | Intel Corporation
R4-1710382 | LS reply on UE Power Class and Power Control | Intel Corporation
R4-1710708 | Further evaluation on NR UE power class at mmWave | LG Electronics France
R4-1710896 | mmWave UE power class definition | MediaTek Inc.
R4-1710900 | P-Max signaling FR2 | Ericsson
R4-1710901 | TP to 38.101-2: Maximum output power and Pcmax | Ericsson
R4-1711406 | UE power class proposals for mm-wave | Apple Inc.
R4-1711516 | Output power requirements for mmW UE | Qualcomm Incorporated
R4-1711519 | mmW PCmax and power control | Qualcomm Incorporated
R4-1710430 | On Spherical Coverage: EIRP CDF data for mm-wave | Intel Corporation, Apple, Samsung
R4-1711036 | Consideration on EIRP for spherical coverage | Samsung, Apple, Intel
R4-1711068 | CDF percentile for spherical coverage | NTT DOCOMO, INC., Vadafone, Orange, Deutsche Telekom, Dish Network
R4-1711424 | UE Power class and spherical coverage for mmWave 28GHz | Sony
R4-1711429 | Discussion of antenna array pre-coder imperfections for mmWave 28GHz antennas | Sony