## Slide 1: WF on V2X requirements for asynchronous SyncRef UE Selection / Reselection
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #84bis Dubrovnik, Croatia, 9 - 13 October 2017
Agenda Item: 5.7.2
R4-1711720

## Slide 2: Background
V2X SyncRef UE Selection / Reselection are defined in TS 36.133 Section 13.4

## Slide 3: Background
Based on Rel-14 V2X RRM requirements UE may be required to perform asynchronous SyncRef UE detection
  UE is allowed to perform V2X Data and SLSS/PSBCH transmissions dropping for the purpose of asynchronous SyncRef UE detection
  UE is not allowed to perform V2X Data and SLSS/PSBCH reception dropping for the purpose of asynchronous SyncRef UE detection
SyncRef UE selection / reselection procedure requires SyncRef UE PSBCH decoding
UE may be required to perform simultaneous reception of PSSCH/PSCCH and SLSS/PSBCH from different UEs
Rel-14 UE is not mandated to support multiple V2X RX timings
Simultaneous reception of asynchronous PSSCH/PSCCH and SLSS/PSBCH from different UEs may not be supported by all UEs

## Slide 4: Way Forward
RAN4 to further study mechanisms and requirements to allow UE to perform asynchronous SyncRef UE PSBCH decoding during the SyncRef UE selection / reselection
Open issues
  Whether UE is allowed to drop PSSCH/PSCCH reception for the purpose of asynchronous SyncRef UE PSBCH decoding and associated drop rate
  Conditions when PSSCH/PSCCH drop may happen (e.g. definition of asynchronous transmission)
No performance requirements tests will be defined for this requirement if it is introduced.