## Slide 1: WF on in-band and out-of-band boundary
NTT DOCOMO, INC., Nokia, Ericsson, Huawei, ZTE
R4-1711779
3GPP TSG- RAN Working Group 4 (Radio) meeting #84bis
Dubrovnik, Croatia, 9st - 13th October 2017
Agenda Item: 9.5.3.2.1

## Slide 2: Background
The boundary between in-band and out of band for FR1 is discussed in [1-6] on Tx and Rx respectively.
This contribution summarizes way forward/agreement on this topic.
We discussed the boundary for all Bands except for Band 46.
[1] R4-1710976 The boundary between OBUE and spurious for FR1 NR NTT DOCOMO
[2] R4-1711018 Transition between unwanted and spurious emissions Ericsson
[3] R4-1710265 In-band /out of band boundary for FR1 Huawei
[4] R4-1711373 On aligning the boundary of FR1 NR spectrum emission mask Nokia
with AAS BS for E-UTRA operating bands = 100 MHz
[5] R4-1711420 On NR blocking requirements for FR1 for bands >= 100 MHz Nokia
[6] R4-1710824 Discussion on out of blocking requirement for FR1 NR BS ZTE

## Slide 3: Agreements on Tx
 |  | E-UTRA |  | NR | 
 |  | 37.104/141 (non-AAS type) | 37.105/145-1/145-2 (AAS type) | 37.104/141 (non-AAS type(1-C)) | 37.105/145-1/145-2 (AAS type(1-H/1-O))
ΔfUEM | Operating band <100MHz | 10MHz | 10MHz | 10MHz | 10MHz
 | 100MHz≦Operating band ≦200MHz | 10MHz | 40MHz | 10MHz | 40 MHz
 | 200MHz<Operating band ≦900MHz |  |  | 40MHz | 40MHz
 | 900MHz<Operating band |  |  |  | 
Agreements of the boundary between OBUE and spurious emissions are summarized in below tables.
The boundary is valid regardless of whether it is single-RAT case or MSR case, and NR new band or refarming band.
If wider band(s) than current maximum bandwidth of Band is specified, the values of the boundary should be discussed. (Wider than 200MHz for E-UTRA, wider than 900MHz for NR)
 |  | E-UTRA |  | NR | 
 |  | 36.104/141 (non-AAS type) | 37.105/145-1/145-2 (AAS type) | 38.104/141 (non-AAS type(1-C)) | 38.104/141 (AAS type(1-H/1-O))
ΔfUEM | Operating band <100MHz | 10MHz | 10MHz | 10MHz | 10MHz
 | 100MHz≦Operating band ≦200MHz | 10MHz | 40MHz | 10MHz | 40 MHz
 | 200MHz<Operating band ≦900MHz |  |  | 40MHz | 40MHz
 | 900MHz<Operating band |  |  |  | 
Table 1: ΔfUEM (NR or E-UTRA single-RAT case).
Table 2: ΔfUEM (NR and E-UTRA MSR case).

## Slide 4: Agreements on Rx
Agreements of the in-band / out of band boundary are summarized in below tables.
The boundary is valid regardless of whether it is single-RAT case or MSR case, and NR new band or refarming band.
If wider band(s) than current maximum bandwidth of Band is specified, the values of the boundary should be discussed. (Wider than 200MHz for E-UTRA, wider than 900MHz for NR)
 |  | E-UTRA |  | NR | 
 |  | 37.104/141 (non-AAS type) | 37.105/145-1/145-2 (AAS type) | 37.104/141 (non-AAS type(1-C)) | 37.105/145-1/145-2 (AAS type(1-H/1-O))
ΔfOOB | Operating band <100MHz | 20MHz | 20MHz | 20MHz | 20MHz
 | 100MHz ≤ Operating band ≤ 200MHz | 20MHz | 60MHz | 20MHz | 60MHz
 | 200MHz<Operating band ≤ 900MHz |  |  | 60MHz | 60MHz
 | 900MHz<Operating band |  |  |  | 
 |  | E-UTRA |  | NR | 
 |  | 36.104/141 (non-AAS type) | 37.105/145-1/145-2 (AAS type) | 38.104/141 (non-AAS type(1-C)) | 38.104/141 (AAS type(1-H/1-O))
ΔfOOB | Operating band <100MHz | 20MHz | 20MHz | 20MHz | 20MHz
 | 100MHz ≤ Operating band ≤ 200MHz | 20MHz | 60MHz | 20MHz | 60MHz
 | 200MHz<Operating band ≤ 900MHz |  |  | 60MHz | 60MHz
 | 900MHz<Operating band |  |  |  | 
Table 3: ΔfOOB (NR or E-UTRA single-RAT case).
Table 4: ΔfOOB (NR and E-UTRA MSR case).