## Slide 1: Way Forward on NR Measurement Requirements
Ericsson, […]
3GPP TSG-RAN WG4 Meeting #84bis R4-1711884
Dubrovnik, Croatia, 9th – 13th October 2017
Agenda Item: 9.7.12

## Slide 2: SS-Block Based RSRP: Observations from Link-Level Results (for information)
Less than or equal to LTE number of samples based on SSS are sufficient to achieve at least the same RSRP measurement accuracy as in LTE
Using PBCH DMRS in the same SS block may further improve the RSRP measurement accuracy
Simulation results are summarized in R4-1711722 (“Simulation results summary for SS block based RSRP”)

## Slide 3: SS Block Based RSRP Measurement Requirements
SS-block based RSRP measurement and accuracy requirements are to be derived based on SSS only
  PBCH DMRS may be used by UE optionally to further improve the accuracy, but no RSRP requirements based on DMRS PBCH will be specified in Rel-15
RSRP measurement period
  1 sample will not be used when defining the requirement for sub-6GHz
  RAN4 will decide the exact measurement period for sub-6GHz and mmWave in RAN4#85

## Slide 4: Principles for Defining Frequency Layers for Monitoring with NR
In 36.133, specify to cover LTE with inter-RAT NR:
  inter-RAT NR carriers for non-NSA
In 36.133, specify to cover NSA:
  Nfreq, inter-RAT NR, NSA Inter-RAT NR carriers for NSA
  Nfreq, E-UTRA inter-frequency LTE carriers (FDD and TDD)
In 38.133, specify to cover NSA:
  Nfreq, inter-freq NR, NSA inter-frequency NR carriers
The total number Nfreq, NSA for NSA is Nfreq, NR + Nfreq, E-UTRA
  Nfreq, NR = Nfreq, inter-RAT NR, NSA + Nfreq, inter-freq NR, NSA, where Nfreq, inter-RAT NR, NSA is defined in 36.133 and Nfreq, inter-freq NR, NSA is defined in 38.133
  Nfreq, NSA is defined in one place (38.133)
    In 36.133, mention Nfreq, NSA but refer to 38.133
  Nfreq, NSA is to be used for measurement period scaling
    In 36.133: for inter-frequency LTE measurements and inter-RAT NR measurements for UE configured with NSA
    In 38.133, for inter-frequency NR measurements for UE configured with NSA
Note: the possible overlap between Nfreq, inter-RAT NR, NSA and Nfreq, inter-freq NR, NSA is FFS