## Slide 1: WF on V2X PSSCH-RSRP Measurement Accuracy Impact on COM algorithm of R15 TxD
Qualcomm Inc.
R4-1711933
3GPP TSG-RAN WG4 Meeting #84bis
Dubrovnik, Croatia, 9 – 13 Oct, 2017

## Slide 2: Background
In RAN4#84 bits, RAN4 have performed some study on the PSSCH-RSRP measurement accuracy impact of R15 non-transparent TxD.
Some company observes that there is significant impact to Center of Mass based (COM) algorithm. (O1)
The group has no consensus on this observation.
The group will further investigate the performance of COM based RSRP estimator to verify O1.

## Slide 3: WF
Side condition for the simulation:
  Measurement bandwidth for PSSCH-RSRP: 3 resource blocks
  PSSCH_Ec/Iot: 0 dB, 5 dB, 10 dB, 20dB
Companies are encourage to bring more analysis on the impact of R15 TxD, the following factors are encouraged to taking into account:
  Different DMRS design impact
    e.g., Different cycle shift for different antenna port,
      the sequence in the second ports is half symbol cyclic shifted of the R14 DMRS sequence.
    or different root sequence for different antenna port
      the sequence in the second ports is another ZC sequence derived from the id of the R14 DMRS sequence.
    and other examples are not precluded
Clarification: the intention is not to compare performance of different RSRP estimators

## Slide 4: For information

## Slide 5: COM Receiver
Ifft the channel response in frequency: h1, h2, …, hN where N is the sequence length.
Find the index of the strongest tap. (Imax)
Calulate ICOM as the center of mass, with mass being h1, h2, …, hN and reference point is Imax
The center of Max supported delay spread is 8us, equivalent to N/8 window size.
The window is set at [ICOM - N/16, ICOM + N/16].
RSRP = Sumi in window (hi^2)