## Slide 1: WF on FeCoMP UE demodulation and CSI reporting requirements
Intel Corporation, ZTE
3GPP TSG-RAN WG4 Meeting #84bis Dubrovnik, Croatia, 9 - 13 October 2017
Agenda Item: 8.25
R4-1711934

## Slide 2: Introduction
The Rel-14 WI on Further enhancements to Coordinated Multi-Point (FeCoMP) Operation for LTE has the following objectives
  Objective of SI or Core part WI or Testing part WI
    The work item aims to specify the enhancements identified during FeCoMP study item. The detailed objectives are as follows.
      Specify enhancements to support non-coherent joint transmission (JT) schemes [RAN1]
        Support of a new QCL assumption for DM-RS antenna ports
        Support of control signalling enhancements to assist QCL,PDSCH REs mapping and resource allocation
        Support possible CSI feedback enhancement
      Specify higher layer support of enhancements listed above [RAN2]
  Objective of Performance part WI
    Specify the necessary UE performance requirements to support non coherent JT.

## Slide 3: UE Demodulation Requirements
Introduce TM10 NC-JT PDSCH demodulation test cases
  Test purpose: Verify performance of UE supporting the following functionality:
    New QCL assumption for different DM-RS antenna port groups
    FFS New QCL PDSCH RE mapping
  Scenario: UE receives NC-JT PDSCH from TP1 (serving cell) and TP2
  Test cases
    Test #1: 2RX UE receives 2 MIMO layers PDSCH (1 MIMO layer per TP)
    FFS Test #2: 4RX UE receives [3 or 4] MIMO layers PDSCH
      3 MIMO layers: 1 MIMO layer from TP1 and 2 MIMO layers from TP2
      4 MIMO layers: 2 MIMO layers per TP
  Power imbalance
    Option 1: No power imbalance between the TPs (SNRTP1 = SNRTP2)
    Other options are not precluded
  Number of CRS APs for each TP are FFS
    Option 1: 2 CRS APs
    Option 1: 4 CRS APs
  FFS for Cell ID among TPs
  CRS patterns in the two cells are FFS
    Option 1: Colliding
    Option 2: Non-Colliding
  Other test case details are FFS

## Slide 4: CSI Reporting Requirements
Introduction of NC-JT CSI reporting test is FFS
Consider the following NC-JT CSI reporting test setup
  Test setup includes 2 TPs
    TP1 is serving cell
    No time/frequency offset between the TPs
    Power imbalance between TPs is FFS
    Different Cell ID among TPs
    CRS patterns in the two cells are FFS
      Option 1: Colliding
      Option 2: Non-colliding
  CSI reporting
    UE is configured with K = 2 NZP CSI-RS resources and one CSI-IM resource
    Maximize the probability of CRI = 2 (NC-JT) reporting
      Option 1: TP1-UE and TP2-UE links have high MIMO correlation channel.
      Option 2: Single CSI-RS antenna port configured per TP.
      Other options are not precluded
    Aperiodic CSI reporting
  Test metrics: Throughput ratio between follow CRI and fixed CRI (γ = TFollowCRI/TFixed, CRI0)