## Slide 1
3GPP TSG-RAN WG4 Meeting #85 R4-1712378
Reno, Nevada, USA, 27 November - 1 December, 2017
Agenda item: 8.20.1 General [NB_IOTenh2]
Document for: Approval
TDD bands for NB IoT family
KDDI Corporation

## Slide 2: Background
In Rel. 15, it was approved that NB IoT family also supports TDD bands.
This contribution is intended to propose possible TDD bands for NB IoT.

## Slide 3: Proposal
Our proposal is to specify TDD bands for NB IoT “at least” same bands as eMTC (Cat.M1) or FeMTC (Cat.M2).
This means that at least E-UTRA bands 39, 40 and 41 should be captured into related specifications such as TS36.101. In other words, UE category NB1 and NB2 should be designed to operate in at least E-UTRA bands 39, 40 and 41.
If there are another possible bands, they should be also added.

## Slide 4: Appendix
According to TS36.101 ver 15.0.0, below bands are applicable for UE Cat.M1 or M2.
  Subtracted from sub clause 5.5E UE category M1 and M2 is designed to operate in the E-UTRA operating bands 1, 2, 3, 4, 5, 7, 8, 11, 12, 13, 14, 18, 19, 20, 21, 25, 26, 27, 28, 31, 66, 71, 72 and 74 in both half duplex FDD mode and full-duplex FDD mode, and in bands 39, 40 and 41 in TDD mode.