## Slide 1: Way forward on SS/PBCH index acquisition requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #85
Reno, NV, USA, 27 November – 1 December 2017
R4-1712786

## Slide 2: Background
Some NR RRM core requirements should include the SS/PBCH index acquisition time
  Example: Reporting of measurement results including SS/PBCH index
The SS/PBCH index acquisition time is derived based on the assumption:
  PBCH-DMRS sequence acquisition time for FR1
  PBCH decoding (NR-MIB) acquisition time for FR2
  Side condition: SNR = [-6]dB and [99]% decoding success rate
RAN1 has designed BCH transport block processing so that UE can perform soft-combining of PBCH with the same SS/PBCH index within the PBCH TTI (80ms).

## Slide 3: Way forward
For FR1, RAN4 should derive the SS/BPCH block index acquisition time from the PBCH-DMRS sequence acquisition time.
For FR2, RAN4 should derive the SS/PBCH block index acquisition time based on the minimum acquisition time between the result of single-shot receiver and the result of soft-combining receiver.
  Soft-combining receiver assumes to combine 2 consecutive PBCHs and 4 consecutive PBCHs with the same SS/BPCH index