## Slide 1: Discussion on asynchronous LTE-NR dual connectivity
NTT DOCOMO, INC.
Agenda Item : 9.3 R4-1713185 Document for : Approval
GPP TSG-RAN WG4 Meeting #85
Reno, US, 27th November – 1st December 2017

## Slide 2: Introduction
At the last RAN4 meeting, the following UE capability was agreed for asynchronous DC between LTE and NR [1]:
  All UEs support asynchronous DC between LTE and NR for inter-band LTE-NR in Rel-15.
    Asynchronous here refers to subframe/slot timing boundary alignment
In this contribution, we further discuss UE capability to enable asynchronous LTE-NR DC while considering the following aspects:
  Single switched UL
  Measurement Gap
Note that the following was already agreed in RAN2 during SI phase [2]
  To support tight interworking between LTE and NR, a technology of aggregating data flows between the two RATs is studied based on Dual Connectivity (DC) for LTE [3]. In DC between LTE and NR, both (e)LTE eNB and NR gNB can act as a master node as described in sub-clause 4.1.2.1, 4.1.2.2 and 4.1.2.3. It is assumed that DC between LTE and NR supports the deployment scenario where LTE eNB is not synchronised with NR gNB.

## Slide 3: Single switched UL for asynchronous NW
For NR, RAN1 agreed to introduce time-switching mechanism of LTE UL and NR UL assuming synchronous NW to avoid strong inter-modulation distortion (IMD) into LTE DL frequency [3]
  For scheduling/HARQ timing of LTE FDD carrier, the following timing can be considered, e.g., for LTE:
    DL-reference UL/DL configuration for TDD
    DL-reference UL/DL configuration defined for FDD-SCell in TDD-FDD CA with TDD-PCell
    Up to NW implementation (i.e., no RAN1 spec. impact)
Observation 1:
  For single switched UL, only synchronous NW has been considered in RAN1, and there is no agreement for asynchronous NW

## Slide 4: Single switched UL for asynchronous NW (cont.)
Observation 2:
  To enable time-switching mechanism for asynchronous NW, eNB and gNB in DC operation need to share SFN/subframe/slot-boundary timing differences, e.g. obtained by SSTD measurement at UE side
  Otherwise, NW cannot know when to apply time-switching of LTE UL and NR UL
D | D | D | D | D | D | D | D | D | D
U | U | U | U | U | U | U | U | U | U
D | U | D | D | D | D | U | D | D | D
time
In those periods, NW needs to avoid simultaneous UL in LTE and NR if single Tx should be applied
LTE FDD:
NR TDD:
(in async.)

## Slide 5: Measurement Gap for asynchronous NW
In LTE, measurement gap length (MGL) is 6ms
  6ms = 5ms (LTE SS periodicity) + 1ms (re-tuning time)
One MGL includes at least one synchronization signal (SS) of target carrier regardless of timing difference between serving and target carriers
 eNB does not need to consider SS location of target carrier
Observation 3:
  In LTE, MGL is designed so that eNB does not need to consider SS location of target carrier
SF#0 | SF#1 | SF#2 | SF#3 | SF#4 | SF#5 | SF#6 | SF#7 | SF#8 | SF#9
Serving carrier:
Target carrier:
(in async.)
SS
5ms window
This window includes at least one SS of target carrier
regardless of timing difference bw serving and target carriers
SF#7 | SF#8 | SF#9 | SF#0 | SF#1 | SF#2 | SF#3 | SF#4 | SF#5 | SF#6
time

## Slide 6: Measurement Gap for asynchronous NW (Cont.)
In NR, almost SS burst set periodicities are larger than SS periodicity of LTE
  SS burst set periodicities: 5, 10, 20 (default), 40, 80, 160 [ms]
Without knowing SS burst set location of target carrier, too large MGL needs to be introduced for asynchronous NW
  E.g. 161ms MGL (=160 + 1) is necessary if SS burst set periodicity is 160 ms
Observation 4:
  For NR, too large MGL needs to be introduced for asynchronous NW unless eNB know SFN/subframe/slot-boundary timing differences of target NR carrier
  This timing difference can be measured by UE, i.e. SSTD measurement
160ms window
 This window includes at least one SS burst set of NR carrier
160ms periodicity
Serving LTE carrier:
Target NR carrier :
time
SS burst set

## Slide 7: Proposal
Proposal:
  All UE shall support SSTD measurement in asynchronous DC between LTE and NR for inter-band LTE-NR in Rel-15
    To enable time-switching of LTE UL and NR UL for asynchronous NW
    Not to introduce too larger MGL than LTE MGL
Note:
  For single switched UL, the paper [4] describes detailed conditions to allow single UL
  For measurement gap, the papers [5, 6] describe the detail of measurement gap mechanism in asynchronous NW.

## Slide 8: References
R4-1711964, Ericsson, Ericsson, MediaTek, WF on synchronous and asynchronous definitions for LTE-NR DC in Rel-15, Oct. 2017
TR38.804, Study on new radio access technology Radio interface protocol aspects (V14.0.0)
R4-1707022, RAN WG1, LS on Single UL transmission, Oct. 2017
R4-1713184 NTT DOCOMO, Conditions on single Tx switched UL, Nov. 2017.
R4-1713011, NTT DOCOMO, Discussion on measurement gap pattern for NR, Nov. 2017.
R4-1713012, NTT DOCOMO, SSTD measurement for asynchronous LTE-NR DC, Nov. 2017.