## Slide 1: Way Forward on RLM
Ericsson
3GPP TSG-RAN WG4 Meeting #85 R4-1713769
Reno, Nevada, USA, November 27th – December 1st 2017
Agenda Item: 9.7.7.2

## Slide 2: Hypothetical PDCCH/DMRS configuration (cont.)
Unless the UE is explicitly signaled which parameter setting to select (for the hypothetical control channel parameters with multiple options), the UE selects the relevant setting in a pre-defined way, e.g., at least for SSB-based RLM:
  A specific type of the CORESET (e.g., one of the RMSI CORESETs) is assumed when defining hypothetical control channel transmission parameters, Note that RAN1 will define a small number of CORESETs for RMSI. For RLM, RAN4 can choose one of them.
  The number of symbols of the hypothetical control channel is the same as for this CORESET,
  The bandwidth of the hypothetical control channel is the same as this CORESET bandwidth,
  The numerology of the hypothetical control channel is the same as this CORESET numerology,
  The hypothetical control channel is assumed to be monitored within a periodic RMSI PDCCH monitoring window (parameters are FFS in RAN1) associated with the SS/PBCH block.
As a baseline, the rules for selecting the relevant non-ambiguous hypothetical setting with CSI-RS can be the same as described above for SS/PBCH block based RLM

## Slide 3: Hypothetical PDCCH/DMRS configuration (cont.)
Hypothetical DMRS transmit power (e.g., boosting or no boosting) is to be specified
Hypothetical DMRS density is to be specified, based on the CORESET

## Slide 4: Hypothetical PDCCH/DMRS configuration (cont.)
Attribute | Value for BLER pair#0 | Value for BLER pair#1
Control channel SCS | Same as SCS of the RMSI CORESETNote 1 | Same as SCS of the RMSI CORESET Note 1
Control channel bandwidth | Same as the bandwidth of RMSI CORESET | Same as the bandwidth of RMSI CORESET
DCI format | In-sync: 30 bits Out-of-sync: 60 bits | FFS
Number of control OFDM symbols | Same as the number of symbols in RMSI CORESET Note 2 | Same as the number of symbols in RMSI CORESETNote 2
Starting OFDM symbol | Symbol#0 | Symbol#0
Aggregation level (CCE) | In-sync: 4 and 8 Out-of-sync: 8 | FFS
REG bundle size | 6 | FFS
Frequency domain resources | FFS (e.g., contiguous or non-contiguous) | FFS
Transmission type | FFS (e.g., interleaved or non-interleaved) | FFS
Ratio of PDCCH RE energy to average SSS RE energy | 0 dB | FFS
Ratio of DMRS energy to average SSS RE energy | 0 dB | FFS
DMRS density | FFS, determined based on the CORESET | FFS, determined based on the CORESET
CP length | Same as the CP length of RMSI CORESET | Same as the CP length of RMSI CORESET
PDCCH monitoring window | FFS | FFS
NOTE 1: 15 kHz, 30 kHz, or 60 kHz for frequency range FR1; 60 kHz and 120 kHz for frequency range FR2. NOTE 2: Can be 1, 2, or 3 OFDM symbols. |  | 

## Slide 5: Transition Requirements
DRX-related transition requirements need to be specified also for NR
Specify/clarify requirements applicable when the set of RLM-RS resources or some parameters for an already configured RLM-RS resource change, e.g.:
  During the transition period, the UE has to meet the most relaxed requirements between those associated with the old configuration of RLM-RS resources and the new configuration of RLM-RS resources. The transition period start from the time when the change is applied or the new configuration is received and last for one most relaxed evaluation period or the longest RLM-RS periodicity among the configured old and new RLM-RS resources.

## Slide 6: OOS Indication Interval
The IS/OOS indications to higher layers (at least when no measurement gaps are configured) has the same period as the configured RLM-RS with the shortest period
The physical layer assesses the link quality for each configured RLM-RS based on all RLM-RS signal instances received during its latest evaluation period

## Slide 7: Evaluation Period
Specify one common evaluation period for all configured RLM-RS resources
The common evaluation period can be based on the longest periodicity of RLM-RSs in the configured RLM-RS resources
The common evaluation period further depends on the measurement gap pattern when it is configured