## Slide 1
3GPP TSG-RAN WG4 Meeting #85 R4-1713970
Reno, Nevada, USA, 27 November - 1 December, 2017
Agenda item: 7.2.1 [LTE_feMTC-Core]
Document for: Approval
Way forward on B1 Cat.M2 A-MPR requirements
KDDI Corporation
<Revision of R4-1712373>

## Slide 2: Agreements in RAN4#85
A-MPR is NOT necessary for Case#1, #3 and #4.
For Case#2, A-MPR is necessary to protect PHS.  Required values are shown in the next slide.

## Slide 3: Required A-MPR for protecting PHS
Channel bandwidth [MHz] | 20 |  |  |  |  | 
Fc (MHz) | 1930 |  |  |  |  | 
(NBindex,RBstart) | (0,0) | (0,3) | (0,6) | (1,0) |  | (1,3)
LCRB | ≥ 15 | 18 | 15 | 15 | ≥18 | 18
A-MPR [dB] | ≤ [4] | ≤ [4] | ≤ [1] | ≤ [1] | ≤ [4] | ≤ [3]
NOTE 1: NBindex is the narrowband index that is defined in 6.2.7 in [4]. The resource block assignment is defined within the narrowband as defined in 5.3.3.1.12 and 5.3.3.1.13 in [5]. |  |  |  |  |  | 

## Slide 4: Proposals
Proposal#1: Approve A-MPR table in the previous slide.
Proposal#2: Review and agree CRs in R4-1712379 (Cat.F CR for Rel. 14) and R4-1712380 (Cat.A CR for Rel. 15).

## Slide 5: Reference
[1] R4-1707427, “Co-existence between B1 Cat.M2 UE and PHS in Japan”, KDDI
[2] R4-1712454, “UE category M2 A-MPR to protect PHS services”, Nokia
[3] R4-1713083, “NS-05 for CAT-M2”, Ericsson
[4] R4-1713081, “MPR simulation for low output power CAT-M2”, Ericsson

## Slide 6: Appendix
Additional simulation results were provided by Nokia during this meeting as shown from next slides.
RAN4 also referred them to estimate A-MPR.

## Slide 7: Appendix: Additional simulation results from Nokia (I)

## Slide 8: Appendix: Additional simulation results from Nokia (II)

## Slide 9: Appendix: Additional simulation results from Nokia (III)