## Slide 1: 3GPP TSG-RAN WG4 Meeting #85 Reno, USA, 27th Nov-2nd Dec, 2017
ZTE, Huawei, Ericsson
WF on the test arrangements for radiated immunity testing for eAAS&NR BS
R4-1714302

## Slide 2: Background
Some intended installation methods for eAAS&NR BS are given in [1], such as rack mounted, wall mounted, ceiling mounted and so on.
For the rack mounted arrangement, the EM susceptibility of the maximum surface (i.e. back surface) will be tested.
For the table-top arrangement, the EM susceptibility of the maximum surface (i.e. back surface) will not be tested.
Different test arrangements may cause different test results for radiated immunity testing.

## Slide 3: WF Agreement
For the radiated immunity testing of OTA AAS BS, NR BS type 1-O and NR BS type 2-O, the test shall be performed in configuration allowing EM susceptibility testing of the maximum surface.
The EMC RF electromagnetic field immunity requirement for the above BS types applies in the range of angles except the operational range of angles of BS antenna (i.e. except for the half sphere around the main lobe direction),
In order to allow EM susceptibility testing of the maximum surface for OTA AAS BS, NR BS type 1-O and NR BS type 2-O, the EUT shall be mounted using rack mount, if possible.
  NOTE: Table-top testing for the above BS types does not fulfill the maximum surface testing principle.

## Slide 4: References
[1] R4-1713043, Discussion on the test arrangements for radiated immunity testing to NR BS. ZTE