## Slide 1: Way forward on single UL transmission
Apple, Nokia, Vodafone, OPPO, Xiaomi, China Unicom, Sprint, vivo, AT&T, Verizon, ZTE, Qualcomm, China Telecom, SoftBank, Orange, NTT DoCoMo, KT
3GPP TSG RAN WG4 NR
Reno, USA, 27th – 30th Nov 2017
R4-1714356

## Slide 2: Background: RAN4 84b agreements (R4-1711618)
Formula:
  Interference bandwidth: IBW = |a| x CBW1 + |b| x CBW2
    |a| + |b| = 2 (or 3)
    CBW1 and CBW2 are UL channels
  Center frequency of IBW: fIBW = a x f1 + b x f2
    f1 and f2 are center frequency of each UL channel
  The range of IMD 2 (or 3): [fIBW – IBW/2, fIBW + IBW/2]
RAN4 shall discuss the definition of UL and DL channels in the next meeting
  Alt.1. spectrum holdings of a operator in a band
  Alt.2. aggregated UE channel bandwidth configured by the network
  Alt.3. transmission bandwidth

## Slide 3: Proposal
Alt.3 is used in UL and DL channels definition input to the formula in R4-1711618
  Both Case 1 and Case 2 operation and corresponding HARQ timing (as agreed in RAN1 agreement) shall be supported
  Case 1 operation is semi-statically configured by the RRC reconfiguration
IMD impact to LTE secondary component carriers will not be considered.
NOTE: Case 1 and Case 2 operations are fully defined on the next slide.

## Slide 4: Annex: Case 1 and Case 2 Definitions from RAN1
When the UE is configured with multiple UL carriers on different frequencies (where there is at least one LTE carrier and at least one NR carrier of a different carrier frequency), but the UE operates on only one of the carriers at a given time among a pair of LTE and NR carriers
– For LTE carrier, UE can be configured with
  • Case 1: DL-reference UL/DL configuration defined for LTE-FDD-SCell in LTE-TDD-FDD CA with LTE-TDD-PCell
    – For scheduling/HARQ timing of LTE FDD carrier, DL-reference UL/DL configuration defined for LTE-FDD-SCell in LTE-TDD-FDD CA with LTE-TDD-PCell is applied
    – UE is allowed to transmit NR UL signals at least in the subframe(s) where LTE UL transmission is not allowed according to the DL-reference UL/DL configuration
    – FFS whether or not a UE-specific subframe offset for the DL-reference UL/DL configuration can be configured considering system resource utilization and potential spec impact
  • Case 2: Release 15 LTE-FDD HARQ timing
    – No impact on LTE RAN1 specifications