## Slide 1: REFSENS FR1 re-farmed bands
Ericsson
R4-1714451

## Slide 2: Scope
NF assumption for devising REFSENS requirements for re-farmed bands
Modify the NF for which the corresponding LTE requirement is based on an obviously excessive NF
  Low bands up to NF = 12 dB
Aim to devise REFSENS for re-farmed bands: do not ”copy” LTE across the line

## Slide 3: Background: prerequisites for Rel-8 specification
Very limited filter data (none for some bands)
Different filter technology (not SAW or BAW)
IM large, only prototype/demonstrator LTE radios available
From R4-080696 (Ericsson):
  “Next, turning to the noise figure, we assume 9 dB and an implementation margin (including TX noise) of 2 dB. For other bands, we propose additional relaxations of 1, 2 and 3 dB for duplexer distance / band gap > 1.5, 2 and 4, respectively.”

## Slide 4: WF for re-farmed bands
Revaluate NF assumption for the following re-farmed bands
  Put NR requirements for band n2, n3, n5, n8, n20, n28, n71 within square brackets amongst the bands agreed thus far

## Slide 5: Notes:
The IM is not discussed; an IM = 2.5 dB assumed (same as LTE)
  IM a separate disussion
SNR = -1 dB