## Slide 1: WF on some clarification issues for wideband operation
LG Electronics, Intel
R4-1714474
3GPP TSG-RAN WG4 #85 Meeting
Reno, Nevada, USA, Nov. 27 – Dec. 01, 2017
Agenda: 9.3.1.2

## Slide 2: Background (1)
In RAN4 #85 meeting, RAN4 has discussed the related UE RF requirements and UE capability for wideband operation.
  UE behavior
  CA operation
  BWP switching
  UE RF requirements
  UE capability

## Slide 3: Figure 1: How to handle different numerologies in different BWP configurations (single CC case)
Rel-15 gNB
BS CC1
(400MHz)
BWP(1,1)
(60kHz)
time
BWP(1,1)
(60kHz)
BWP(1,1)
(120kHz)
BS CC1
(800MHz)
Rel-x gNB
BS CC2
(400MHz)
UE1 CC1
(400MHz)
single numerology (O)
RAN4 view:
Different numerology in each BWP will be
supported in rel-15
UE2 CC1
(200MHz)
UE2 CC2
(200MHz)

## Slide 4: Figure 2: How to handle different numerologies in different BWP configurations (multiple CC case)
Rel-15 gNB
BS CC1
(400MHz)
time
BS CC1
(800MHz)
Rel-x gNB
BS CC2
(400MHz)
BWP(1,1)
SCS(1,1)
BWP(2,1)
SCS(2,1)
Case 1: contiguous CCs and contiguous BWPs in rel-15
UE1 CC1
(200MHz)
UE1 CC2
(200MHz)
BWP(1,1)
SCS(1,1)
BWP(2,1)
SCS(2,1)
Case 2: contiguous CCs and non-contiguous BWPs in rel-15
BWP(1,1)
SCS(1,1)
BWP(1,2)
SCS(1,2)
Case3: In future release, RAN1 will support multiple BWPs in a serving cell, then UE can support mixed numerology as UE capability

## Slide 5
UE behavior
  The UE meets RF requirements based on the according to set of UE CBW (no additional BWP related RF requirements)
    FFS how to handle configured BWP bandwidth less than UE CBW
  How the UE configures its RF in order to operate the BWP and meet the CBW based RF requirements is implementation dependent
BWP switching
  How to handle different numerologies in different BWP switching (single CC case)? (illustrated in Figure 1)
    Agreement: Different numerology in each BWP will be supported in rel-15
  How to handle BWP switching delay
    Option 1: Specify in UE RF requirements as a time mask
    Option 2: Inform RAN1 of scenarios and related switching delays and let RAN1 to take this information into account
    Option 3: Solve as UE implementation
    Agreement: Adopt Option 2; switching delay is FFS
Agreements (1)

## Slide 6
CA operation from chairman’s notes
  SU agreement
    Option1: Spectral utilization based on individual CCs (UE CC1 and UE CC2)
      E.g. for 50MHz sub6, SU is 65RBs, for 100MHz SU is 135, UE configured with 2x50MHz in 100MHz channel is using 130RBs
    FFS for UE capability to support SU according to wide channel bandwidth
  PRB agreement from the Chairman’s notes
    For wideband operation, PRBs for BWP shall not violate the UE minimum guardband
    UE minimum guardband definition is FFS.
Agreements (2)

## Slide 7
Summary of the impact of wideband operation on RF requirements
  UE RF requirements and UE behavior : not specified in TS38.101
    Single BWP case: single CC RF requirements apply with full CC BW allocation
    Multiple BWPs case : intra-band CA RF requirements apply with full CC BW allocation
  BWP switching delay: not specified in TS38.101 as a time mask
  Different numerology in each BWP for single CC will be supported in rel-15 assuming single active BWP.
Agreements (3)

## Slide 8
The list of UE capabilities related to wideband operation will be finalized during RAN4 NR AH#4 based on agreements (1) through (3) in this WF
Agreements (4)