## Slide 1: Way forward on the SSB time index acquisition time
Huawei, HiSilicon, …
3GPP TSG-RAN WG4 Meeting #85 Reno, USA, 27th November – 1st December 2017
R4-1713442

## Slide 2: Background (1/2)
After RAN1 #90bis, redesign of SSB/PBCH has been agreed and no further redesign is allowed.
Redesign of SSB/PBCH can be illustrated as follows:

## Slide 3: Background (2/2)
RAN4 has the following observations according to RAN1 agreements:
  It is considered that, in each SMTC configured for a certain UE operations of SSB/PBCH acquisition, only 1 SSB can be seen by the UE for the worst case due to beam switching.
  For sub-6GHz, 3bits of SSB time index are indicated by PBCH-DMRS sequence.
  For above-6GHz, 3 other bits of SSB time index other than DMRS are carried in PBCH MIB payload.

## Slide 4: RAN4 conclusions
RAN4 has the following observations for NR SSB/PBCH acquisition time after link level simulations with SSB redesign considered:
  PBCH-DMRS and PBCH MIB acquisition for SSB time index
    For sub-6GHz, only DMRS acquisition is needed for SSB time index reading. Simulation results show that 2 attempts of PBCH-DMRS are needed at -6dB.
    For above-6GHz, DMRS acquisition and PBCH MIB are both needed for SSB time index reading. Simulation results show that 2 attempts of PBCH-DMRS are needed at -6dB. Further 2 attempts of PBCH MIB are needed at -6dB.