## Slide 1: Way forward on eV2X RRM requirements
Huawei, HiSilicon,
3GPP TSG-RAN WG4 Meeting #85 R4-1713922
Reno, USA, November 27th – December 1st, 2017
Agenda Item: 8.19.3

## Slide 2: Proposal for V2X Carrier Aggregation
Synchronization requirements
  For Maximum Receive Timing Difference (MRTD) and Maximum Transmission Timing Difference (MTTD)
    No need to introduce MRTD and MTTD requirements for V2X intra-band contiguous CA
    FFS whether to define MRTD/MTTD requirements for V2X non-contiguous (including inter-band and intra-band non-contiguous) CA
      Interested companies are encouraged to provide the definition of MRTD/MTTD for V2X CA
  No impacts are foreseen on the following requirements:
    UE Transmit Timing
    Initiation/Cease of SLSS Transmissions
  The existing requirements on selection/reselection of V2X SyncRef UE are applied for the component carrier(s) configured as the synchronization carrier.

## Slide 3: Proposal for V2X Carrier Aggregation
The delay and interruption requirements for CC addition/release based on dedicated RRC signaling need be introduced.
  FFS whether there is interruption to PCell and activated SCell on Uu link(s).
  FFS on RRC processing time
  FFS on RF tuning/retuning time in the case of transmission timing alignment for all CCs aggregated for V2X
The existing PSSCH-RSRP and S-RSSI measurement requirements of single CC can be reused.