## Slide 1: WF on MPR for sub6GHz
NTT DOCOMO, INC., [Intel, ZTE, Ericsson, LGE, Huawei, Qualcomm, Nokia, CMCC, Skyworks]
3GPP TSG-RAN WG4 #85 Meeting
Reno, US, 27 November - 1 December 2017
R4-1714047

## Slide 2: Background
Tentative MPR for sub6GHz was agreed in RAN4#84bis [1]
Companies have checked if the tentative values are acceptable until RAN4#85 and provided their proposals as shown in next slide
[1] R4-1711559, “WF on MPR for Sub-6 NR”, Qualcomm Incorporated, Nokia, Skyworks Solutions

## Slide 3: Summary of sub6 MPR in RAN4#85
 |  | Intel (2329) | ZTE (2509) | E/// (2528) | LGE (2851) | HW (3123/3124) | QC (3836) | Nokia (2446) | CMCC (rev of 2912) |  |  |  |  |  | 
Allocation type |  | Outer (max MPR) |  |  |  |  |  |  |  |  |  |  |  |  | 
LCRB |  | all |  |  |  |  |  |  |  |  |  |  |  |  | 
Distance from channel edge |  | <LCRB/2 from edge |  |  |  |  |  |  |  |  |  |  |  |  | 
WF type | modulation | MPR For all BW and SCS |  |  |  |  |  |  |  | ave | std | med | possible agreement by session chairman | R4-1711559 | 
DFT-s-OFDM | PI/2 BPSK | 1 | N/A | N/A | 0.5 | 0 | 2 | 0 | N/A | 0.70 | 0.84 | 0.50 | 0.5 | [0] | dB
 | QPSK | 1.5 | N/A | 0.7 | 1.5 | 0.5 | 2 | 0.5 | 0.5 | 1.03 | 0.62 | 0.70 | 1 | [1] | dB
 | 16QAM | 2 | N/A | 1.4 | 2 | 1.5 | 2.5 | 1 | 0.95 | 1.62 | 0.57 | 1.50 | 1.5 | [1.5] | dB
CP-OFDM | QPSK | 3.5 | 3 | 3.8 | 3.5 | 3 | 4 | 2.5 | 2.15 | 3.18 | 0.64 | 3.25 | 3.5 | [3] | dB
 | 16QAM | 3.5 | 3.5 | 3.1 | 3.5 | 3 | 4.5 | 2.5 | 2.2 | 3.23 | 0.71 | 3.30 | 3 | [3] | dB
 | 64QAM | 3.5 | 3.5 | 2.9 | 3.5 | 3 | 4.5 | 2.5 | 2.2 | 3.20 | 0.72 | 3.25 | 3 | [3] | dB
 | 256QAM | 7 | N/A | N/A | 7 | 6.5 | 7 | 5 | TBD | 6.50 | 0.87 | 7.00 | 6 | [7] | dB
 |  | Intel (12329) | ZTE (12509) | E/// (12528) | LGE (12851) | HW (13123/13124) | QC (13836) | Nokia (12446) | CMCC (rev of 2912) |  |  |  |  |  | 
Allocation type |  | Inner (min MPR) |  |  |  |  |  |  |  |  |  |  |  |  | 
LCRB |  | ≤LCRBmax/2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Distance from channel edge |  | ≥LCRB/2 from edge |  |  |  |  |  |  |  |  |  |  |  |  | 
WF type | modulation | MPR For all BW and SCS |  |  |  |  |  |  |  | ave | std | med | possible agreement by session chairman | R4-1711559 | 
DFT-s-OFDM | PI/2 BPSK | 0 | N/A | N/A | 0.5 | 0 | 0 | 0 | N/A | 0.10 | 0.22 | 0.00 | 0 | 0 | dB
 | QPSK | 0.5 | N/A | 0 | 0.5 | 0 | 0 | 0 | 0 | 0.14 | 0.24 | 0.00 | 0 | [0] | dB
 | 16QAM | 0.5 | N/A | 0.4 | 1 | 0 | 1 | 0 | 0 | 0.41 | 0.45 | 0.40 | 0.5 | [0.5] | dB
 | 64QAM | 2 | N/A | 1.2 | 2 | 1.5 | 2.5 | 1 | 1.06 | 1.61 | 0.57 | 1.50 | 1.5 | [2] | 
 | 256QAM | 4.5 | N/A |  | 4.5 | 4.5 | 5 | 3 | TBD | 4.30 | 0.76 | 4.50 | 4.5 | [5] | 
CP-OFDM | QPSK | 2 | 1 | 1.4 | 1.5 | 1 | 2 | 0 | 0 | 1.11 | 0.78 | 1.20 | 1 | [0.5] | dB
 | 16QAM | 2 | 2 | 0.8 | 2.5 | 1.5 | 3 | 1 | 0 | 1.60 | 0.98 | 1.75 | 2 | [1.5] | dB
 | 64QAM | 3.5 | 3 | 2.9 | 3.5 | 3 | 4.5 | 2.5 | 2.2 | 3.14 | 0.71 | 3.00 | 3 | [3] | dB
Agreed in RAN4#85

## Slide 4: TS 38.101-1 after RAN4#85
6.2.2 UE maximum output power reduction
UE is allowed to reduce the maximum output power due to higher order modulations and transmit bandwidth configurations. For UE Power Class 3, the allowed maximum power reduction (MPR) is defined in Table 6.2.2-1.
Table 6.2.2-1 Maximum power reduction (MPR) for power class 3
Where the following parameters are defined to specify valid RB allocation ranges for Outer and Inner RB allocations:
  LCRBmax is the maximum number of RB for a given Channel bandwidth and sub-carrier spacing derived from from spectrum utilization.
  RBstartLow = LCRB/2 rounded down to next integer with floor at 1
  RBstartHigh = LCRBmax – RBstartLow – LCRB
Where Inner RB allocation range is specified as follows: Inner RB allocation are LCRB/2 away from each edge of the maximum RB allocation for all LCRB ≤ LCRBmax/2 rounded up to the next integer.
  RBstartInner : valid RBstart values for Inner RB allocations
  For LCRB ≤ LCRBmax/2 rounded up to the next integer, RBstartLow ≤ RBstartInner ≤ RBstartHigh
Where Outer RB allocation range is all allocations which are not Inner RB allocation
For the UE maximum output power modified by MPR, the power limits specified in subclause 6.2.5 apply.
Modulation | MPR (dB) | 
 | Outer RB allocations | Inner RB allocations
DFT-s-OFDM PI/2 BPSK | ≤ TBD | 0
DFT-s-OFDM QPSK | ≤ TBD | 0
DFT-s-OFDM 16 QAM | ≤ TBD | ≤ TBD
DFT-s-OFDM 64 QAM | ≤ TBD | 
DFT-s-OFDM 256 QAM | 4.5 | 
CP-OFDM QPSK | ≤ TBD | ≤ TBD
CP-OFDM 16 QAM | ≤ TBD | ≤ TBD
CP-OFDM 64 QAM | ≤ TBD | 
CP-OFDM 256 QAM | ≤ TBD |