## Slide 1: WF on UE mandatory channel bandwidth for NR bands
NTT DOCOMO, …
3GPP TSG-RAN WG4 #85 meeting
Reno, US, 28th Nov. – 1st Dec., 2017
R4-1714105

## Slide 2: Background
Definition of UE Channel bandwidth (R4-1709930):
  The RF bandwidth supporting a single NR RF carrier with the transmission bandwidth configured in the uplink or downlink of a cell. The channel bandwidth is measured in MHz and is used as a reference for transmitter and receiver RF requirements.
Agreements at RAN4 #NR-AH2 (R4-1706977):
  UE can support different max CBW in DL and UL
  UE can operate with different UL and DL bandwidth.
Agreements at RAN4 #84 (R4-1708845):
  UE maximum channel bandwidth is a UE capability. UE can support different max CBW in DL and UL
    It is FFS if the UE capability is per band or a group of bands (such as sub6 and mmWave)
  UE shall meet either a single carrier or CA based RF requirements for the channel bandwidths in Slide #3-#4 that is equal to or smaller than UE maximum channel bandwidth for any SCS.
  RAN4 should agree some threshold value for which BW’s should be supported by single CC configuration.

## Slide 3: Current operator’s request (for information)
Below 3GHz
NR Band | Data SCS = 15kHz |  |  |  |  |  |  |  |  | Data SCS = 30kHz |  |  |  |  |  |  |  |  | Data SCS = 60kHz (for more than 1GHz bands) |  |  |  |  |  |  |  |  | 
 | 5MHz | 10MHz | 15MHz | 20MHz | 25MHz | 30MHz | 40MHz | 50MHz | 15MHz | 10MHz (Note 1) | 20MHz | 25MHz | 30MHz | 40MHz | 50MHz | 60MHz | 80MHz (Note 2) | 100 MHz (Note 2) | 10MHz (Note 1) | 15MHz (Note 1) | 20MHz (Note 1) | 25MHz (Note 1) | 30MHz | 40MHz | 50MHz | 60MHz | 80MHz (Note 2) | 100 MHz (Note 2)
1.427-1.518 GHz | Yes | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  | 
Band 1 | Yes | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  | 
Band 2 | Yes | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  | 
Band 3 | Yes | Yes | Yes | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | Yes |  |  |  |  |  | Yes | Yes | Yes | Yes | Yes |  |  |  |  | 
Band 5 | Yes | Yes | Yes |  |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  | 
Band 7 | Yes | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  | 
Band 8 | Yes | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Band 20 | Yes | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Band 28 | Yes | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Band 38 | Yes | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  | 
Band 41 |  | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | Yes
Band 50 |  | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes | Yes |  |  | Yes | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  | 
Band 51 | Yes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Band 66 | Yes | Yes | Yes | Yes |  |  | Yes |  | Yes | Yes | Yes |  |  | Yes |  |  |  |  | Yes | Yes | Yes |  |  | Yes |  |  |  | 
Band 70 | Yes | Yes | Yes | Yes | Yes |  |  |  | Yes | Yes | Yes | Yes |  |  |  |  |  |  | Yes | Yes | Yes | Yes |  |  |  |  |  | 
Band 71 | Yes | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Band 74 | Yes | Yes | Yes | Yes |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  |  | Yes | Yes | Yes |  |  |  |  |  |  | 
Band 75 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Band 76 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Note 1: 90% spectrum utilization may not be achieved Note 2: UE may support this Channel Bandwidth |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Note: 30MHz was agreed to introduce into band n3 in RAN4 #85.

## Slide 4: Current operator’s request (for information)
3GHz – 6Ghz [2]
  n77, n78
  n79
n77/78 | UE channel bandwidth [MHz] |  |  |  |  |  |  |  |  |  |  |  | 
Operator | Data SCS = 15kHz |  |  |  |  | Data SCS = 30kHz |  |  |  |  |  |  | 
 | 10 | 15 | 20 | 40 | 50 | 10 | 15 | 20 | 40 | 50 | 60 | 80 | 100
Operator A, B, C, D, E |  |  | M | M | M |  |  | M | M | M | M | M | M
Operator F, G, L | M | M | M | M | M | M | M | M | M | M | M | M | M
Operator H |  |  |  | M | M |  |  |  | M | M | M | M | M
Operator I | M |  | M | M | M | M |  | M | M | M | M | M | M
n79 | UE channel bandwidth [MHz] |  |  |  |  |  | 
Operator | Data SCS = 15kHz |  | Data SCS = 30kHz |  |  |  | 
 | 40 | 50 | 40 | 50 | 60 | 80 | 100
Operator A, B, C | M | M | M | M | M | M | M

## Slide 5: Current operator’s request (for information)
24.25-52.6GHz (FR2) [2]
  n257, n258
  n259
n257/258 | UE channel bandwidth [MHz] |  |  |  |  |  | 
Operator | Data SCS = 60kHz |  |  | Data SCS = 120kHz |  |  | 
 | 50 | 100 | 200 | 50 | 100 | 200 | 400
Operator A, B, C, L | M | M | M | M | M | M | 
Operator D, E, J, K | M | M | M | M | M | M | M
n260 | UE channel bandwidth [MHz] |  |  |  |  |  | 
Operator | Data SCS = 60kHz |  |  | Data SCS = 120kHz |  |  | 
 | 50 | 100 | 200 | 50 | 100 | 200 | 400
Operator J, K | M | M | M | M | M | M | M

## Slide 6: Way forward
For Rel.15 NR UE, RAN4 introduce some threshold value for each frequency range for which BW’s should be supported by single CC configuration in terms of RF
  Frequency range: below [2.49]3GHz, [2.49]3-6GHz, 24.25-52.6GHz (FR2)
  Carrier Aggregation support shall be discussed separately
  FFS: SCS-specific threshold or maximum threshold within SCS

## Slide 7: Proposed threshold
Agree the following threshold values as working assumption
  The values could be revisit if some issues to support those values are identified considering supported MIMO layers, modulation order, etc
  Low cost UE capability (i.e. low data rate devices) for SA NR UE is not precluded and is to be handled separately
Freq. range |  | Threshold
Below [2.49]GHz | DL | no less than 40MHz
 | UL | no less than 40MHz
[2.49]-6GHz | DL | no less than 60MHz
 | UL | no less than 60MHz
24.25-52.6GHz | DL | no less than 200MHz
 | UL | no less than 200MHz

## Slide 8: References
R4-1712155 New UE mandatory channel bandwidth for NR band3 China Unicom
R4-1712165 UE Channel Bandwidth support in NR Dish Network
R4-1713179 Discussion on UE mandatory channel bandwidth for new NR bands NTT DOCOMO, INC.
R4-1713543 NR channel bandwidth and UE mandatory channel bandwidth for NR Band 3 China Unicom