## Slide 1: WF on FeCoMP UE Demodulation and CSI Reporting Requirements
Intel Corporation, ZTE, Qualcomm,
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #85 Reno, Nevada, USA, 27 November - 1 December 2017
Agenda Item: 8.25
R4-1714260

## Slide 2: UE Demodulation Requirements (1)
Test purpose: Verify performance of UE supporting the following functionality:
  RAN4 84bis: New QCL assumption for different DM-RS antenna port groups
RAN4 84bis: Scenario: UE receives NC-JT PDSCH from TP1 (serving cell) and TP2
Test cases
  RAN4 84bis: Test #1: 2RX UE receives 2 MIMO layers PDSCH (1 MIMO layer per TP)
  Test #2: 4RX UE, 3 MIMO layers PDSCH (2 MIMO layer from TP1 and 1 MIMO layer from TP2)
  FFS whether to have test with 4 MIMO layers PDSCH
Antenna configuration:
  Test #1: 2x2 ULA low (for TP1-UE and TP2-UE links)
  Test #2: 4x4 ULA low (for TP1-UE and TP2-UE links)
Power imbalance
  Test #1: Equal power between the TPs (SNRTP1 = SNRTP2)
  Test #2: TP2 SNR is [3] dB lower than TP1 SNR (SNRTP1 = SNRTP2 + [3]dB)

## Slide 3: UE Demodulation Requirements (2)
FRC:
  Test #1: 16QAM,1/2, Rank 1 for each TP
  Test #2:
    TP1: 16QAM, 1/2, Rank 2
    TP2: 16QAM, 1/2, Rank 1
Number of CRS APs:
  Test #1: 2 CRS APs for each TP
  Test #2: FFS between 2 and 4 CRS APs for each TP
Beamforming model: Random PMI
Cell ID
  TP1: 0
  TP2: 126
Time offset: 2 μs TP2 time offset relative to TP1
Frequency offset: 200 Hz TP2 frequency offset relative to TP1
Number of control OFDM symbols: 2

## Slide 4: CSI Reporting Requirements (1)
Introduce NC-JT CSI reporting test case
Candidate test methodology
  Option 1:
    Test purpose: Verify proper CRI = 2 reporting
    Fixed RI and CQI (fixed reference channel)
      Option 1: Rank 1, 16QAM, MCS 13
      Other options are not precluded
    Follow PMI
    Test metrics:
      Use the following metrics:
      is [X] % of the maximum throughput obtained at SNRFollowCRI using the CRI configured according to the CSI UE report
      is the throughput obtained at SNRFollowCRI under assumption of single TP transmission (TP1 transmission)
  FFS other options

## Slide 5: CSI Reporting Requirements (2)
Candidate test setup
  Option 1:
    Test setup includes 2 TPs (serving TP1 and TP2)
      No time/frequency offset between the TPs
      Power imbalance between TPs is FFS
      Colliding CRS patterns with Different Cell IDs
    Antenna configuration: 2x2 ULA Low antenna correlation (for TP1-UE and TP2-UE links)
    CSI reporting
      UE is configured with K = 2 NZP CSI-RS resources and one CSI-IM resource
      2 CSI-RS antenna ports are configured for each NZP CSI-RS resource
      ZP CSI-RS configurations are aligned among TPs
      Aperiodic CSI reporting
  Other options not precluded