## Slide 1: WF on FR2 REFSENS
Intel Corporation
R4-1714354
3GPP TSG-RAN WG4 Meeting #85
Reno, Nevada, USA, November 27 – December 1, 2017
Agenda: 9.4.4.1.2

## Slide 2: Background
In RAN4 #85, FR2 REFSENS definition was discussed. Overall, there is agreement on using beam peak EIS for definition, but alignment on some parameters used in the sensitivity equation is needed
  There was significant variation in the reported diversity gain values
  Using a table with greater granularity on loss terms included in the total Implementation Loss will help companies agree on a value
A summary of reported values is presented, as well as options for choosing a beam peak EIS value
How to test REFSENS using OTA was also discussed [1]. The approved document proposes choosing between three different approaches.
  Agreement on which approach to use is pending

## Slide 3: Way Forward – Work Plan
Align on equation parameters for beam peak EIS calculation
  Use the table in slide 5 as guideline for accounted losses in Implementation Loss parameter
  Agree on diversity gain value based on points made [2,3]
Discuss updated values and finalize beam peak EIS definition in RAN4 AH #1801. The options for requirement definition are:
  Option 1: Maximum across all companies
  Option 2: Average across all companies
  Option 3: XXth percentile of CDF of proposals
For testability, discussion and agreement on an approach to take place during RAN4 AH #1801. The three proposed approaches are found in slide 4.

## Slide 4: Way Forward – Work Plan (2)
Approach | Test Point | Procedure
1 | (qpeak,q,f peak,q) & (qpeak,f,f peak,f) | Position the UE so that the peak gain for the q-polarization is formed towards the measurement antenna Adjust the test signal power so that the power of the q-polarization at the centre of the quiet zone matches the REFSENS power level Determine whether the throughput meets/exceeds the requirements for the specified reference measurement channel Position the UE so that the peak gain for the f-polarization is formed towards the measurement antenna Adjust the test signal power so that the power of the f-polarization at the centre of the quiet zone matches the REFSENS power level Determine whether the throughput meets/exceeds the requirements for the specified reference measurement channel Whether the REFSENS test case has passed with just one pass or two passes is TBD
2 | qpeak,i,fpeak,i | Position the UE so that the peak gain for the strongest individual polarization is formed towards the measurement antenna Adjust the test signal power so that the power at the centre of the quiet zone matches the REFSENS power level Determine whether the throughput meets/exceeds the requirements for the specified reference measurement channel
3 | qpeak,T,fpeak,T | Position the UE so that the peak gain for the q-polarization is formed towards the measurement antenna Measure the EISq for q-polarization, i.e., the power level for the q-polarization at which the throughput exceeds the requirements for the specified reference measurement channel Position the UE so that the peak gain for the f-polarization is formed towards the measurement antenna Measure the EISf for f-polarization, i.e., the power level for the f-polarization at which the throughput exceeds the requirements for the specified reference measurement channel Calculate the resulting EIS for the total component EIST=[1/EISq +1/EISf]-1 Determine whether REFSENS meets/exceeds EIST

## Slide 5: Implementation Loss
Parameter | Comments
Mismatch and transmission line loss | Array topology dependent, material dependent, transmission line design dependent; includes impact of load pull
Beam forming loss (phase shifter and amplitude error) | Phase shifter quantization and amplitude accuracy dependent
Form factor integration | Losses due to integrating the antenna array within a form factor spanning a variety of potential placements and materials
Module/assembly variations | Includes fabrication tolerances, registration and alignment issues for the design, as well as any substrate irregularities
The table below, provides details on the parameters included in the Implementation Loss term [4]

## Slide 6: Summary of proposed beam peak EIS @ 28 GHz
 | Intel [5] | LGE [5] | Huawei [6] | MediaTek [2] | Qualcomm [7]
kTB/Hz [dBm] | -174 | -174 | -174 | -174 | -174
10log(Rx BW) [dB] | 76.99 | 76.77 | 76.99 | 76.99 | 76.99
Effective realized antenna array gain [dB] 1 | 8 | 10 | 9 | 7 | 8.7
Diversity Gain [dB] | 2.2 | 2.2 | 1 | 0 | 0
SNR [dB] | -1 | -1 | -1 | -1 | -1
NF [dB] | 10 | 10 | 10 | 9 | 10
Total Implementation Loss [dB] | 9.6 | 8.5 | 7 | 6.7 | 4.6
Form factor de-sense (FFD) | 1 | - | - | - | -
Sensitivity EIS [dBm] | -87.61 | -91.93 | -91.01 | -89.31 | -92.11
1 Effective realized antenna array gain includes realized array gain + roll-off

## Slide 7: Summary of proposed EIS @ 28 GHz – Div G = 0
 | Intel [5] | LGE [5] | Huawei [6] | MediaTek [2] | Qualcomm [7]
kTB/Hz [dBm] | -174 | -174 | -174 | -174 | -174
10log(Rx BW) [dB] | 76.99 | 76.77 | 76.99 | 76.99 | 76.99
Effective realized antenna array gain [dB] 1 | 8 | 10 | 9 | 7 | 8.7
Diversity Gain [dB] | 0 | 0 | 0 | 0 | 0
SNR [dB] | -1 | -1 | -1 | -1 | -1
NF [dB] | 10 | 10 | 10 | 9 | 10
Total Implementation Loss [dB] | 9.6 | 8.5 | 7 | 6.7 | 4.6
Form factor de-sense (FFD) | 1 | - | - | - | -
Sensitivity EIS [dBm] | -85.41 | -89.73 | -90.01 | -89.31 | -92.11
1 Effective realized antenna array gain includes realized array gain + roll-off

## Slide 8: Summary of proposed beam peak EIS @ 39 GHz
 | Intel [5] | LGE [5] | Huawei [6] | MediaTek [2] | Qualcomm [7]
kTB/Hz [dBm] | -174 | -174 | -174 | -174 | -174
10log(Rx BW) [dB] | 76.99 | 76.77 | 76.99 | 76.99 | 76.99
Effective realized antenna array gain [dB] 1 | 7.5 | 9 | 9 | 8.5 | 10.4
Diversity Gain [dB] | 2.2 | 2.2 | 1 | 0 | 0
SNR [dB] | -1 | -1 | -1 | -1 | -1
NF [dB] | 11 | 11 | 12 | 10.5 | 11.6
Total Implementation Loss [dB] | 10.9 | 9.5 | 8 | 7.7 | 5.0
Form factor de-sense (FFD) | 1 | - | - | - | -
Sensitivity EIS [dBm] | -84.81 | -88.93 | -88.01 | -88.31 | -91.81
1 Effective realized antenna array gain includes realized array gain + roll-off

## Slide 9: Summary of proposed EIS @ 39 GHz – Div G = 0
 | Intel [5] | LGE [5] | Huawei [6] | MediaTek [2] | Qualcomm [7]
kTB/Hz [dBm] | -174 | -174 | -174 | -174 | -174
10log(Rx BW) [dB] | 76.99 | 76.77 | 76.99 | 76.99 | 76.99
Effective realized antenna array gain [dB] 1 | 7.5 | 9 | 9 | 8.5 | 10.4
Diversity Gain [dB] | 0 | 0 | 0 | 0 | 0
SNR [dB] | -1 | -1 | -1 | -1 | -1
NF [dB] | 11 | 11 | 12 | 10.5 | 11.6
Total Implementation Loss [dB] | 10.9 | 9.5 | 8 | 7.7 | 5.0
Form factor de-sense (FFD) | 1 | - | - | - | -
Sensitivity EIS [dBm] | -82.61 | -86.73 | -87.01 | -88.31 | -91.81
1 Effective realized antenna array gain includes realized array gain + roll-off

## Slide 10
References
# | Tdoc | Title | Source
[1] | R4-1713678 | On Testing REFSENS using OTA for FR2 | Rohde & Schwarz
[2] | R4-1712935 | NR FR2 UE REFSENS | MediaTek
[3] | R4-1713696 | Array antenna receiver characteristics | Sony, Ericsson
[4] | R4-1712319 | UE power class for FR2 | Intel, Apple, OPPO, Samsung, LGE, Xiaomi, MediaTek, Motorola, Huawei
[5] | R4-1712321 | REFSENS for FR2 | Intel, Apple, LGE, OPPO, Xiaomi
[6] | R4-1712924 | mmWave smartphone EIS results update | Huawei, HiSilicon
[7] | R4-1714031 | mmW UE Sensitivity | Qualcomm