## Slide 1: WF on simulation assumption for NR FR2 BS EVM 256QAM
NTT DOCOMO, INC., Huawei, ZTE
R4-1714524
3GPP TSG- RAN Working Group 4 (Radio) meeting #85
Reno, USA, 27th November – 1st December, 2017
Agenda Item: 9.5.2.4.2.1 OTA EVM [NR_newRAT]

## Slide 2: Background
Discussion for how to evaluate the NR EVM for FR2 have been provided in contributions [1, 2].
The effectivity of 256QAM modulation scheme for FR2 is not clear and EVM for 256QAM is TBD.
Assumptions in [3] has been approved to perform system simulation for UE EVM evaluation for FR2, and the reference simulation methodology is shown in [4].
Modulation Scheme for PDSCH | Required EVM
QPSK | [17.5 – 19] %
16QAM | [12.5 – 14]%
64QAM | [8 – 9]%
[256QAM] | [TBD]
EVM requirements for BS type 2-O carrier

## Slide 3: WF for assumptions for FR2
RAN4 will investigate the RF impairments.
Both system and link simulation should be considered to clarify the effectivity of 256QAM modulation.
  Investigate approperiate DM-RS patterns and PT-RS patterns needed
  Considering the following assumptions for evaluation
    Modulation: 256QAM, 64QAM
    EVM(256QAM): 3.5%. 4%, 4.5%, 5% , 5.5%, 6%
    EVM(64QAM): Agreed value
For system simulation, to evaluate BS Tx EVM by considering the following aspects.
  The simulation assumptions shall include urban macro scenario and indoor hotspot scenario in 38.803
    The assumptions agreed for UE [3] can be used as a reference for urban macro scenario

## Slide 4: WF for clarifying the general phase noise compensation level for FR2
Considering phase noise compensation on UE is needed to clarify the effectivity of 256QAM
Companies are encourage to provide views of the general ability of phase noise compensation on UE in next meeting.

## Slide 5
Reference
  [1] R4-1713558, Link Level Simulation Results for EVM FR2, Ericsson
  [2] R4-1713125, Evaluation on BS Tx EVM for mmWave, Huawei, HiSilicon
  [3] R4-1709666, Simulation assumptions on UE Tx EVM for mmWave, Huawei, HiSilicon
  [4] R4-1710493, Evaluation on UE Tx EVM for mmWave, Huawei, HiSilicon