## Slide 1: Summary of email discussion on UE feature list in RAN4
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #86 R4-1802139
Athens, Greece, 26 February – 2 March 2018
Agenda item: 7.1

## Slide 2: Background
ASN.1 for NSA will be frozen in Mar. 2018, the specification related to capability signaling should be finalized in RAN4 #86 and RAN2 #101 in Feb.
RAN2 needs time to implement the capability signaling in Feb. meeting. Hence, RAN4 needs decide type of capability described as below (R4-1712119) as soon as possible.
  Type 1: Layer-1 features relevant to RF characteristics
    They are reported per band (not per band combination).
  Type 2: Layer-1 features that influence baseband processing when UE is configured with NR CA/MR-DC/SUL
    They are reported in the baseband capability combination signaling.
  Type 3: Layer-1 features having both Type 1 and Type 2 characteristics (like the MIMO capability and the other LTE UE capabilities included per band in the band combination or per band combination)
    It is noted that for type-3 features RAN2 aims to follow the above agreements and working assumptions made for the MIMO capability.
  Type 4: Layer-1 features independent from the other features and not categorized into any of the above types
    In LTE, they are defined as physical layer parameters in TS 36.306. They are reported without linkage to band combination signalling.
To decide type of capability, RAN4 had email discussion from 2/1 - 2/9 as shown in the attachment
In this document, summary of the email discussion and possible way forward are provided
  Note that the items are re-ordered to improve visibility

## Slide 3: 1. 60kHz of subcarrier spacing for FR1
Summary:
  Type:
    Type 4: MediaTek, DOCOMO (if needed), Intel, Qualcomm
  Mandatory or optional
    Keep optional: Ericsson, Dish, ZTE, Qualcomm
    Mandatory without capability: Huawei
    Mandatory with capability: Vodafone
    Need capability if optional: Nokia, Sprint
  Other comments:
    If optional, all supported SCS by UE needs to be signaled per UE/per FR (Intel)
Proposal 1:
  Continue to discuss the followings during RAN4#86 for 60kHz of subcarrier spacing for FR1
    Option1: Keep optional, and Type 4 (per UE) signaling
    Option2: Mandatory without capability signaling for forward combability
    Option3: Mandatory with capability signaling, and Type 4 (per UE) signaling

## Slide 4: Capabilities for EN-DC/CA

## Slide 5: 2. Maximum channel bandwidth
Summary:
  Type:
    Type 1: MediaTek (given the number of CCs), DOCOMO (only FR2), Intel
    Type 2 (or 3?): Ericsson
    Unclear: Nokia, Sprint, Dish, Orange, LGE, intel
  Supported CBW needs to be signaled in FR1 for forward compatibility?
    Need: Sprint, Dish, Orange, Intel
    No need: DOCOMO, Nokia, Vodafone, OPPO, LGE, Ericsson
  Other comments:
    UE mandatory CBW for FR2
    CA related capability (CA bandwidth class, etc)
    Need to follow RAN agreements in RP-172832 (Intel)
Proposal 2:
  During RAN4 #86, continue to discuss overall EN-DC/NR CA capability framework including (aggregated) channel bandwidth, CA bandwidth class, supported SCS and non-contiguous intra-band CA frequency span, etc

## Slide 6: 5. Mixed numerologies for CA
Summary
  For inter-band CA:
    Mandatory: Nokia, Ericsson, Sprint, ZTE, DOCOMO, Dish, Orange, LGE(CA with FR1-FR2), (Huawei?)
    Type 2: MediaTek, intel?
    Type 3: Intel (both BB and RF capabilities)
    Optional (type is unclear): LGE(CA within FR1)
  For intra-band CA:
    Type 2: Huawei, intel?
    Type 3: Intel (both BB and RF capabilities)
    Type 4: DOCOMO, Ericsson, ZTE, Dish,
    Optional (type is unclear): Nokia, LGE
    Mandatory: Sprint
    Not support: MediaTek
  For EN-DC:
    Mandatory: Sprint
  Other comments:
    Separate capability between DL and UL (Huawei, Intel)
    overall NR CA capability framework is needed (Qualcomm)
Proposal 3:
  If a UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s), the UE shall support mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL with or without capability signaling
  FFS: other cases (e.g. inter-band NR CA only including FR1 (or FR2) bands, intra-band NR CA, EN-DC)

## Slide 7: 10. Non-contiguous intra-band CA frequency span
Summary
  Applicability:
    Only to FR2: MediaTek, Huawei, Intel, LGE, Qualcomm
  Capability granularity
    Combine CA bandwidth class: DOCOMO, Ericsson
    Type 1 : Qualcomm
    Type 4 : MediaTek (only FR2)
  Other comments
    UL intra-band non-contiguous CA not supported in Rel-15 and no capability signalling needed (Intel)
Proposal 4:
  Non-contiguous intra-band CA frequency span is applicable only to FR2
  Continue to discuss the followings during RAN#86
    Option1: Combine CA bandwidth class, i.e. no dedicated capability
    Option2: Type 1
    Option3: Type 4

## Slide 8: 4. Simultaneous reception and transmission for inter band CA or EN-DC (TDD-TDD or TDD-FDD)
Summary
  There would be two options:
    Option 1: Capability per band combination
      MediaTek, ZTE, Intel, LGE (TDD-TDD only),Qualcomm
    Option 2: This should be mandatory but exception is allowed in challenging band combination(s)
      Nokia, Ericsson, DOCOMO, Sprint, Huawei, Orange, Vodafone
    Option 3: Simultaneous reception and transmission is default only in exception band combination(s)
      OPPO
Proposal 5:
  For Simultaneous reception and transmission for inter band CA or EN-DC, continue to discuss the following options and related capability during RAN4 #86
    Option 1: Capability per band combination
    Option 2: Mandatory but exception is allowed in challenging band combination(s)
    Option 3: Simultaneous reception and transmission is default only in exception band combination(s)

## Slide 9: x. FDD-FDD intra-band LTE-NR DC
Summary
  RAN4 receive RAN2 LS on capability of intra-band FDD EN-DC (R2-1801633)
    RAN2 has discussed UE capability signalling on FDD-FDD intra-band LTE-NR DC. It was agreed that “In intra-band FDD EN-DC, a single capability bit is introduced to indicate if the UE supports asynchronous/synchronous operation.” at RAN2#100. However during the email discussion implementing the agreement into the specification and at RAN2 NR Ad-Hoc, companies raised the question whether this UE capability needs to be signalled per band combination (BC) or per UE signalling is sufficient.
    Q1: Should the UE capability indicating the support of FDD-FDD intra-band LTE-NR DC be per BC or per UE?
Proposal 6:
  For capability of FDD-FDD intra-band LTE-NR DC
    Option1: Per band combination
    Option2: Type 4 (per UE)

## Slide 10: Capabilities for RRM

## Slide 11: 3. Simultaneous reception of data and SS block with different numerologies
Summary:
  Type:
    Type 4 (per UE): MediaTek, DOCOMO (per FR), ZTE, Huawei (per FR), Intel (FR1 only), LGE, Ericsson
    Type 2: Huawei (Type 2 or 4)
    Type 1: Qualcomm (per FR)?
  Other comments:
    If capability is introduced, related RAN4 requirements are needed (Nokia)
    Scope of this feature should be clarified (Huawei, Intel, DOCOMO)
      Applicable only to intra-frequency only including both intra-cell and inter-cell SSB reception. It should not apply to inter-frequency case (Huawei)
      Applicable only to FR1 based on agreed WF R4-1801088 (Intel)
      Unclear for inter-band CA case (DOCOMO)
Proposal 7:
  Renamed to “Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement”
    FFS: inter-band CA case
  Type 4 (per UE) and applicable only to FR1
  RAN4 will discuss whether related requirement is introduced in Rel.15

## Slide 12: Capabilities for modulation order

## Slide 13: 12. 64QAM modulation for FR2 PDSCH
Summary
  Mandatory or Optional
    Mandatory without capability: MediaTek, DOCOMO, Nokia, ZTE, Huawei, CMCC, Orange, Vodafone, Ericsson, Qualcomm
    Optional: Intel (Type 1 for further FR2 extension to higher frequency bands)
  Other comments:
    If lower cost UE categories are defined, capability signaling can be discussed: Nokia
Proposal 8:
    64QAM for PDSCH is mandatory without capability at least for all FR2 bands defined within Rel.15 timeframe
    Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced

## Slide 14: 14. 64QAM for PUSCH
Summary
  Mandatory or Optional:
    Mandatory without capability: MediaTek, DOCOMO, Nokia, ZTE, Huawei, Dish (FR1), CMCC, Orange, Sprint, Vodafone, Ericsson,
    Optional: Intel, Qualcomm (per FR)
  Type:
    Type 4 for FR1 and Type 1 for FR2: Intel
    Per FR: Qualcomm
  Other comments:
    UE type needs to be clarified: OPPO
Proposal 9
  64QAM for PUSCH is mandatory without capability at least for all bands defined within Rel.15 timeframe
  Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced

## Slide 15: 15. 256QAM for PDSCH
Summary
  FR1
    Mandatory: MediaTek (or Type 4), DOCOMO, Huawei, Dish, CMCC, Orange, Sprint, Vodafone, Ericsson
    Type 1: Nokia, OPPO
    Type 4: Intel, LGE, Qualcomm, (ZTE?)
  FR2
    Type 1: MediaTek, Nokia, LGE
    Type 4: DOCOMO, (ZTE?)
    FFS: Intel, Ericsson, Qualcomm
    Subject to outcome of feasibility studies: Intel
  Other comments
    RAN1 specified 256QAM for PDSCH in a band agnostic manner. No capability for FR2 means that 256QAM is “mandatory without capability” for FR2 PDSCH (DOCOMO)
Proposal 10
  For FR1
    Option 1: 256QAM for PDSCH is optional and Type 4 (per UE) capability
    Option 2: 256QAM for PDSCH is mandatory without capability
    Option 3: 256QAM for PDSCH is mandatory with Type 4 (per UE) capability
  For FR2
    256QAM for PDSCH is optional
    Option 1: Type1 (per band)
    Option 2: Type4 (per UE)

## Slide 16: 16. 256QAM for PUSCH
Summary
  FR1:
    Type 1: MediaTek, Nokia, Huawei, Dish, Vodafone, OPPO, Intel, Qualcomm
    Mandatory: DOCOMO, CMCC, Orange, Sprint (or Type1)
    Optional: LGE
  FR2:
    Type 1: Nokia, Huawei, Dish, Qualcomm
    Type 3: MediaTek
    Type 4: DOCOMO
    FFS: OPPO, Intel
    Subject to outcome of feasibility studies: Intel
Proposal 11
  For FR1:
    Type 1 (per band) capability
      Option 1: 256QAM for PUSCH is mandatory with capability
      Option 2: 256QAM for PUSCH is optional
  For FR2:
    256QAM for PUSCH is optional
    Type 1 (per band) signaling

## Slide 17: 13. pi/2-BPSK for PUSCH
Summary
  Mandatory or Optional:
    Optional: ZTE, Huawei, Intel,
    No strong view: MediaTek, DOCOMO, Nokia,
  Type:
    Type 4: MediaTek (per FR), DOCOMO (per FR), Nokia(with/without FR1/2 differentiation), ZTE, Ericsson, Qualcomm (per FR), Intel (per FR)
    Type 1: Huawei
  Other comments:
    Split into 2 sub-features (Intel)
      1) Pulse-shaped pi/2 BPSK
      2) Non pulse-shaped pi/2 BPSK.
Proposal 12:
  pi/2-BPSK for PUSCH is optional
  Type 4 (per UE) with FR1/2 differentiation
  FFS: Split into 2 sub-features
    1) Pulse-shaped pi/2-BPSK
    2) Non pulse-shaped pi/2-BPSK.

## Slide 18: 18. pi/2-BPSK for PUCCH format 3/4
Summary
  Type
    Type 1: Huawei, Ericsson,
    Type 4: Nokia (w/ or w/o FR differentiation), Intel (per FR), DOCOMO (per FR), (ZTE?)
    Mandatory: MediaTek (for FR2), (ZTE?)
    Same as pi/2-BPSK for PUSCH: Qualcomm
Proposal 13:
  pi/2-BPSK for PUCCH format 3/4 is optional
  Type is same as pi/2-BPSK for PUSCH, i.e. Type 4 (per UE) with FR1/2 differentiation

## Slide 19: Other capabilities

## Slide 20: 21. Number of MIMO layers
Summary
  Type
    Type 3: MediaTek, DOCOMO
    Type 1: ZTE, Qualcomm
  Other comments
    RAN4 needs to discuss the following options in R4-1714257 (intel, DOCOMO)
      Option 1: Signal the number of MIMO layers per band per CA band combination for the combinations that have constraints
      Option 2: Signal the maximum number of MIMO layers per CA band combination for the combinations that have constraints
    This feature is duplicated to RAN1 feature list (Ericsson)
Additional comments from DOCOMO
  RAN1 already agreed the following rows in their list R1-1801289 (yellow parts are not agreed yet):
Proposal 14:
  Remove this feature from RAN4 feature list
 | 2-3 | PDSCH MIMO layers | 1. Maximal number of MIMO layers, candidate values: {1,2,4,8} | 2-1 |  |  | Type 3 |  |  |  |  |  |  | 
 | 2-14 | Codebook based PUSCH MIMO transmission | 1. Supported codebook based PUSCH MIMO with maximal number of supported layers | 2-13 |  |  | Type 3 |  |  |  |  |  | At least 1 layer is mandatory. Candidate value: {2, 4} | 
 | 2-15 | non-codebook based PUSCH transmission | 1. Maximal number of supported layers (non-codebook transmission scheme): [FFS: whether the above apply for “reciprocity based”] | 2-12 |  |  | Type 3 |  |  |  |  |  | Component-1 candidate values: {1, 2, 4} | 

## Slide 21: 6. Number of Rx/Tx ports
Summary
  Whether this capability is needed
    No need: MediaTek, DOCOMO, Ericsson, ZTE, Qualcomm
    Necessity is unclear : Nokia
    FFS: LGE
    Need: Huawei (Type1), Intel (Type is unclear)
Proposal 15:
  Clarify benefit to introduce this capability in addition to MIMO capability during RAN4 #86

## Slide 22: 9. BWP switching delay
Summary
  FFS: MediaTek, DOCOMO, ZTE, Huawei (maybe no need), Intel, Qualcomm
  Handled by minimum requirements: Nokia
  No need: LGE, Ericsson
Proposal 16:
  Continue to discuss necessity of this capability during RAN#86

## Slide 23: 17. Extended CP
Summary
  ECP can be configured only for UE that support 60kHz SCS
  Mandatory or Optional
    Mandatory without capability: Nokia, ZTE, Huawei, Orange, Vodafone, Ericsson
    Optional: MediaTek (Type 4 per FR), Intel (per FR), Qualcomm (Either normal or extended CP can be mandatory)
Proposal 17:
  Option1: ECP is mandatory without capability
  Option2: ECP is optional and Type 4 (per UE) with FR1/FR2 differentiation

## Slide 24: 19. Non-contiguous UL CP-OFDM
Summary
  Necessity
    Optional Type 1: MediaTek, Qualcomm
    Mandatory: Nokia, ZTE
    Optional but almost contiguous allocation is mandatory: DOCOMO
    No capability: intel
  Other comments:
    Mandatory and handled by minimum requirement, but capability for early UE is ok (Nokia).
    The following agreements were made in RAN4#AH1801 (DOCOMO)
      Almost contiguous signal is defined by setting minimum bandwidth for the signal (Lcrb > LCRBmax / A) and maximum number of puncture RB’s (Lcrb/B) within the almost contiguous signal.
        Companies are encouraged to provide proposal to A and B for the next RAN 4 meeting,
      Other methods to define almost contiguous are not precluded.
Proposal 18:
  Non-contiguous UL CP-OFDM is mandatory with Type 1 capability (per band)
  RAN4 will define minimum requirement to handle non-contiguous allocation for UL CP-OFDM in Rel.15

## Slide 25: 11. PA calibration gap
Summary:
  Necessity of this capability
    FFS: DOCOMO, Ericsson, ZTE, Huawei, Vodafone, LGE, Qualcomm
    Handled by minimum requirement: Nokia
    Agreed to introduce to FR2: Intel
  Applicability
    Only to FR2: MediaTek, Huawei, Intel
  Type:
    Type 4: MediaTek
Proposal 19:
  Continue to discuss detail/necessity of PA calibration gap during RAN4#86
  If there is no consensus in RAN4#86, this means that capability signaling is not introduced

## Slide 26: 20. 1-symbol GP for 120KHz SCS in unpaired spectrum
Summary
  Only for FR2
  Type
    Type 1: Qualcomm
    Type 4: MediaTek (or no need)
    No Need: Intel
  Other comments:
    Minimum requirement is needed if introduced (Nokia)
Additional comment from DOCOMO
  It seems that 1-symbol GP for 120kHz SCS is configurable from current RAN2 spec
    Ex. In tdd-UL-DL-configurationCommon in TS38.331, the following two parameters are defined:
    Therefore, if the slot preceding the first full UL slot is the same as the slot following the last full DL slot and for example nrofDownlinkSymbols = 1 and nrofUplinkSymbols =12, then 1-symbol GP can be configured
Proposal 20:
  Introduce UE capability for 1-symbol GP for 120KHz SCS in unpaired spectrum since it can be configured in the current RAN2 specification (e.g. tdd-UL-DL-configurationCommon in TS38.331)
    Option 1: Type 1 (per band)
    Option 2: Type 4 (per UE)
  RAN4 will discuss whether corresponding requirements are introduced in Rel.15 timeframe
-- Number of consecutive DL symbols in the beginning of the slot following the last full DL slot (as derived from nrofDownlinkSlots). -- Corresponds to L1 parameter 'number-of-DL-symbols-common' (see 38.211, section FFS_Section). nrofDownlinkSymbols INTEGER (0..maxSymbolIndex) -- Number of consecutive UL symbols in the end of the slot preceding the first full UL slot (as derived from nrofUplinkSlots). -- Corresponds to L1 parameter 'number-of-UL-symbols-common' (see 38.211, section FFS_Section) nrofUplinkSymbols INTEGER (0..maxSymbolIndex)

## Slide 27: 24. UE power class
Summary
  signaling framework
    Similar to E-UTRA (only indication of non-default PC): Nokia, Ericsson, Sprint, Dish, CMCC, OPPO, Intel (FR1)
    Capability signaling needed for power classes of new UE type: LGE
  Other comments:
    How to mandate Power Class 2 UE in certain regions is FFS (CMCC)
    Need to be able to support multiple PCs (handheld, fixed wireless access, transportable wireless access) for FR2 (Intel)
    Definition under inter-band CA and EN-DC (MediaTek, DOCOMO, Sprint)
Proposal 21:
  Introduce capability signaling of non-default UE power class, and Type 1 (per band) signaling
    FFS: Default power class(es) for FR2
  FFS: Definition under inter-band NR CA and EN-DC

## Slide 28: Capabilities for LTE/NR coexistence

## Slide 29: 22. 7.5kHz UL raster shift
Summary
  This is only for FR1
  Type
    Type 1: ZTE, Qualcomm
    Type 4: MediaTek
    Mandatory for UEs supporting SUL band(s): Nokia, Huawei, Orange, Vodafone, LGE, Ericsson
  Other comments:
    Should be clarified that this shall not be required for new NR spectrum SUL bands (Dish)
Proposal 22:
  Continue to discuss the following options during RAN4#86
    Option1: Type1 (per band)
    Option2: Type4 (per UE)
    Option3: Mandatory for UEs supporting SUL band(s)

## Slide 30: 8. “Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective”
Summary
  Type of “switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective” capability
    Type 4: MediaTek, LGE
    Per band combination: Intel
Proposal 23:
  For “Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective”,
    Option 1: Type 4
    Option 2: Per band combination

## Slide 31: 8. “Support of UL sharing from UE perspective”
Summary
  Necessity of “Support of UL sharing from UE perspective” capability
    Need: Nokia, ZTE, Qualcomm
    No need: Huawei, LGE
Proposal 24:
  For capability of “Support of UL sharing from UE perspective”
    Option 1: Need (Type is FFS)
    Option 2: No need

## Slide 32: 23. Supplemental uplink related features
Summary
  Capability for “Supplemental uplink”
    Type 3: MediaTek
  Capability for “Supplemental uplink with different numerology”
    Type 2: MediaTek
  Capability for “Supplemental uplink with different numerology”
    Type 4: MediaTek
  Other comments
    Above features should be merged (Huawei)
    Consider SUL without UL sharing (Dish, ZTE, Nokia)
Proposal 25
  Continues discussion on capability for each features during RAN4 #86