## Slide 1: WF on UE RF for subPRB R15 feature
Ericsson
3GPP TSG-RAN4 Meeting #86
Athens, Greece, 26th Feb – 2nd March 2018
R4-1802546

## Slide 2: Proposals
MPR, A-MPR and IBE will be impacted for UE RF spec (36.101)
Companies are encouraged to submit MPR simulation result for CAT-M1 and CAT-M2 for subPRB allocation in RAN4#86bis
  system bandwidth (1,4MHz, 3MHz, 5MHz, 10MHz, 15MHz, 20MHz)
  Modulation( QPSK, 16QAM, 64QAM)
Companies are encouraged to submit A-MPR simulation result for CAT-M1 and CAT-M2 for subPRB allocation at RAN4#86bis for the current NS value in table Table 6.2.4E-1 and Table 6.2.4E-2 in 36.101 R15.1.0
IBE requirement need to be specified for the non-allocated tones for subPRB allocation PRB
  Reuse the legacy CAT-M1/M2 IBE image and LO requirement
  Specify new general IBE mask
    One possible format :
      Granularity of the requirement to be defined
      Slope slew rate for IBE mask to be defined

## Slide 3: Proposals
Simulation assumption of MPR, A-MPR for CAT-M1,M2 UE
  PA calibrated in the same way MPR/A-MPR derived for CAT-M1/M2 device together with other parameter setting:
    Counter-IM3 : 60 dB,
    IQ image : -25 dB
    LO leakage of -25 dBc
  Resource granularity within 1 PRB
    Continuous # of tones: 2, 3, 6
  Modulation:
    BPSK (2 tone)
    QPSK (3 and 6 tone)
  Start position of the continuous subPRB allocation
    Wait RAN1 agreement
  DMRS design and Phase rotation
    Wait RAN1 agreement
  PC
    PC3