## Slide 1: WF on NR TDD UL/DL configurations and HPUE behavior
vivo, CMCC, OPPO,
3GPP TSG-RAN WG4#86 Meeting R4-1802714
Athens, Greece, 26th Feb– 2nd Mar, 2018

## Slide 2: Background
The TDD UL/DL configuration problem was raised in RAN4#AH 1801 and a way forward was approved in R4-1801125
More papers were submitted in RAN4#86.

## Slide 3: Way Forward
Setting appropriate UL duty cycle is a potential solution to satisfy SAR requirements for HPUE.
  Possible options are included in Annex.
Other solutions are not precluded.
More analysis are encouraged in next meeting.

## Slide 4: Annex (1)
Option 1:
  Network configuration should satisfy: Less than 50% symbols were used as UL during a predefined evaluation period to ensure UE could operate in power class higher than default. Otherwise, UE is allowed to do power back off using P-MPR which is up to UE implementation
    An evaluation period of [X] ms or [Y] symbols in which the number could be discussed further
    The flexible symbols can be categorized to UL/DL/Gap considering statistical approach and/or other factors, the details are FFS

## Slide 5: Annex (2)
Option 2:
  Restrict the slot formats to those who satisfy 50% duty cycle restriction.
  If the TDD format is outside of the restricted set of TDD formats, the UE must still operate as HPUE, but may take P-MPR autonomously according to its implementation.