## Slide 1: Way forward on eFeMTC RRM requirements under CRS muting
Ericsson
3GPP TSG-RAN WG4 Meeting #86 R4-1802810
Athens, Greece, 26 February – 2 Mars, 2018
Agenda Item: 6.19.4.2

## Slide 2: Proposals for CRS muting
Initial cell acquisition
  CRS transmissions are switched on over full BW in 1 DL subframe every 10 ms and CRS muting information (such as frequency, location, timing etc.), which is optional for the UE to use, is also communicated to the UE.
Muted CRS BW for category M2
  For category M2 UEs, CRS transmissions in the center frequency and corresponding UE timing requirements are defined as in Table 2.

## Slide 3: Proposals on high-velocity support for efeMTC
On intra-frequency DRX requirements
  The DRX measurement requirements are relaxed by a factor of 2 for shorter DRX cycle length and they are kept unchanged for the longest DRX cycle lengths compared to the current high-speed DRX cycle measurement requirements.
On gap-sharing allocation
  Introduce a new measurement gap sharing table for eFeMTC UEs operating under high-velocity.
On information about high-velocity operation
  Reuse the existing highSpeedEnhancedMeasFlag indicator for eFeMTC UEs, and if this flag is signaled, the UE shall use the measurement gap allocation table associated with this flag and carry out measurements accordingly.