## Slide 1: Way forward on NR Idle and Inactive Mode and Mobility for SA
3GPP TSG-RAN WG4 #86 R4-1803019
Athens, Greece, February 26th – March 2nd, 2018
Agenda item: 7.9.5
Nokia, Nokia Shanghai Bell, …

## Slide 2: NR Idle and Inactive Mode and Mobility for SA
Define requirements for NR RRC_IDLE state mobility
  Cell selection
  Idle Mode mobility
  Evaluation of cell reselection criteria
  Maximum interruption in paging reception
Further details on page 3 - 7.

## Slide 3: NR Idle and Inactive Mode and Mobility for SA
Cell selection
  Already concluded by RAN4
UE measurement capability
  number of NR inter-frequency carriers: [7]
  number of E-UTRAN Inter-RAT carriers:
    FDD [7],
    TDD [7]
  Total number of carriers: [13]
Measurements and evaluation of serving cell:
  Measurements:
    SS-RSRP,
    SS-RSRQ
  Measurement averaging:
    number of samples: [2],
    sample window: (MAX[DRX, SMTC]/2)

## Slide 4: NR Idle and Inactive Mode and Mobility for SA
Measurements of intra-frequency NR cells
  Measurements:
    SS-RSRP,
    SS-RSRQ
  Measurement averaging:
    number of samples: [2],
    sample window: [MAX[DRX, SMTC]/2]
  Cell detection time (Tdetect,NR_Intra): [TBD]*Max[DRX, SMTC]
  Measurement interval (Tmeasure,NR_Intra): [TBD]*Max[DRX, SMTC]
  Cell evaluation time (Tevaluate,NR_intra): [TBD]*Max[DRX, SMTC]

## Slide 5: NR Idle and Inactive Mode and Mobility for SA
Measurements of inter-frequency NR cells
  Measurements:
    SS-RSRP,
    SS-RSRQ
  Measurement averaging:
    number of samples: [2],
    sample window: [MAX[DRX, SMTC]/2]
  Measurements of inter-frequency NR cells
    Cell detection time (Tdetect,NR_Inter): [TBD]*Max[DRX, SMTC]
    Measurement interval (Tmeasure,NR_Inter): [TBD]*Max[DRX, SMTC]
    Cell evaluation time (Tevaluate,NR_inter): [TBD]*Max[DRX, SMTC]

## Slide 6: NR Idle and Inactive Mode and Mobility for SA
Measurements of inter-RAT E-UTRAN cells
  Measurements:
    SS-RSRP,
    SS-RSRQ
  Measurement averaging:
    number of samples: [2],
    sample window: [MAX[DRX, SMTC]/2]
  Measurements of inter-frequency NR cells
    Cell detection delay (Tdetect,EUTRAN_Inter): [TBD]*Max[DRX, SMTC]
    Measurement interval (Tmeasure,EUTRAN_Inter): [TBD]*Max[DRX, SMTC]
    Cell evaluation time (Tevaluate,E-UTRAN_inter): [TBD]*Max[DRX, SMTC]

## Slide 7: NR Idle and Inactive Mode and Mobility for SA
Evaluation of cell reselection criteria
  Define UE cell reselection criteria requirements. Both intra-frequency, inter-frequency and inter-RAT evaluation.
Maximum interruption in paging reception
  Define UE requirements related to maximum interruption time in paging reception in connection with cell reselection.