## Slide 1: Way forward on demodulation and CSI requirements for high capacity stationary wireless link and 1024QAM
Huawei, HiSilicon,
3GPP TSG-RAN WG4 Meeting #86 R4-1803106
Athens, Greece, February 26 – March 2, 2018
Agenda Item: 6.20.4

## Slide 2: Background
RAN1 progresses and impacts on UE implementation:
RAN1 progresses | Impact on UE implementation
New 1024QAM constellation | New demodulation scheme for 1024QAM
New additional CQI/MCS/TBS tables: 1024QAM capable UE needs to support this new ones as well as the legacy tables, which is configurable | New CSI reporting and link adaptation scheme in addition to the legacy schemes
New UE category which uses 1024QAM to reach peak data rate | Larger soft buffer and improved Rx EVM at UE side
New entries to support OCC4 for rank 3 and 4 transmission | Demodulation performance on new DMRS port combinations for 3/4-layer MIMO

## Slide 3: Test purposes
Demodulation performance requirements
  To verify the demodulation performance using 1024QAM reference channel under the fading channels;
  To verify the support of peak data rate for the new UE categories, i.e., by defining sustained data rate tests.
  To verify the functionality and performance for reduced DMRS ports.
CSI reporting requirement
  To verify the link adaptation performance following the new CQI/MCS/TBS tables, e.g., CQI definition test.

## Slide 4: Demodulation requirements under fading conditions
Test parameters | 
Transmission Mode | TM4, TM9
Antenna configurations | 4 x 2 low, FFS 4 x 4 low [1]
Tx EVM | Option 1: 2% Option 2: 1.5% RAN4 should consider the feasibility of test equipment
MCS | TBD, coding rate < 0.85, based on RAN1 new MCS table (select lower MCS for 1024QAM)
MIMO layer | 2-layer (FSS 1-layer optional)
Propagation condition | EPA5
Bandwidth | 10MHz for FDD and TDD
Reference receiver | LMMSE or MMSE-IRC
Note[1]: Ensure 4Rx UE performance can be verified

## Slide 5: SDR test
Common parameters
  TM3
  2 x 2 (for 2-layer transmission per CC, and 4 x 4 (for 4-layer transmission per CC)
    For 4x4, the definition of 1024QAM capable UE category should be considered (to address the concern on high SNR, the MCS can be further study)
  CFI=1
Tx EVM assumption :
  Option 1: 2%
  Option 2: 1.5%
  RAN4 should consider the feasibility of test equipment
85% throughput
Companies to provide input on per-CC MCS selection for
  Rank 2 and rank 4
  Different bandwidth
    10MHz, 15MHz, 20MHz

## Slide 6: DMRS overhead reduction
Table 1. DM-RS table for OCC4 DM-RS support for rank 3/4 SU-MIMO transmission.
New DMRS entries
16QAM, EVA5, 4-layer, FRC test case number TBD

## Slide 7: CQI test
Definition test:
Option 1: Minimum requirement PUCCH 1-0 (Cell-Specific Reference Symbols): CRS based TM single codeword with TM1 under static channel in Annex B.1
  Bandwidth:
    FDD: 10MHz
    TDD: 20MHz
Option 2: Minimum requirement PUCCH 1-1 (Cell-Specific Reference Symbols): CRS based TM dual codeword with TM4 under static channel in Annex B.1
  Bandwidth
    FDD: 10MHz
    TDD: 20MHz
FFS: frequency selective test for TM9