## Slide 1: WF on UE feature list for CA/EN-DC, other capability and LTE-NR co-existence
Intel Corporation
3GPP TSG-RAN WG4 Meeting 86 Athens, Greece, 26 February – 2 March 2018 Agenda Item: 7.1
R4-1803279

## Slide 2: Capabilities for EN-DC/CA

## Slide 3: EN-DC/NR CA capabilities
  RAN4 #86 online agreements
During RAN4 #86, continue to discuss overall EN-DC/NR CA capability framework including (aggregated) channel bandwidth, CA bandwidth class, supported SCS and non-contiguous intra-band CA frequency span, etc
The capability of supporting SCS within the single carrier in the CA configuration will be signalled separately, i.e., there is no need to mandatory UE to support mixed numerologies in CA case.
  If a UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s), the UE shall support two mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL with or without capability signalling
  Capability signalling for CA case can be further discussed.
Non-contiguous intra-band CA frequency span is applicable only to FR2 (FFS for whether applicable for downlink only or both downlink and uplink)
  Continue to discuss the followings during RAN#86
    Option1: Combine CA bandwidth class, i.e. no dedicated capability
    Option2: Type 1
For Simultaneous reception and transmission for inter band CA or EN-DC, the capability signalling is per band combination. Whether to mandating this feature in certain band combinations will FFS.
The capability of asynchronous FDD-FDD intra-band LTE-NR DC is per band combination

## Slide 4: Maximum Channel BW
  Background:
    UE capability signalling agreed in RP-172832 (Per-band capability signalling, separately for DL and UL and for each SCS)
    For FR1, all the bandwidths listed in TS38.101-1 v15.0.0 Table 5.3.5-1 for each band shall be mandatory with a single CC
    For FR2, the set of mandatory CBW is under discussion
  Offline discussion summary
    Conclusion: Confirm feature list description
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
    Feature description
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-1 | Maximum channel bandwidth supported in each band for DL and UL separately and for each SCS that UE supports with a single CC | 1) FR1 channel bandwidths in TS38.101-1 Table 5.3.5-1 2) FR2 channel bandwidths in TS38.101-2 Table 5.3.5-1 |  | Yes | For FR1, all the bandwidths listed in TS38.101-1 v15.0.0 Table 5.3.5-1 for each band shall be mandatory with a single CC For FR2, UE does not support some UE channel bandwidths | Type 1 | No Need | No Need |  | UE capability signalling shall follow RP-172832 (Per-band capability signalling, separately for DL and UL and for each SCS) For FR1, all the bandwidths listed in TS38.101-1 v15.0.0 Table 5.3.5-1 for each band shall be mandatory with a single CC For FR2, the set of mandatory CBW is FFS Overall EN-DC/NR CA capability framework will be discussed in RAN4 #86 | RAN2/4 RAN4 | NA Optional | 

## Slide 5: Mixed numerologies for CA (1)
  Background:
    RAN4 AH 1801 agreements
    Same numerology for intra-band NR CA including both continuous and non-continuous is mandatory support for Rel15
    RAN4 86 agreements
    The capability of supporting SCS within the single carrier in the CA configuration will be signalled separately, i.e., there is no need to mandatory UE to support mixed numerologies in CA case.
      If a UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s), the UE shall support two mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL with or without capability signalling
      Capability signalling for CA case can be further discussed.
    RAN1 feature list
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
0-9 | Subcarrier spacings and FFT size in conjunction with supportable BW with normal CP | 1) 15kHz 2) 30 kHz 3) 60 kHz 4) 120 kHz |  | Yes |  | Type 4 [Type 3] RAN4 to decide | RAN4 to decide | RAN4 to decide |  | It is up to RAN4 decision Baseband processing (memory) in CA combination related as well as RF (SCS support is per band between sub6 and mmWave) | RAN4 |  | 

## Slide 6: Mixed numerologies for CA (2)
  Offline discussion summary (green text marks conclusions)
  Q1: Whether to merge RAN1 feature 0-9 and RAN4 feature 2-2?
    Option 1: Keep a single feature
    Option 2: Keep separate features
    Conclusion: No consensus. Some companies observed that features are duplicated.
  Q2: Baseband UE capabilities signalling
    Option 1: Signal supported SCS per CC in BPC entry
    Conclusion: Signal supported SCS per CC in BPC entry (UE can signal different SCS combinations)
  Q3: RF capabilities signalling
    Option 1: Signal support of mixed numerologies operation per-BC
    Option 2: No RF capabilities signalling
    Conclusion: Signalling details are unclear (e.g. for BCs involving inter-band + intra-band). Proponents need to provide more details
  Q4: Feature description (changes in red)
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-2 | Mixed numerologies for CA | 1) Support simultaneous reception or transmission with different numerologies in CA |  | Yes | UE does not support simultaneous reception or transmission with different numerologies in CA | [Type 3] | No | No |  | If a UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s), the UE shall support two mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL with or without capability signaling | RAN4 | Optional | 

## Slide 7: Mixed numerologies for CA (3)
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
  Signal supported SCS per CC in BPC entry (UE can signal different SCS combinations)
  Do not define RF capabilities signalling
  Feature description
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-2 | Mixed numerologies for CA | 1) Support simultaneous reception or transmission with different numerologies in CA |  | Yes | UE does not support simultaneous reception or transmission with different numerologies in CA | Type 2 | No | No |  | UE capability signalling: Signal supported SCS per CC in BPC entry If a UE supports inter-band NR CA including both FR1 band(s) and FR2 band(s), the UE shall support two mixed numerologies between FR1 band(s) and FR2 band(s) in DL and UL with or without capability signaling | RAN4 | Optional | 

## Slide 8: Non-contiguous intra-band CA frequency span
  Background: RAN4 86 agreements
  Non-contiguous intra-band CA frequency span is applicable only to FR2 (FFS for whether applicable for downlink only or both downlink and uplink)
  Continue to discuss the followings during RAN#86
    Option1: Combine CA bandwidth class, i.e. no dedicated capability
    Option2: Type 1
  Offline discussion summary (green text marks conclusions)
  Conclusion: Capture UE RF session agreements
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
  UE capability signalling shall follow UE RF session agreements in [R4-1803251]
    UE signals the Frequency separation classes with per band granularity (Type 1)
    Separate Frequency separation classes can be signaled for DL and UL
  Feature description
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-3 | Non-contiguous intra-band CA frequency span for FR2 | Support of non-contiguous intra-band CA in FR2 with frequency span |  | Yes | UE does not support non-contiguous intra-band CA for FR2 frequency span | Option 1: Combine with CA BW class Option 2: Type 1 | No need | Applicable only to FR2 |  | UE signals the Frequency separation classes with per band granularity (Type 1) based on [R4-1803251] Separate Frequency separation classes can be signalled for DL and UL FFS for whether applicable for downlink only or both downlink and uplink | RAN4 | Optional | 

## Slide 9: Simultaneous reception and transmission for inter-band CA or EN-DC (TDD-TDD or TDD-FDD)
  Background: RAN4 86 agreements
  For Simultaneous reception and transmission for inter-band CA or EN-DC, the capability signalling is per band combination. Whether to mandating this feature in certain band combinations will FFS
  Offline discussion summary (green text marks conclusions)
    Q1: Whether to mandate this feature in certain band combinations
      Option 1: Further discuss whether to mandate feature in certain band combinations in RAN4 86bis
      Option 2: Do not mandate
      Conclusion: no conclusion. Keep original agreements (“Whether to mandating this feature in certain band combinations will FFS”)
    Q2: Feature description (changes in red)
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-4 | Simultaneous reception and transmission for inter-band CA or EN-DC (TDD-TDD or TDD-FDD) | 1) Simultaneous reception and transmission for inter-band CA or EN-DC (TDD-TDD or TDD-FDD) |  | Yes | UE does not support simultaneous reception and transmission for inter-band CA or EN-DC (TDD-TDD or TDD-FDD) | Type 3 Per band combination | No Need | No Need |  | Per band combination UE capability signalling granularity For Simultaneous reception and transmission for inter band CA or EN-DC, the capability signalling is per band combination. Whether to mandating this feature in certain band combinations will FFS | RAN4 | Optional | 

## Slide 10: Simultaneous reception and transmission for inter-band CA or EN-DC (TDD-TDD or TDD-FDD)
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
    Further discuss in RAN4 86bis whether to mandate this feature in certain band combinations
    Capabilities signalling
      Option 1: Same signalling for EN-DC and NR CA
      Option 2: Separate signalling for EN-DC and NR CA
    Feature description
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-4 | Simultaneous reception and transmission for inter-band CA or EN-DC (TDD-TDD or TDD-FDD) | 1) Simultaneous reception and transmission for inter-band CA or EN-DC (TDD-TDD or TDD-FDD) |  | Yes | UE does not support simultaneous reception and transmission for inter-band CA or EN-DC (TDD-TDD or TDD-FDD) | Type 3 Per band combination | No Need | No Need |  | Per band combination UE capability signalling granularity (Type 3) Whether to mandate this feature in certain band combinations is FFS | RAN4 | Optional | 

## Slide 11: Asynchronous FDD-FDD intra-band LTE-NR DC
  RAN4 86 agreements
  The capability of asynchronous FDD-FDD intra-band LTE-NR DC is per band combination
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
  Feature description
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-5 | Asynchronous FDD-FDD intra-band LTE-NR DC | Asynchronous FDD-FDD intra-band LTE-NR DC |  | Yes | UE does not support asynchronous FDD-FDD intra-band LTE-NR DC | Type 3 (Per band combination) | Applicable only to FDD | Applicable only to FR1 |  | Per band combination UE capability signalling granularity (Type 3) | RAN4 | Optional | 

## Slide 12: Other capabilities

## Slide 13: Background
  RAN4 86 agreements
    For 60Khz SCS, it is agreed to introduce capability signalling per UE for FR1. Further discussion on the mandatory or optional in this week is needed.
    Remove number of MIMO layers from RAN4 feature list
    No capability signalling for number of Rx/Tx ports. We can revisit the need of capability signalling of number of Tx ports when we discuss the number of MIMO layers in this week.
    Continue to discuss necessity of the capability of BWP switching delay during RAN#86
    Capability signaling for ECP will be Type 4 (per UE) if we introduce the capability signalling. FFS for wehther ECP is mandatory or optional. FFS for whether we need this feature for FR2 pending on the further check from operators in this week.
    Postpone the non-continuous CP-OFDM for uplink feature to June 2018.
    RAN4 can inform the Type 4 (per UE) capability for the feature of PA calibration gap in RAN4 #86 meeting (detailed wording of information can be discussed). RAN4 will further discuss the UE capability in the future. We can revisit the need of calibration gap once RAN4 reach consensus.
    Introduce capability signaling of [non-default] UE power class, and Type 1 (per band) signaling
      FFS: Default power class(es) for FR2. ( different UE device types may have different default power class)
      FFS: Definition under inter-band NR CA and EN-DC
      RAN4 will further discuss the mandatory of PC2 for FR1 in certain region.

## Slide 14: 60kHz of subcarrier spacing for FR1
  Background: RAN4 86 agreements
    For 60Khz SCS, it is agreed to introduce capability signalling per UE for FR1. Further discussion on the mandatory or optional in this week is needed.
  Offline discussion summary (green text marks conclusions)
    Q1: Whether 60Khz SCS for FR1 is mandatory/optional
      Conclusion: no consensus.
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
    Per UE capability signalling granularity
    Applicable to FR1 only
    Feature description
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-1 | 60kHz of subcarrier spacing for FR1 | 1) 60kHz subcarrier spacing for data channel in FR1 |  | Yes | UE does not support 60kHz of subcarrier spacing for data channel | Type 4 | No Need | Applicable only to FR1 |  |  | RAN4 | TBD | 

## Slide 15: Extended CP
  Background:
    RAN4 86 agreements: Capability signaling for ECP will be Type 4 (per UE) if we introduce the capability signalling. FFS for whether ECP is mandatory or optional. FFS for whether we need this feature for FR2 pending on the further check from operators in this week.
    RAN1 agreements: Optional with capability signalling
  Offline discussion summary (green text marks conclusions)
  Conclusion: Follow RAN1 decision. Keep the feature in the RAN1 feature list. “Extended CP” can be removed from the RAN4 UE feature list
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
  Keep the feature in the RAN1 feature list. Remove “Extended CP” from the RAN4 UE feature list.
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-2 | Extended CP | 1) Extended CP | Only for UE that supports 60kNHz SCS | Yes | UE does not support extended CP | Type 4 if needed | No need | TBD |  |  | RAN4 | TBD | 

## Slide 16: PA Calibration Gap (1)
  Background:
    RAN4 AH 1801 agreements
      The need for UE calibration gap is a UE capability
        The capability definition is per UE as a baseline assumption
        Companies are encouraged to provide additional analysis whether a per-band definition is needed or if the baseline assumption can be confirmed next meeting
    RAN4 86 agreements
      RAN4 can inform the Type 4 (per UE) capability for the feature of PA calibration gap in RAN4 #86 meeting (detailed wording of information can be discussed). RAN4 will further discuss the UE capability in the future. We can revisit the need of calibration gap once RAN4 reach consensus.
  Offline discussion summary (green text marks conclusions)
    Q1: Capabilities signalling
      Introduce Type 4 (per UE) UE capability signaling of PA Calibration gap (PCG)
      Option 1: Signal whether UE supports PCG
      Option 2: Signal the supported PCG Type (up to X= 4 types)
    Q2: Feature description (changes in red)
    Conclusion: continue discussion in the main session
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-7 | PA calibration gap | 1) Support of PA calibration gap to implement digital pre-distortion techniques |  | Yes | UE does not support PA calibration gap | Type 4 | No Need | Applicable only to FR2 |  | RAN4 will further discuss the UE capability in the future. Can revisit the need of calibration gap once RAN4 reach consensus. | RAN4 | Optional | 

## Slide 17: PA Calibration Gap (2)
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
    Introduce Type 4 (per UE) UE capability signaling of PA Calibration gap (PCG)
      1 bit indication to inform NW whether UE supports PCG
    Feature description
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-7 | PA calibration gap | 1) Support of PA calibration gap to implement PA digital pre-distortion techniques |  | Yes | UE does not support PA calibration gap | Type 4 | No Need | Applicable only to FR2 |  | RAN4 will further discuss the UE capability in the future. Can revisit the need of calibration gap once RAN4 reach consensus. | RAN4 | Optional | 

## Slide 18: Non-contiguous UL CP-OFDM
  Background: RAN4 86 agreements
    Postpone the non-continuous CP-OFDM for uplink feature to June 2018. .
  Offline discussion summary (green text marks conclusions)
  Q1: Whether to keep in feature list
    Option 1: Remove “Non-contiguous UL CP-OFDM” from the UE feature list
    Option 2: Keep “Non-contiguous UL CP-OFDM” from the UE feature list (how to fill in all fields?)
    Conclusion: no decision. Continue offline discussion
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
    Option 1: Remove feature from the list. Do not introduce requirements and capability signalling in Rel15
    Option 2: Rename feature to “Almost contiguous UL CP-OFDM”. Optional feature. Introduce Type 4 signalling with per-FR1/FR2 differentiation
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-6 | Non-contiguous UL CP-OFDM |  |  |  |  |  |  |  |  | Postpone the non-continuous CP-OFDM for uplink feature to June 2018. | RAN4 |  | 
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-6 | Almost contiguous UL CP-OFDM | 1) Support of almost contiguous UL CP-OFDM transmissions |  | Yes | UE cannot support almost contiguous UL CP-OFDM transmissions | Type 4 | No | Yes |  |  | RAN4 | Optional | 

## Slide 19: UE Power Class (1)
  Background: RAN4 86 agreements
    Introduce capability signaling of [non-default] UE power class, and Type 1 (per band) signaling
      FFS: Default power class(es) for FR2. ( different UE device types may have different default power class)
      FFS: Definition under inter-band NR CA and EN-DC
      RAN4 will further discuss the mandatory of PC2 for FR1 in certain region.
  Offline discussion summary (green text marks conclusions)
  Q1: FFS whether to keep UE PC in the UE feature list
    Option 1: Remove UE power class from the UE feature list
    Option 2: Keep UE power class from the UE feature list
    Conclusion: no decision
  Q2: UE capability signalling
    Option 1: Type 1
    Option 2: Type 3 (per band combination)
    Conclusion: further discuss offline if Type 3 is needed
  Q3: Whether signalling provided for non-default power class
    FR1: Signaling provided for non-default UE power class only
    FR2:
      Option 1: Signaling provided for UE power class
      Option 2: Signaling provided for non-default UE power class (FFS how NW knows the default PC for certain device type)
    Conclusion: no decision. Continue offline discussion
  Q3: Default power class for FR2
    Option 1: Define default power class for different UE device types for FR2
    Option 2: Do not define default power class for different UE device types for FR2
    Conclusion: no decision. Continue offline discussion

## Slide 20: UE Power Class (2)
  Proposal (note: agreed aspects in offline are marked green, non-agreed in offline are marked in red)
    Capability signalling
      Introduce Type 1 (per band) signaling of UE power class
        FR1: Signaling provided for non-default UE power class only
        FR2:
          Option 1: Signaling provided for UE power class
          Option 2: Signaling provided for non-default UE power class
      FFS whether to introduce per band combination signalling of UE PC
      FFS whether to split signalling for FR1 PC and FR2 PC.
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
2-8 | UE power class | 1) Support of [non-default] UE power class |  | Yes | UE does not support UE power class | Type 1, [Type 3] | No Need | No Need |  | TBA | RAN4 | TBD | 

## Slide 21: Capabilities for LTE/NR coexistence

## Slide 22: Background
RAN4 86 agreements
  7.5kHz UL raster shift is mandatory in the SUL bands with uplink sharing either from UE perspective or from network perspective
  Further discussion on supporting 7.5kHz UL raster shift for LTE-NR co-existence for Band n2, n5 and n66.
  It is common understanding that some UE support UL sharing from UE perspective and some UE does not support UL sharing from UE perspective, UE need to indicate the supports to the network. For UE supporting UL sharing from UE perspective, the capability signaling type for “Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective” shall be per band combination
  Continue discuss on the feature 1-14, 1-15 and 1-16 in this meeting.

## Slide 23: 7.5kHz UL raster shift
RAN4 86 agreements
  7.5kHz UL raster shift is mandatory in the SUL bands with uplink sharing either from UE perspective or from network perspective
  Further discussion on supporting 7.5kHz UL raster shift for LTE-NR co-existence for Band n2, n5 and n66.
  Proposal
    Option 1: 7.5kHz UL raster shift is mandatory for LTE-NR co-existence for Bands n2, n5 and n66
    Option 2: Introduce Type 1 capability signalling for 7.5 kHz UL raster shift.
      Further discuss the set of mandatory bands (i.e. mandatory with capability signalling)
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-13 | 7.5kHz UL raster shift | 1) 7.5kHz UL raster shift | [1-11] | Yes | UE does not support 7.5kHz UL raster shift | [NA or Type 1] | N/A | Applicable to FR1 only |  |  | RAN4 | Mandatory in the SUL bands with uplink sharing either from UE perspective or from network perspective FFS: band n2, n5, n66 | 

## Slide 24: Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective
  Proposal
  FFS whether to keep the feature
    Option 1: Keep feature
    Option 2: Remove feature and postpone to Jun 2018
  UE Capability signalling (if feature is kept)
    Option 1: Type 3 (per BC)
    Option 2: Type 4 (per UE)
  UE Capability signalling elements
    Capability 1: ~0us switching type
    Capability 2: <20us switching type
  FFS whether signalling of “switching time” implies that UE supports UL sharing from UE perspective
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-12 | Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective | 1) ~0us 2) <20us | 1-11 | Yes | UE does not support UL subcarrier alignment between LTE and NR for EN-DC with LTE-NR coexistence in UL | Type 3 | No Need | Applicable only to FR1 |  | Per band combination signalling (Type 3) | RAN4 | TBD | 

## Slide 25: Support of UL sharing from UE perspective
  Proposal
  FFS whether to keep the feature
    Option 1: Keep feature
    Option 2: Remove feature and postpone to Jun 2018
  UE Capability signalling (if feature is kept)
    Option 1: Type 3 (per BC)
# | Feature group | Components | Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-11 | Support of UL sharing from UE perspective | 1) Support of UL sharing from UE perspective |  | Yes | UE does not support UL sharing from UE perspective | TBD | No Need | Applicable only to FR1 |  |  | RAN4 | Optional | 

## Slide 26: Supplemental uplink features
  RAN1 feature list
  Proposal
  Postpone discussion till RAN1 reaches further agreements
Prerequisite feature groups | Need for gNB to know | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
6-15 | Yes | UE will not be able to perform the RACH/PUSCH/PUCCH/SRS operation in a band combination including SUL | Type 2 or 4 |  |  |  | This is conditioned on the support of SUL band combination(s). The band combination definition is up to RAN4. |  |  | 
6-16? | Yes | The UE will not be able to access or operate on a SUL carrier | Type 2 or 4 | Need Support not required for an FDD-only UE |  |  | This is conditioned on the support of SUL band combination(s). The band combination definition is up to RAN4. |  |  | 
6-16, 6-17? | Yes |  | Type 2 or 4 | Need Support not required for an FDD-only UE |  |  | This is conditioned on the support of SUL band combination(s). The band combination definition is up to RAN4. |  |  |