## Slide 1: 3GPP TSG-RAN WG4 Meeting # 86 Athens, Greece, 26 Feb-2 Mar, 2018
T-Mobile, Qualcomm, Ericsson, Nokia, Qorvo, C Spire, US Cellular
WF on DC_(n)71B UE reference architecture related issues
R4-1803334

## Slide 2: Background
Intra-band EN-DC configurations have been proposed in Bands 71 and 41.
Prior RAN4 agreement:
  a single PA reference architecture was agreed for deriving requirements for DC_(n)71B. [1]
A number of issues associated with intra-band EN-DC due to single PA and dual PA reference architectures have been identified in WG4 Meeting # 86. [2][3][4][5]
[1] R4-1714344, WF on DC_71-n71
[2] R4-1802243, Measurements of power backoff requirements for DC_(n)71B with single PA, Qualcomm
[3] R4-1802241, Intra-band EN-DC MPR and related discussion, Qualcomm
[4] R4-1801957, Intra-band EN-DC reference architectures , Qualcomm
[5] R4-1803062, A-MPR for DC_41A_n41A, Apple

## Slide 3: Summary of issues
Issue 1 - large power backoff needed in order to meet emissions requirements
Issue 2 – conservative to worst MPR/A-MPR must apply.
Issue 3 – Tx power-mismatch restriction between LTE and NR.
Issue 4 – cannot have independent power control for LTE and NR because of issue 3.
Issue 5 – inability to support EN-DC dynamic power sharing because of issue 3.

## Slide 4: Way forward
In addition to agreed WF in [1], RAN4 adopt a 2nd reference architecture based on 2PA for DC_(n)71B.
RAN4 define two sets of requirements, the 1st set of requirements based on the 1PA reference architecture as in [1], and the 2nd set of requirements based on the 2PA reference architecture.
RAN4 complete both sets of requirements by RAN4 #87.