## Slide 1: WF on UE RF requirements for intra-band contiguous NR CA in FR1
NTT DOCOMO, INC.
Qualcomm
3GPP TSG-RAN WG4 Meeting #86
Athens, Greece, 26 Feb. – 2 Mar. 2018
R4-1803357

## Slide 2: Background
To specify intra contiguous NR CA in FR1, Tx and Rx requirement were proposed[1]
For the proposal, several concerns were raised
  Concern1: Need to clarify maximum output power definition, i.e. , to clarify whether output power is measured over each component carrier or all component carriers.
  Concern2: Lack feasibility of proposed BW of ACI/IBB/OBB which is 100MHz for all CA configuration

## Slide 3: Way forward: Concern 1
We clarify the proposal for MOP as below
    Proposal : As with the LTE CA, UE maximum output power for 2UL intra-band contiguous NR CA for NR bands in FR1 should be measured over all component carriers, which means aggregated power of all component carriers, and the aggregated output power should follow the same requirement as that of single carrier.
      Ex1) PC3 in intra-band contiguous CA is 20+20 dBm
      Ex2) PC2 in intra-band contiguous CA is 23+23 dBm

## Slide 4: Way forward: Concern 2
As discussed in online session[2],
  BWs of ACI/IBB are same as Aggregated CBW of CA
  Interference power of ACI is REFSENS + 45.5 dB for all CA configuration
CC1
CBW
CBW
[-56]
[-44]
ACI
CC2
IBB1
IBB2
CBW
CBW
REFSENS + 45.5
Note that power of IBB is set as tentative because power of ACI could be higher than that of IBB in current specification though ACI is closer to wanted signal. Therefore, power of IBB should be further discussed and changed if needed. (this issue already exists in single-carrier as well)
OBB for 2DL/1UL intra-band contiguous NR CA for NR bands in FR1 should be specified with out-of-band blocker of case 3 only and the frequency offset is 3CBW.

## Slide 5: Way forward
UE RF requirements for 2DL/1UL intra contiguous NR CA in FR1 should be captured in the draft CR RAN4 #86.
UE RF requirements for 2DL/2UL intra contiguous NR CA in FR1 should be targeted to be captured in Rel-15.
  Companies are encouraged to evaluate MPR values based on above agreement by next RAN4 meeting, since MPR values are needed to specify 2DL/2UL intra contiguous NR CA.
  Note that squire bracket values can be adopted at May and can be revised if the values need to be changed.

## Slide 6: Appendix
Agreements in [1] as below
  Proposal 2: Transmit OFF power for 2UL intra-band contiguous NR CA for NR bands in FR1 should follow the mean power of -50 dBm per CC.
  Proposal 3: Occupied bandwidth for 2UL intra-band contiguous NR CA for NR bands in FR1 should follow the same requirement of single-carrier.
  Proposal 4: Spectrum emission mask for 2UL intra-band contiguous NR CA for NR bands in FR1 should be specified with the requirement as shown in Figure 1.
  Proposal 5: Adjacent Channel Leakage power Ratio for 2UL intra-band contiguous NR CA for NR bands in FR1 should shall be higher than 31 dB for power class 2 and 30 dB for power class 3 if the measured adjacent channel power is greater than [–50] dBm.
  Proposal 6: Spurious emissions for 2UL intra-band contiguous NR CA for NR bands in FR1 should follow the same requirements as those of single-carrier.
  Proposal 7: Transmit intermodulation for 2UL intra-band contiguous NR CA for NR bands in FR1 should follow the intermodulation attenuation of -29 dBc and -35 dBc with an unwanted CW signal of -40 dBc.
  Proposal 8: Other Tx requirements should be further discussed and completed in the next meeting at the latest.

## Slide 7: References
[1] R4-182709, UE RF requirements for intra-band contiguous NR CA for FR1, NTT DOCOMO, INC.
[2]R4-1802267, 2DL/1UL intra-band contiguous NR CA ACS, IBB for NR bands in Sub 6, Qualcomm Incorporated.