## Slide 1: WF on UE RF requirements for intra-band contiguous NR CA in FR2
NTT DOCOMO, INC.
Intel Corporation
3GPP TSG-RAN WG4 Meeting #86
Athens, Greece, 26 Feb. – 2 Mar. 2018
R4-1803358

## Slide 2: Background
To specify intra contiguous NR CA in FR2, Tx requirement were proposed[1]
For the proposal, several comments were raised
  Comment 1: Need to clarify definition of below requirements, i.e. , to clarify whether each requirement targets power measured over each component carrier or all component carriers.
    Maximum output power
    Transmit OFF power
    Occupied bandwidth
  Comment 2: Note that companies need to evaluate MPR values for below requirements
    NR General spectrum emission mask
    Adjacent channel leakage ratio
    Spurious emissions

## Slide 3: Way forward: Comment 1
We clarify the proposal as below
  Maximum output power
    Proposal 1: As with the LTE CA, UE maximum output power for 2UL intra-band contiguous NR CA for NR bands in FR1 should be measured over all component carriers, which means aggregated power of all component carriers, and the aggregated output power should follow the same requirement as that of single carrier.
      Ex1) PC3 in intra-band contiguous CA is 20+20 dBm
      Ex2) PC2 in intra-band contiguous CA is 23+23 dBm
  Transmit OFF power
    Proposal 2: As with the LTE CA, Transmit OFF power for UL intra-band contiguous NR CA for NR bands in FR2 should follow the mean power of -35 dBm per CC, where transmit OFF power is defined as the mean power per component carrier when the transmitter is OFF on all component carriers.
  Occupied bandwidth
    Proposal 3: Occupied bandwidth for UL intra-band contiguous NR CA for NR bands in FR2 should follow the same requirement of single-carrier, where occupied bandwidth is defined as a measure of the bandwidth containing 99 % of the total integrated power of the transmitted spectrum.

## Slide 4: Way forward: Comment 2
Companies are encouraged to evaluate MPR values based on agreements until next RAN4 meeting, since MPR values are needed to specify 2DL/2UL intra contiguous NR CA.
Based on agreements, Tx requirements for 2DL/1UL intra contiguous NR CA in FR2 should be captured in the draft CR RAN4 #86.
Tx and Rx requirement for 2DL/2UL intra contiguous NR CA in FR2 should be captured by RAN4 #87 in May at the latest.

## Slide 5: Appendix
Proposals in [1] as below
  Proposal 1: UE maximum output power for UL intra-band contiguous NR CA for NR bands in FR2 should follow the same requirements as those of single-carrier.
  Proposal 2: Transmit OFF power for UL intra-band contiguous NR CA for NR bands in FR2 should follow the mean power of -35 dBm per CC.
  Proposal 3: Occupied bandwidth for UL intra-band contiguous NR CA for NR bands in FR2 should follow the same requirement of single-carrier.
  Proposal 4: Spectrum emission mask for UL intra-band contiguous NR CA for NR bands in FR2 should be specified with the requirement as shown in Figure 1.
  Proposal 5: Adjacent Channel Leakage power Ratio for UL intra-band contiguous NR CA for NR bands in FR2 should shall be higher than 17 dBc for n257 and n258 and 16dBc for n259.
  Proposal 6: Spurious emissions for UL intra-band contiguous NR CA for NR bands in FR2 should follow the same requirements as those of single-carrier.
  Proposal 7: Transmit intermodulation for 2UL intra-band contiguous NR CA for NR bands in FR2 doesn’t need to be specified.
  Proposal 8: Other Tx requirements should be further discussed and completed in the next meeting at the latest.

## Slide 6: References
[1] R4-182710, UE RF requirements for intra-band contiguous NR CA for FR2, NTT DOCOMO, INC.