## Slide 1: WF on output power requirements on FR2
Qualcomm, Samsung, Verizon, AT&T, T-Mobile USA, NXP, DISH, Orange, ZTE, US Cellular, C Spire, Ericsson, Telstra, KT, Nokia, Vodafone, Mavenir, Telecom Italia, Reliance Jio, IITH, IITM, CEWiT, Tejas Networks
R4-1803372
3GPP TSG-RAN WG4 Meeting #86
Athens, Greece, 26th Febuary – 2nd March
Agenda item: 7.

## Slide 2: Background
Contributions and proposals submitted to RAN4#86
  [1] R4-1801786, Peak EIRP for FR2 handheld UE type, Intel Corporation
  [2] R4-1801953, FR2 peak EIRP requirement, Qualcomm Incorporated
  [3] R4-1802032, Peak EIRP for power class in FR2, Samsung
  [4] R4-1802158, Follow-up on R4-1800944: Boresight and 40deg scan angle EIRP of an antenna module, NXP Semiconductors Netherlands
  [5] R4-1802827, On UE peak EIRP requirement for FR2 - impact on UL network performance, Qualcomm Incorporated
Proposals submitted
  Intel, Apple: 21.2 dBm @ 28 GHz; 19.4 @ 39 GHz
  Samsung: 22.4 dBm @ 28 GHz; 20.6 dBm @ 39 GHz
  NXP: 30 dBm @ 28 GHz
  Qualcomm: Compromise 23.2 dBm (from 25.2) @ 28 GHz; 21.5 dBm (from 23.7) @ 39 GHz

## Slide 3: Background – Spherical coverage
Agreed work plan:
  Initiate offline and email discussion (after RAN4#85) on the use cases and model assumptions for NW performance analysis
  RAN4 NR AH #4 (January ’18)
    Initial discussion of simulation results (Both EIRP CDF and Network) based on the harmonized assumptions in this way forward.
    Propose harmonized NW model assumptions and update based on preliminary analysis.
  RAN4 #86 (February ’18)
    Deadline to submit the EIRP CDF simulation results based on the harmonized assumptions. Target preliminary EIRP CDF spherical requirement, based on the simulation outcomes.
    Continue to improve the NW simulation accuracy reflecting initial EIRP CDF requirement (from AH #4)
    Initial discussion of measurement results for prototype devices
  RAN4 #86bis (April ’18)
    Continue to improve the NW simulation accuracy reflecting preliminary EIRP CDF requirement (#86)
    Continue to improve the prototype measurement effort and compare to preliminary EIRP CDF simulation
  RAN4 #87 (May ’18)
    Finalize the spherical coverage requirement for handheld UEs based on the contributions

## Slide 4: Background – Spherical coverage
Proposed spherical coverage CDFs for network simulation in RAN4#86
 | Apple/Intel (R4-1802220) | Qualcomm (R4-1802828) | Samsung (R4-1803245)
UL peak EIRP (dBm) | 21.2 | 23.2 | 22.4
Proposed spherical coverage (from peak) | -11.5dB@50%tile -17.7dB@20%tile | -7dB@50%tile -10dB@20%tile | -8.6dB@50%tile -15dB@20%tile
EIRP at 50%-tile (dBm) | 9.7 | 15.2 | 13.8

## Slide 5: Way Forward
For Rel-15
  For 28GHz
    Min peak EIRP is 23.2 dBm
    50%-tile requirement for EIRP CDF is 13.8dBm, 9.4 dB down from peak (above)
  For 39GHz
    Min peak EIRP is 21 dBm
    50%-tile requirement for EIRP CDF is FFS
For Rel-16
  Strive to specify 20%-tile requirement for EIRP CDF in Rel-16