## Slide 1: 3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26 Feb - 2 Mar 2018
Huawei, HiSilicon,Intel, Samsung, Qualcomm,…
Way forward on NR UE REFSENS IM and FRC
R4-1803445

## Slide 2: Background
During RAN4#86 Athens meeting, as per the simulation results from companies, the following agreements are reached:
  -1dB SNR value is feasible for both FR1 and FR2 UE REFSENS analysis
  One single -1dB SNR value is agreed to be used for all CBW/SCS combinations.
References:
  R4-1803341 “Alignment results for UE REFENSE SNR simulation” Ericsson
  R4-1801674 “Discussion on NR UE REFSENS SNR and simulation results”, Huawei, HiSilicon
  R4-1801755 “NR UE REFSENS SNR” Intel Incorporated
  R4-1802035 “Updated Simulation Results for NR REFSENS Target SNR” Samsung
  R4-1802116 “UE REFSENS simulation results for FR1 and FR2”, Nokia, Nokia Shanghai Bell
  R4-1802442 “Updated simulation results for target SNR of NR REFSENS” LGE
  R4-1803047 “Simulation results for UE REFSENS SNR levels” Ericsson

## Slide 3: Way Forward for IM
Clarification about SNR and IM&ILs in sensitivity equation
  FR1: (R4-1714452)
    Sensitivity = -174dBm(kT) + 10*log(RX BW) + NF – diversity gain + SNR + IM
      SNR = -1dB
      IM = 2.5dB including both baseband impairments and RF impairments
  FR2 (R4-1709140)
    Sensitivity = -174dBm(kT) + 10*log(Max. RX BW) + NF – Total Ant. gain - diversity gain + SNR + ILs
      SNR = -1dB
      ILs = TBD which should includes both baseband impairments and RF impairments

## Slide 4: Way Forward for FRC
Slot format
  FDD: slot format 0 (Full DL) and 1 (Full UL)
  TDD slot format pattern
    Option 1: {0, 0, 0, 11, 1}
    Option 2: {0, 0, 12, 1}
    Option 3: {0, 33, 0, 41}
    Other options not precluded
  Note: 0, 1, 11, 12, 33 and 41 stands for the corresponding slot format as defined in Table 4.3.2-3 of TS 38.211
For TDD the PDSCH is transmitted in slots with slot format 0 only
Same FRCs will be defined for both FDD and TDD
Define the FRCs for all CBW/SCS combinations for both FR1 and FR2 in next RAN4 meeting as per the agreed slot format