## Slide 1: WF on FR2 peak EIRP for handheld UE
Intel, Xiaomi, OPPO, vivo, MediaTek, [Huawei], LGE, Apple, Qorvo
R4-1803460
3GPP TSG-RAN WG4#86 Meeting
Athens, Greece, Feb 26 – Mar 2, 2018
Agenda: 7.4.9.3.2

## Slide 2: Background
No consensus on peak EIRP was found during AH-1801 meeting [1] and the proposals presented on RAN4 #86 received similar feedback
  Proposed values are either too high for UE vendors or too low for network providers
In RAN4 #86, two proposals were presented during offline discussion
  Proposal 1 [R4-1803372]
    @28GHz = 23.20 dBm
    @39GHz = 21.00 dBm
  Proposal 2
    @28GHz = start discussion with 21.52 dBm as compromise
    @39GHz = start discussion with 19.57 dBm as compromise
Parameters | Unit | Intel | LGE | MediaTek | Huawei | Samsung | Motorola | Qualcomm plastic | Qualcomm glass
Total Loss [28GHz] | dB | -9.60 | -10.00 | -7.45 | -8.70 | -9.60 | -6.10 | -3.30 | -4.30
Min peak EIRP [28GHz] | dBm | 20.20 | 21.50 | 21.05 | 22.30 | 22.40 | 21.70 | 26.24 | 25.24
Total Loss [39GHz] | dB | -10.90 | -11.45 | -8.55 | -8.80 | -10.20 | -6.70 | -5.00 | -6.30
Min peak EIRP [39GHz] | dBm | 18.40 | 19.05 | 20.45 | 19.70 | 20.60 | 18.60 | 24.74 | 23.44
Summary of reported min peak EIRP data

## Slide 3: Data Analysis
 | 28GHz | 39GHz
0 | 20.20 | 18.40
0.1 | 20.80 | 18.54
0.2 | 21.23 | 18.78
0.3 | 21.52 | 19.12
0.4 | 21.66 | 19.57
0.5 | 22.00 | 20.08
0.6 | 22.32 | 20.48
0.7 | 22.39 | 20.59
0.8 | 24.10 | 22.30
0.9 | 25.54 | 23.83
1 | 26.24 | 24.74
Chart: Distribution of min peak EIRP proposals
| 20.2 | 20.795000000000002 | 21.23 | 21.52 | 21.66 | 22 | 22.32 | 22.389999999999997 | 24.103999999999999 | 25.54 | 26.24
28 GHz | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
39 GHz | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
50th percentile @28GHz = 22.00 dBm
50th percentile @39GHz = 20.08 dBm

## Slide 4: Way Forward
Option 1: Use the 50th percentile value of reported data for min peak EIRP definition
  For 28GHz = 22.00 dBm
  For 39GHz = 20.08 dBm
Option 2: Narrow the previously approved range [2] by taking equal percentile on each side of the data distribution. The new ranges will be:
  For 28GHz = [21.52 – 22.39] dBm, 30% each side
  For 39GHz = [19.57 – 20.48] dBm, 40% each side
Option 3: Use the 50th percentile value of reported data for min peak EIRP definition and use the nominal peak EIRP value as given below:
  For 28GHz: Min = 22.00 dBm, Nominal value = 25dBm
  For 39GHz: Min = 20.08 dBm, Nominal value = 23dBm
  In Rel. 16, the minimum value will be increased with the average of measured min peak EIRP values provided by companies in Rel.15
Peak EIS levels will be specified using the same approach

## Slide 5
References
# | TDoc | Title | Source
[1] | R4-1801106 | WF peak EIRP requirement for mmW | Qualcomm
[2] | R4-1714445 | WF on pi/2 BPSK spectrum shaping and power class in FR2 | Intel Corporation, Apple, Qualcomm, IITH, LGE, Nokia, Huawei, Motorola Mobility