## Slide 1: 3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26 Feb - 2 Mar 2018
Huawei, HiSilicon,Intel, Samsung,…
Way forward on NR UE REFSENS SNR FR2 IM and FRC
R4-1813381

## Slide 2: Background(1/2)
During RAN4#86 Athens meeting, as per the simulation results from companies, the following agreements are reached:
  -1dB SNR value is feasible for both FR1 and FR2 UE REFSENS analysis
  One single -1dB SNR value is agreed to be used for all CBW/SCS combinations.
References:
  Revised R4-1803048 “Alignment results for UE REFENSE SNR simulation” Ericsson
  R4-1801674 “Discussion on NR UE REFSENS SNR and simulation results”, Huawei, HiSilicon
  R4-1801755 “NR UE REFSENS SNR” Intel Incorporated
  R4-1802035 “Updated Simulation Results for NR REFSENS Target SNR” Samsung
  R4-1802116 “UE REFSENS simulation results for FR1 and FR2”, Nokia, Nokia Shanghai Bell
  R4-1802442 “Updated simulation results for target SNR of NR REFSENS” LGE
  R4-1803047 “Simulation results for UE REFSENS SNR levels” Ericsson

## Slide 3: Background(2/2)
Sensitivity equation
  FR1:
    REFSENS = -174 + NF +10Log(CBW)+ 10log(Utilization)- diversity gain+ SNR + IM
  FR2
    Sensitivity = -174dBm(kT) + 10*log(Max. RX BW) + NF – Total Ant. gain - diversity gain + SNR + ILs
Impairments Modelling
  FR2 (R4-1711625)
    Remaining baseband impairments are added on top of SNR

## Slide 4: Way Forward for FR2 BB IM
FR2 BB IM value
  Option 1: 2.0 dB
  Option 2: 2.5 dB
  Other options not precluded

## Slide 5: Way Forward for FRC
Slot format
  FDD: slot format 0 (Full DL) and 1 (Full UL)
  TDD slot format pattern
    Option 1: {0, 0, 0, 11, 1}
    Option 2: {0, 0, 12, 1}
    Other options not precluded
  Note: 0: slot format 0; 1: slot format 1; 11: slot format 11; 12: slot format 12 as defined in Table 4.3.2-3 of TS 38.211
For TDD the PDSCH is transmitted in slots with slot format 0 only
Same FRCs will be defined for both FDD and TDD
Define the FRCs for all CBW/SCS combinations for both FR1 and FR2 in next RAN4 meeting as per the agreed slot format