## Slide 1: Way forward on Intra-frequency Cell Identification Requirements without Gap
Intel
3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26 Feb - 02 Mar 2018
R4-1801766

## Slide 2: Background
In RAN4-NR-AH1801 the following formulae were agreed to define Intra-frequency Cell Identification requirements without gap
In FR1:
TPSS/SSS_sync = max( 600, [5 or 6] x SMTC_period ) ms (1)
TSSB_time_index = max( [TBD], [2+X] x SMTC_period ) ms (2)
TSSB_measurement_period = max( 200, [5] x SMTC_period ) ms (3)
In FR2:
TPSS/SSS_sync = max( [X1], [Y1] x N1 x SMTC_period ) ms (4)
TSSB_time_index = max( [X2], [3+Y2] x N2 x SMTC_period ) ms (5)
TSSB_measurement_period = max( [X3], [Y3] x N3 x SMTC_period ) ms (6)
Interested companies are encouraged to propose [TBD] values in formulas (1) to (6), and the parameter N related to Rx beamforming and Rx beam sweeping in formulas (4) to (6)

## Slide 3: Way Forward
Based on Simulation results and discussion we propose the following
In FR1:
TPSS/SSS_sync = max( 600, 6x SMTC_period ) ms
TSSB_time_index = max( 120, 3x SMTC_period ) ms
TSSB_measurement_period = max( 200, 5x SMTC_period ) ms
In FR2:
TPSS/SSS_sync = max(600, 5x 8 x SMTC_period ) ms
TSSB_time_index = max(280, 7x 1x SMTC_period ) ms
TSSB_measurement_period = max( 200, 5 x 8 x SMTC_period ) ms