## Slide 1: WF on BS demodulation for sTTI and PT
Ericsson, Huawei, Nokia
3GPP TSG-RAN WG4 Meeting #86 Athens,Greece, 26 Feb – 2 Mar 2018
R4-1803102

## Slide 2: General Simulation Assumption
Parameter | Value
Number of Tx antennas | 1
Number of Rx antennas | 2, 4
Propagation condition | EPA5
Cyclic prefix | Normal
Reference receiver | MRC
Channel bandwidth | [5 MHz], 10 MHz, 15 MHz, 20 MHz
TTI length | Subslot TTI
Number of OFDM-symbols | Subslot TTI: 2 and 3
Fraction of maximum throughput | 70 %
Maximum number of HARQ transmissions | 4
DMRS configuration | IFDMA is not configured
Number of HARQ processes | 16
RV sequence | 0, 2, 3, 1, 0, 2, 3, 1
Modulation | 16QAM

## Slide 3: DMRS pattern for PUSCH
For subslot-based PUSCH
  Option 1:
    With DMRS sharing RDD DD DD RD DD RDD
  Option 2:
    With DMRS sharing: RDD DD|R RD DD|R RD RDD

## Slide 4: UCI on sPUSCH
Not define performance requirements for UCI on sPUSCH

## Slide 5: sPUCCH
For subslot-based
  Define performance requirements for format 1a
    1-bit HARQ-ACK w/o SR is assumed in the test setup
    Use Ack/Nack performance as the test metric
  Define performance requirements for format 4
    In the test setup it is assumed:
      [3 bits with 2 PRBs]
    Use ACK/NACK performance as the test metric
  Test method
    In the test, 2/3 OS are transmitted consecutively follow RAN1 spec