## Slide 1: WF on UE feature list for RRM and modulation order
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting #86 R4-1803278
Athens, Greece, 26 February – 2 March 2018
Agenda item: 7.1

## Slide 2: Capabilities for modulation order

## Slide 3: Background
Agreements
  64QAM for PDSCH is mandatory without capability at least for all FR2 bands defined within Rel.15 timeframe
  Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced
  64QAM for PUSCH is mandatory without capability at least for all bands defined within Rel.15 timeframe
  Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced
  256QAM for PDSCH for FR1 is mandatory with Type 4 capability signalling. It can be revisited in the future whether the 256QAM is mandated in all UE types or cateogories.
  If capability signalling is introduced for FR2 256QAM PDSCH and PUSCH (pending on the feasibility study), it shall be type 1 signalling. FFS on whether type 1 is sufficient considering the number of supporting MIMO layers.
  256QAM for PUSCH for FR1 is optional with type 1 capability signalling. RAN4 can further discuss to mandate 256QAM for PUSCH for FR1 in future release.
  pi/2-BPSK for PUSCH is optional
  Type 4 (per UE) with FR1/2 differentiation
  RAN4 will define the same minimum requirements for pulse-shaped pi/2 BPSK and non pulse-shaped pi/2 BPSK for FR2.
  pi/2-BPSK for PUCCH format 3/4 is optional
  Type is same as pi/2-BPSK for PUSCH, i.e. Type 4 (per UE) with FR1/2 differentiation

## Slide 4: Background
Current RAN4 feature list for modulation order part
Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
64QAM modulation for FR2 PDSCH | 1) 64QAM modulation for FR2 PDSCH |  | Yes | 64QAM for PUSCH is not possible |  | No need | Applicable only to FR2 |  | Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced | RAN4 | Mandatory without capability | 
64QAM for PUSCH | 1) 64QAM for PUSCH |  | Yes | 64QAM for PUSCH is not possible |  | No need | No need |  | Capability can be discussed in future, e.g. when low cost device (e.g. IoT) and/or higher frequency band in FR2 are introduced | RAN4 | Mandatory without capability | 
256QAM for PDSCH | 1) 256QAM for PDSCH |  | Yes | 256QAM for PDSCH is not possible | Type4 for FR1 [Type1] if needed for FR2 | No need | Yes |  | For FR1, it can be revisited in the future whether the 256QAM is mandated in all UE types or categories For FR2, FFS on whether type 1 is sufficient considering the number of supporting MIMO layers. | RAN4 | Mandatory with capability for FR1 TBD for FR2 | 
256QAM for PUSCH | 1) 256QAM for PUSCH |  | Yes | 256QAM for PUSCH is not possible | Type1 for FR1 [Type1] if needed for FR2 | No need | Yes |  | For FR1, RAN4 can further discuss to mandate 256QAM for PUSCH for FR1 in future release. For FR2, FFS on whether type 1 is sufficient considering the number of supporting MIMO layers. | RAN4 | Optional for FR1 TBD for FR2 | 
pi/2-BPSK for PUSCH | 1) pi/2-BPSK for PUSCH |  | Yes | pi/2-BPSK for PUSCH is not possible | Type 4 | No need | Yes |  | RAN4 will define the same minimum requirements for pulse-shaped pi/2 BPSK and non pulse-shaped pi/2 BPSK for FR2. | RAN4 | Optional | 
pi/2-BPSK for PUCCH format 3/4 | 1) pi/2-BPSK for PUCCH format 3/4 |  | Yes | pi/2-BPSK for PUCCH format 3/4 is not possible | Type 4 | No need | Yes |  |  | RAN4 | Optional | 

## Slide 5: Type of 256QAM for FR1 PDSCH
Open issue
  RAN2 already agreed that the modulation order is included in BPC (in RAN2 #99bis) , i.e., type of modulation order is type 2 or type 3
  Tentative agreement in RAN1 feature list is [type 3] but final decision is up to RAN4
Discussion
  Proposal 1: Type of capability signaling
    Option 1: Keep agreement (type 4 with FR1/FR2 differentiation), i.e. modulation order is not in BPC
      Option 1-1: Instead, introduce data scaling factor into BPC (type 3)
      Option 1-2: No such scaling
    Option 2: Revise to Type 3 (per CC in BPC)
  Proposal 2: Following feature description (only FR1)
Feature group | Components | Prerequisite feature groups | Need for gNB to know…. | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
256QAM for PDSCH | 1) 256QAM for PDSCH |  | Yes | 256QAM for PDSCH is not possible | Type 4 Type 3 (per CC) | No need | Yes No need |  | For FR1, it can be revisited in the future whether the 256QAM is mandated in all UE types or categories | RAN4 | Mandatory with capability for FR1 | 
Option 1-1: Data scaling factor for 256QAM | 1) Data scaling factor for 256QAM |  | YES | Data scaling is not possible | Type 3 (per CC) | No need | No need |  |  | RAN4 | Mandatory with capability for FR1 | 

## Slide 6: Type of 256QAM for FR1 PUSCH
Open issue
  RAN2 already agreed that the modulation order is included in BPC (in RAN2 #99bis) , i.e., type of modulation order is type 2 or type 3
  Tentative agreement in RAN1 feature list is [type 3] but final decision is up to RAN4
Discussion
  Proposal 1: Type of capability signaling
    Option 1: Keep agreement (type 1), i.e. modulation order is not in BPC
    Option 2: Revise to Type 3 (per CC in BPC)
  Proposal 2: Following feature description (only FR1)
Feature group | Components | Prerequisite feature groups | Need for gNB to know…. | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
256QAM for PUSCH | 1) 256QAM for PUSCH |  | Yes | 256QAM for PUSCH is not possible | Type 1 Type 3 (per CC) | No need | Yes No need |  | For FR1, RAN4 can further discuss to mandate 256QAM for PUSCH for FR1 in future release. | RAN4 | Optional for FR1 | 

## Slide 7: Type of pi/2-BPSK for PUSCH
Open issue
  RAN2 already agreed that the modulation order is included in BPC (in RAN2 #99bis) , i.e., type of modulation order is type 2 or type 3
  Tentative agreement in RAN1 feature list is [type 3] but final decision is up to RAN4
Discussion
  Proposal 1: Type of capability signaling
    Option 1: Keep agreement (type 4 with FR1/FR2 differentiation), i.e. modulation order is not in BPC
    Option 2: Revise to Type 3 (per CC in BPC)
  Proposal 2: Following feature description
Feature group | Components | Prerequisite feature groups | Need for gNB to know…. | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
pi/2-BPSK for PUCCH format 3/4 | 1) pi/2-BPSK for PUCCH format 3/4 |  | Yes | pi/2-BPSK for PUCCH format 3/4 is not possible | Type 4 Type 3 (per CC) | No need | Yes No need |  |  | RAN4 | Optional | 

## Slide 8: Type of pi/2-BPSK for PUCCH format 3/4
Open issue
  RAN2 already agreed that the modulation order is included in BPC (in RAN2 #99bis) , i.e., type of modulation order is type 2 or type 3
  Tentative agreement in RAN1 feature list is [type 3] but final decision is up to RAN4
Discussion
  Proposal 1: Type of capability signaling
    Option 1: Keep agreement (type 4 with FR1/FR2 differentiation), i.e. modulation order is not in BPC
    Option 2: Revise to Type 3 (per CC in BPC)
  Proposal 2: Following feature description
Feature group | Components | Prerequisite feature groups | Need for gNB to know…. | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
pi/2-BPSK for PUCCH format 3/4 | 1) pi/2-BPSK for PUCCH format 3/4 |  | Yes | pi/2-BPSK for PUCCH format 3/4 is not possible | Type 4 Type 3 (per CC) Type 3 (per CA BW class) | No need | Yes |  | Signaled value is common within all FR1 (or FR2) bands | RAN4 | Optional | 

## Slide 9: 256QAM for FR2 PDSCH
Agreement
  If capability signaling is introduced for FR2 256QAM PDSCH and PUSCH (pending on the feasibility study), it shall be type 1 signalling. FFS on whether type 1 is sufficient considering the number of supporting MIMO layers.
Discussion
  Introduce 256QAM for FR2 PDSCH in Rel.15?
    Option 1: Do not define 256QAM requirements and capability signaling for 256QAM for FR2 in Rel-15 in RAN4 specification. We can further discuss to introduce 256QAM in future release in release independent manner.
      Ericsson, Samsung, QC, Intel, ZTE, LG, MTK
    Option 2: Define the 256QAM for FR2 as optional features in Rel-15. RAN4 will further discuss the requirements including EVM, power back-off and so on.
      CMCC, NTT DoCoMo, AT&T, Huawei, Nokia, Verizon
  If introduced, what is type?
    Option 1. Type 1 (per band), i.e. not included in BPC
    Option 2. Type 3 (per CC)
  Feature description (only FR2 part)
Feature group | Components | Prerequisite feature groups | Need for gNB to know…. | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
256QAM for PDSCH | 1) 256QAM for PDSCH |  | Yes | 256QAM for PDSCH is not possible | Type1 Type 3 (per CC) Type 3 (per CA BW class) | No need | Applicable only to FR1 Yes |  |  | RAN4 | NA Optional | 

## Slide 10: Other capabilities

## Slide 11: BWP switching delay
Agreement
  Introduce the type 4 capability signaling to differential the type 1 and type 2 for each scenario if the capability signaling is agreed to be introduced. We may remove the capability signaling if RAN4 can agree single minimum delay for each scenario.
Discussion
    Proposal1: Following feature description
Frequency Range | Scenario | Delay (us)(Note) | Comment
1 | 1 | Type 1: 600us Type 2: 2ms | 
 | 2 | Type 1: 600us Type 2: 2ms | 
 | 3 | Type 1: 600us Type 2: 2ms | 
 | 4 | Type 1: 350us Type 2: 950us | No delay required from the RF perspective
2 | 1 | Type 1: 600us Type 2: FFSms | 
 | 2 | Type 1: 600us Type 2: FFSms | 
 | 3 | Type 1: 600us Type 2: FFSms | 
 | 4 | Type 1: 350us Type 2: FFSus | No delay required from the RF perspective
  Note: Network cannot configure the shorter delay for certain UE type
Feature group | Components | Prerequisite feature groups | Need for gNB to know… | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
BWP switching delay | 1) BWP switching delay specified in TS38.101-1 for FR1 and TS38.101-2 for FR2, candidate values set: {type1, type2} |  | Yes | UE does not support BWP switching delay | Type 4 | No need | No need |  | Network cannot configure the shorter delay for certain UE type RAN4 may remove the capability signaling if RAN4 can agree single minimum delay for each scenario. | RAN4 | Mandatory with capability | 

## Slide 12: 1-symbol GP in unpaired spectrum
Agreement
  Capability signaling type for 1-symbol GP for 120KHz SCS in unpaired spectrum will be type 4 for FR2. RAN4 will further discuss whether it is feasible to support this feature or not in Rel-15.
  Capability signaling type for 1-symbol GP for 60KHz SCS in unpaired spectrum will be type 4 for FR1. RAN4 will further discuss whether it is feasible to support this feature or not in Rel-15.
Discussion
  Proposal 1:Keep type 4 capability. RAN4 may remove the capability signaling if RAN4 concluded that 1-symbol GP in unpaired spectrum is not feasible
  Proposal 2: Following feature description
Feature group | Components | Prerequisite feature groups | Need for gNB to know… | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
1-symbol GP in unpaired spectrum | 1) Slot formats with 1-symbol GP(s) for 120KHz SCS in unpaired spectrum in FR2 2) Slot formats with 1-symbol GP(s) for 60KHz SCS in unpaired spectrum in FR1 |  | Yes | UE does not support 1 symbol GP in unpaired spectrum | Type 4 | Applicable only to TDD | Yes |  | RAN4 may remove the capability signaling if RAN4 concluded that 1-symbol GP in unpaired spectrum is not feasible | RAN4 | Optional | 

## Slide 13: Number of Tx ports
Agreement
  No capability signalling for number of Rx/Tx ports. We can revisit the need of capability signalling of number of Tx ports when we discuss the number of MIMO layers in this week.
Discussion
  Proposal 1: MIMO capability is enough and remove this capability from RAN4 feature list
Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
Number of UE TX ports |  |  |  |  |  |  |  |  | No capability signalling for number of Rx/Tx ports. We can revisit the need of capability signalling of number of Tx ports when we discuss the number of MIMO layers in this week. | RAN4 |  | 

## Slide 14: Capabilities for RRM

## Slide 15: Background
Agreements
  Renamed to “Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement with SSB within the active BWP”
    FFS: inter-band CA case
  Type 4 (per UE) and applicable only to FR1
Current RAN4 feature list for RRM part
Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
Independent measurement gap configurations for FR1 and FR2 | 1) measurement gaps for FR1 and FR2 are configured independently |  | Yes | UE does not support independent gap configuration between FR1 and FR2 | Type 4 | No Need | No Need |  |  | RAN4 | Optional | 
Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement | 1) Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement |  | Yes | UE does not support simultaneous reception of data and SS block with different numerologies | Type 4 | No Need | Applicable only to FR1 |  | FFS: inter-band CA case | RAN4 | Optional | 

## Slide 16: Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement
Open issue
  If inter-band CA (e.g. band A + band B) is configured, whether data reception on one band (e.g. band A) is possible or not, when UE conduct serving cell or intra-frequency measurement in another band (e.g. band B) with different numerologies between those bands
Discussion
  Proposal 1: For inter-band CA (FR1+FR1)
    No additional capability, and same capability between this case and intra-band CA
  Proposal 2: For inter-band CA (FR1+FR2)
    No additional capability, and UE is expected to simultaneously receive data and SSB when UE conducts serving cell or intra-frequency measurement in either band regardless of the numerologies of FR1 and FR2 bands
  Proposal 3: For inter-band CA (FR2+FR2)
    Option 1: Introduce capability signaling to indicate whether UE share Rx beam between the bands. If UE share the Rx beam, UE is not expected to simultaneously receive data and SSB in the bands
    Option 2: No additional capability, and RAN4 will further discuss how to handle this case
data
Band A
Band B
f
SSB
Diff. numerology

## Slide 17: Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement
Discussion
  Proposal 4: Following feature description
Feature group | Components | Prerequisite feature groups | Need for gNB to know whether the feature is supported by the UE (what happens if gNB does not know?) | Consequences if the feature is not supported by the UE | Type (See R4-17121 19) | Need of FDD/TDD differentiation | Need of FR1/FR2 differentiation | RAN5 implication | Remarks | Responsible WG | Recommendation for TSG-RAN | TSG-RAN decision
Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement | 1) Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement |  | Yes | UE does not support simultaneous reception of data and SS block with different numerologies | Type 4 | No Need | Applicable only to FR1 No need |  | For inter-band CA (FR1+FR1), No additional capability, and same capability between this case and intra-band CA For inter-band CA (FR1 + FR2), UE is expected to simultaneously receive data and SSB when UE conducts serving cell or intra-frequency measurement in either band regardless of the numerologies of FR1 and FR2 bands For inter-band CA (FR2+FR2), No additional capability, and RAN4 will further discuss how to handle this case | RAN4 | Optional |