## Slide 1: 3GPP TSG-RAN WG4 RAN4-86 Athens, Greece, 26 February - 2 March, 2018
ZTE, [Huawei, Ericsson]
WF on Narrow Band Response
R4-1803312

## Slide 2: Background
According to ETSI EN 301 489 – 1 [1], and previous RAN4 spec TS 37.113[2], response of the BS in immunity test can be identified as narrow band response or wide band EMC phenomena. And narrow band responses are disregarded.
Frequency offset foffset is used to identify a narrow band response.
foffset is discussed in [4] [3].
Notes: ΔfOOB

## Slide 3: WF Agreement
Keep the definition of narrow band response.
Define the foffset for narrow band reponse.
Alternatives on how to define foffset is shown as below:
  Option 1: foffet equals to twice the nominal 6 dB bandwidth of the IF filter immediately preceding the demodulator of the receiver.
  Option 2: foffet equals to twice the bandwidth over which the equipment is intended to operate, as declared by the manufacturer, which is BWchannel defined in TS 38.104[3][4].
  Option 3: Other alternatives are not precluded.

## Slide 4: References
[1] ETSI EN 301 489 – 1. ElectroMagnetic Compatibility (EMC) standard for radio equipment and services; Part 1: Common technical requirements; Harmonised Standard covering the essential requirements of article 3.1(b) of Directive 2014/53/EU and the essential requirements of article 6 of Directive 2014/30/EU.
[2] TS 37.113
[3] TS 38.104
[4] R4-1801523 Discussion on narrow band responses of NR BS during radiated immunity test, ZTE