## Slide 1: WF on FR2 peak EIRP for handheld UE
Intel, Xiaomi, OPPO, vivo, MediaTek, [Huawei], LGE, Apple, Qorvo
R4-1803451
3GPP TSG-RAN WG4#86 Meeting
Athens, Greece, Feb 26 – Mar 2, 2018
Agenda: 7.4.9.3.2

## Slide 2: Background
No consensus on peak EIRP was found during AH-1801 meeting [1] and the proposals presented on RAN4 #86 received similar feedback
  Proposed values are either too high for UE vendors or too low for network providers
In RAN4 #86, two proposals were presented during offline discussion
  Proposal 1 [R4-1803372]
    @28GHz = 23.20 dBm
    @39GHz = 21.00 dBm
  Proposal 2
    @28GHz = start discussion with 21.52 dBm as compromise
    @39GHz = start discussion with 19.57 dBm as compromise
Parameters | Unit | Intel | LGE | MediaTek | Huawei | Samsung | Motorola | Qualcomm plastic | Qualcomm glass
Total Loss [28GHz] | dB | -9.60 | -10.00 | -7.45 | -8.70 | -9.60 | -6.10 | -3.30 | -4.30
Min peak EIRP [28GHz] | dBm | 20.20 | 21.50 | 21.05 | 22.30 | 22.40 | 21.70 | 26.24 | 25.24
Total Loss [39GHz] | dB | -10.90 | -11.45 | -8.55 | -8.80 | -10.20 | -6.70 | -5.00 | -6.30
Min peak EIRP [39GHz] | dBm | 18.40 | 19.05 | 20.45 | 19.70 | 20.60 | 18.60 | 24.74 | 23.44
Summary of reported min peak EIRP data

## Slide 3: Data Analysis
 | 28GHz | 39GHz
0 | 20.20 | 18.40
0.1 | 20.80 | 18.54
0.2 | 21.23 | 18.78
0.3 | 21.52 | 19.12
0.4 | 21.66 | 19.57
0.5 | 22.00 | 20.08
0.6 | 22.32 | 20.48
0.7 | 22.39 | 20.59
0.8 | 24.10 | 22.30
0.9 | 25.54 | 23.83
1 | 26.24 | 24.74
Chart: Distribution of min peak EIRP proposals
| 20.2 | 20.795000000000002 | 21.23 | 21.52 | 21.66 | 22 | 22.32 | 22.389999999999997 | 24.103999999999999 | 25.54 | 26.24
28 GHz | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
39 GHz | 0 | 0.1 | 0.2 | 0.3 | 0.4 | 0.5 | 0.6 | 0.7 | 0.8 | 0.9 | 1
50th percentile @28GHz = 22.00 dBm
50th percentile @39GHz = 20.08 dBm

## Slide 4: Way Forward
Option 1: Use the 50th percentile value of reported data for min peak EIRP definition
  For 28GHz = 22.0 dBm
  For 39GHz = 20.0 dBm
Option 2: Narrow the previously approved range [2] by taking equal percentile on each side of the data distribution. The new ranges will be:
  For 28GHz = [21.52 – 22.39] dBm, 30% each side
  For 39GHz = [19.57 – 20.48] dBm, 40% each side
Peak EIS levels will be specified using the same approach

## Slide 5
References
# | TDoc | Title | Source
[1] | R4-1801106 | WF peak EIRP requirement for mmW | Qualcomm
[2] | R4-1714445 | WF on pi/2 BPSK spectrum shaping and power class in FR2 | Intel Corporation, Apple, Qualcomm, IITH, LGE, Nokia, Huawei, Motorola Mobility