## Slide 1: Way forward on higher velocity UE RRM requirements
Huawei, HiSilicon, Ericsson, …
3GPP TSG-RAN WG4 Meeting #86 Athens, Greece, 26th February – 2nd March, 2018
Agenda item: 6.19.4.1
R4-1803479

## Slide 2: Background
We have reached the following agreements in RAN4 #85:
  For non-DRX requirements with gap pattern #0 and for intra-frequency measurement
    Reuse Rel-13 cell identification and measurement delay requirements in high Doppler channel up to 220Hz Doppler spread.
    Reuse Rel-13/14 measurement accuracy requirements in high Doppler channel up to 220Hz Doppler spread.
  FFS for inter-frequency measurement requirements
  FFS for RRM requirements with DRX

## Slide 3: Way forward
DRX measurement requirements
  Under RRC_IDLE state
    TIdentify_Intra_UE cat M1 and Tmeasure_intra_UE cat M1 should be reduced due to faster UE velocity
DRX cycle length (s) | Tdetect_intra (s) (DRX cycles) | Tmeasure_intra (s) (DRX cycles) | Tevaluate_intra (s) (DRX cycles)
0.32 | [TBD] | [TBD] | [TBD]
0.64 | [TBD] | [TBD] | [TBD]
1.28 | [TBD] | [TBD] | [TBD]
2.56 | [TBD] | [TBD] | [TBD]

## Slide 4: Way forward
  Under RRC_CONNECTED state
    TIdentify_Intra_UE cat M1 and Tmeasure_intra_UE cat M1 should be reduced due to faster UE velocity
    Gap sharing should be considered when consider values in the above table
DRX cycle length (s) | Tidentify_intra (s) (DRX cycles) | Tmeasure_intra (s) (DRX cycles)
≤0.04 | [0.8] (Note1) | [0.2] (Note1)
[0.04<DRX-cycle≤TBD] | Note2([TBD]) | Note2 ([TBD])
[TBD<DRX-cycle≤TBD] | Note2([TBD]) | Note2 ([TBD])
[TBD<DRX-cycle≤2.56] | Note2([TBD]) | Note2 ([TBD])
Note1: Number of DRX cycle depends upon the DRX cycle in use. Note2: Time depends upon the DRX cycle in use. |  | 

## Slide 5: Way forward
  On gap sharing and high-velocity operation
    Introduce a new measurement gap sharing table for eFeMTC UEs operating under higher velocity, and the values of the table are FFS.
    Inter-frequency requirements under high-velocity operation is FFS.
    If high-velocity indication is received by the efeMTC UE, the UE shall sue the measurement gap sharing table associated with high-velocity.